## Slide 1: CE4-related: Hybrid Merge Estimation Region
H. Wang, V. Seregin, W.-J. Chien, T. Hsieh, Y. Han, M. Karczewicz

## Slide 2: Introduction
Merge estimation region
Neighbor MVs are not used as candidates in the area

## Slide 3: Area determination
Area size N is used do define the processing area.
Log2(N) is signaled PPS
Area is aligned with block partitioning splits
At each split, the partition area size is checked against the size N
64x64 block

## Slide 4: QT/TT partition with size 2N
If just check partition size against the area size, it can be a case when processing areas are smaller than the desired area size.
Group smaller partition blocks

## Slide 5: Picture boundary handling
  The processing area is not clipped if it goes outside picture
    Regular neighbor availability checking process is used

## Slide 6: Shared and merge estimation areas
Merge share list and MER are supported together
  Within any MER area, all generation of merge candidate list can be performed in parallel
  All blocks with an shared list area uses the same merge candidate list.

## Slide 7: Experimental Results
Reference software: VTM-3.0.
Test results of all the 3 proposed modifications:
Share list results
 | RA |  |  | LB |  | 
 | Y | U | V | Y | U | V
N=32 | 0.00% | 0.04% | 0.02% | 0.01% | 0.08% | 0.12%
N=64 | 0.05% | 0.04% | 0.03% | 0.08% | -0.06% | -0.06%
N=128 | 0.17% | 0.26% | 0.27% | 0.25% | 0.10% | 0.42%
N=256 | 0.46% | 0.60% | 0.68% | 0.67% | 0.72% | 0.78%

## Slide 8: Experimental Results
Reference software: VTM-3.0.
Test results of all the 3 proposed modifications:
Merge Estimation Region results
 | RA |  |  | LB |  | 
 | Y | U | V | Y | U | V
N=32 | 0.00% | 0.00% | 0.01% | 0.00% | 0.00% | -0.02%
N=64 | 0.02% | 0.02% | 0.06% | 0.01% | 0.10% | 0.11%
N=128 | 0.10% | 0.18% | 0.20% | 0.08% | 0.02% | 0.21%
N=256 | 0.30% | 0.43% | 0.42% | 0.33% | 0.31% | 0.53%

## Slide 9: Experimental Results
Reference software: VTM-3.0.
Test results of all the 3 proposed modifications:
Shared and merge estimation areas both enabled ( MER size + Share list are Size)
 | RA |  |  | LB |  | 
 | Y | U | V | Y | U | V
64 + 32 | 0.02% | 0.02% | 0.06% | 0.04% | -0.09% | -0.09%
128 + 32 | 0.10% | 0.14% | 0.16% | 0.05% | 0.11% | 0.10%
128 + 64 | 0.11% | 0.14% | 0.16% | 0.12% | 0.03% | 0.25%
256 +32 | 0.30% | 0.43% | 0.48% | 0.31% | 0.26% | 0.47%
256 + 64 | 0.30% | 0.42% | 0.48% | 0.33% | 0.25% | 0.40%
256 + 126 | 0.33% | 0.44% | 0.50% | 0.43% | 0.41% | 0.36%

## Slide 10: Experimental Results
Reference software: VTM-3.0.
Test results of all the 3 proposed modifications:
Proposed share list compared with supplementary results D.1~4 of CE4.3.1
 |  | RA |  |  | LB |  | 
 |  | Y | U | V | Y | U | V
N=32 | Proposed | 0.00% | 0.04% | 0.02% | 0.01% | 0.08% | 0.12%
 | CE4.3.1 D.1 | 0.00% | 0.06% | 0.03% | 0.04% | 0.10% | 0.18%
N=64 | Proposed | 0.05% | 0.04% | 0.03% | 0.08% | -0.06% | -0.06%
 | CE4.3.1 D.2 | 0.07% | 0.11% | 0.08% | 0.13% | 0.20% | 0.07%
N=128 | Proposed | 0.17% | 0.26% | 0.27% | 0.25% | 0.10% | 0.42%
 | CE4.3.1 D.3 | 0.23% | 0.34% | 0.40% | 0.33% | 0.44% | 0.50%
N=256 | Proposed | 0.46% | 0.60% | 0.68% | 0.67% | 0.72% | 0.78%
 | CE4.3.1 D.4 | 0.54% | 0.70% | 0.77% | 0.77% | 0.67% | 0.96%

## Slide 11: Boundary handling
In JVET-M170, bottom right check for shared list is performed for all partition nodes with area equal to 32.
  Area, for which merge list is derived, is clipped to be inside the picture.
In JVET-M0507, bottom right check for shared merge list area is removed.
  In the software, availability check for center TMVP is added, specification already has it.
  Merge list derivation for blocks smaller than 32 is not happening.

## Slide 12: Specification change
if (isInShareRegion == 0 && (cbWidth*cbHeight/4) < 32 && (x0 + cbWidth) <= pic_width_in_luma_samples && (y0 + cbHeight) <= pic_height_in_luma_samples && treeType != DUAL_TREE_CHROMA) {
isInShareRegion = 1
if((((MttSplitMode[ x0 ][ y0 ][ mttDepth ] == SPLIT_BT_VER ¦¦ MttSplitMode[ x0 ][ y0 ][ mttDepth ] == SPLIT_BT_HOR) && (cbWidth*cbHeight /2) < 32 ) ¦¦ ((MttSplitMode[ x0 ][ y0 ][ mttDepth ] == SPLIT_TT_VER ¦¦ MttSplitMode[ x0 ][ y0 ][ mttDepth ] == SPLIT_TT_HOR) && (cbWidth*cbHeight /4) < 32) )&& isInShareRegion == 0 && ( x0 + cbWidth) <= pic_width_in_luma_samples && ( y0 + cbHeight ) <= pic_height_in_luma_samples && treeType != DUAL_TREE_CHROMA){
isInShareRegion= 1