## Slide 1: JVET-M0814 Non-CE3: block size restriction on PDPC
LGE

## Slide 2: Summary
Problem statement
Considering throughput, apply PDPC to small blocks are not desirable. Furthermore, disabling PDPC could reduce computational complexity in large
Proposed method
Test 1: small block restriction
not apply PDPC to the luma and chroma blocks which have less or equal to 16 pixels (W*H<=16)
Test 2: small block and large block restriction
On top of test1, the maximum luma and chroma block size for PDPC is restricted as 32x32 and 16x16, respectively. (max(W, H)<=32 for luma, max(W,H)<=16 for chroma)

## Slide 3: Experiment results
Experiment results of test 1 and 2
- In test 2, decoder is decreased by 2%
 | Random access Main10 |  |  |  | 
 | Over VTM 3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.02% | 0.11% | 99% | 100%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 0.03% | 0.08% | -0.16% | 103% | 101%
Class C | 0.04% | -0.30% | -0.03% | 100% | 99%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.08% | -0.58% | -0.07% | 100% | 100%
Class F | -0.17% | -0.26% | -0.18% | 101% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM 3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | -0.04% | 0.04% | 100% | 99%
Class A2 | 0.04% | 0.11% | 0.08% | 100% | 100%
Class B | 0.03% | 0.04% | -0.15% | 100% | 101%
Class C | 0.07% | -0.40% | -0.11% | 100% | 102%
Class E |  |  |  |  | 
Overall | 0.05% | -0.08% | -0.05% | 100% | 101%
Class D | 0.06% | -0.49% | -0.15% | 101% | 103%
Class F | -0.20% | -0.23% | -0.14% | 100% | 101%
 | All Intra Main10 |  |  |  | 
 | Over VTM 3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.03% | 0.05% | 100% | 102%
Class A2 | 0.04% | 0.06% | 0.00% | 98% | 99%
Class B | 0.05% | 0.04% | 0.00% | 100% | 100%
Class C | 0.06% | -0.10% | -0.01% | 100% | 100%
Class E | 0.12% | 0.10% | 0.11% | 100% | 101%
Overall | 0.05% | 0.01% | 0.03% | 100% | 100%
Class D | 0.10% | -0.06% | -0.04% | 100% | 99%
Class F | -0.14% | -0.19% | -0.09% | 99% | 99%
 | All Intra Main10 |  |  |  | 
 | Over VTM 3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.10% | -0.16% | 100% | 98%
Class A2 | 0.07% | -0.11% | -0.10% | 100% | 99%
Class B | 0.06% | -0.06% | -0.13% | 101% | 98%
Class C | 0.06% | -0.05% | -0.05% | 101% | 99%
Class E | 0.13% | -0.12% | 0.09% | 101% | 97%
Overall | 0.06% | -0.08% | -0.08% | 101% | 98%
Class D | 0.10% | -0.09% | -0.01% | 103% | 99%
Class F | -0.14% | -0.24% | -0.24% | 101% | 98%