## Slide 1: AHG14: Reviced software for ultra low-latency encoding
K.Kazui (Fujitsu)
JVET-N0080

## Slide 2: Summary
Proposal of CTC on ultra low-latency encoding
Revised software (1st was in JVET-M0197)
  Delay model
  Encoding scheme
  Software implementation
Test conditions
Parallel processing

## Slide 3: Delay model
Target delay: ≈50ms for remote control applications
  Note: 150ms is enough for communication applications
End-to-end delay model for 1st DU of CVS
  Capturing TC: = 33ms (30Hz sequence)
  Encoding TE: proportional to DU size (in #CU), ≦ 33ms
  Transmission TX: proportional to DU size (in #bits)
  Buffering TX: = CPB size
  Decoding TD: = TE
  Outputting TO: = 33ms − TD

## Slide 4: IDR vs. progressive refresh
“Progressive refresh + DU” achieves the target delay
  “IDR + DU”: 142ms (1080p30, 1 DU = 1 CTU row, BIDR = 4*BTRAIL)
  “Progressive refresh + DU”: 73ms
Assumption: Same DU size in #CTU and bits

## Slide 5: Layout of intra CU and DU
Requirements
  Uniform bit allocation to minimize the CPB size
  Uniform intra-CU allocation to maximize visual quality
Typical layouts of intra-coded region and DU
  Vertical striped → Implemented (L to R)
  Horizontal striped
  Isolated

## Slide 6: Layouts of intra-coded region & DU
Vertical stripe

## Slide 7: Layouts of intra-coded region & DU
Horizontal stripe

## Slide 8: Layouts of intra-coded region & DU
Isolated

## Slide 9: Software implementation
VTM-4.0
1 DU per 1 CTU row
  Use of slice (provisionally)
    LFCrossSliceBoundaryFlag = 1
Encoder-only control
  Redundant intra coding at right size of refresh boundary
  Restricted intra prediction mode
  Restricted MV

## Slide 10: Redundant intra coding
Avoiding contamination in in-loop filtering
Worst case: rightmost 11 samples
Width of redundant intra CU is 8 or 16

## Slide 11: Restricted intra prediction mode
Avoiding contamination in intra prediction
  Only a mode which only refers to clean samples is chosen.

## Slide 12: Restricted MV
Avoiding contamination in motion compensation
  Any MV points to dirty area is not chosen in ME process.
  DMVR is disabled
Avoiding contamination in TVMP
  TVMP is disabled at random-access picture

## Slide 13: Cycle of random-access picture
Two schemes are tested.
  Input: target refresh cycle C1, picture width WPIC, frame rate F, unit of intra stripe U
  Output: refresh cycle C2, width of intra stripe w1
Scheme 1: simple but different from intended cycle
  w1 = U * ceil ( (WPIC + ( C1 * F / 2) ) / (C1 * F / U )
  C2 = ceil ( WPIC / w1 )
  Example: 1080p60, C1=1.0sec, U=8 → w1 = 32, C2 = 60
Scheme 2: C2 = C1
  w1 = ceil(WPIC / C1 / U ) * U
  First t1 frames have W1, remaining t2 frames have (W1 − U)
    t1 * w1 + t2 * (W1 − U) = WPIC, t1 + t2 = C1

## Slide 14: First access unit in bitstream
An IDR picture
  Same tile structure as for trailing pictures
No size control to IDR picture
  Larger bit consumption than trailing pictures
Suggestion for CTC
  Not to use the encoding result of first IDR picture and first cycle

## Slide 15: Suggested test conditions
Test sequence
  Same sequences as for LDB condition
Refresh cycle = 1.0 sec
  In scheme 2, the same as for random access condition
    Example: 64 frames for 60Hz sequence
Number of DU
  Equal to number of CTU rows
    Example: 9 DUs for 1080p sequence

## Slide 16: Simulation results
Anchor: LBD with periodical IRAP
 | Sequence | C1 | Scheme 1 |  |  |  | Scheme 2 |  | 
 |  |  | C2 | Y | Cb | Cr | Y | Cb | Cr
B | MarketPlace | 64 | 60 | 79.18% | 79.18% | 79.18% |  |  | 
 | RitualDance | 64 | 60 | 22.10% | 30.62% | 33.13% | 22.27% | 30.70% | 33.61%
 | Cactus | 48 | 60 | 28.92% | 62.51% | 81.06% | 31.33% | 64.69% | 83.58%
 | BasketballDrive | 48 | 60 | 11.68% | 37.58% | 32.46% | 12.42% | 38.67% | 33.29%
 | BQTerrace | 64 | 60 | 31.88% | 180.20% | 264.66% | 31.44% | 177.90% | 259.12%
C | BasketballDrill | 48 | 52 | 43.21% | 48.53% | 44.90% | 49.79% | 54.62% | 51.27%
 | BQMall | 64 | 52 | 32.21% | 60.20% | 57.57% | 31.48% | 59.77% | 56.49%
 | PartyScene | 48 | 52 | 47.58% | 83.28% | 90.07% | 60.10% | 95.12% | 102.17%
 | RaceHorses | 32 | 26 | 14.04% | 41.72% | 37.35% | 14.50% | 41.70% | 37.28%
D | BasketballPass | 64 | 26 | 23.68% | 48.15% | 33.91% | 25.40% | 49.57% | 35.49%
 | BQSquare | 48 | 26 | 48.39% | 122.43% | 164.13% | 78.94% | 190.86% | 222.01%
 | BlowingBubbles | 48 | 26 | 61.66% | 93.76% | 99.53% | 65.48% | 99.64% | 104.03%
 | RaceHorses | 32 | 26 | 23.86% | 42.97% | 43.47% | 24.81% | 50.04% | 51.50%
E | FourPeople | 64 | 80 | 52.18% | 94.94% | 97.68% | 68.87% | 110.01% | 115.11%
 | Johnny | 64 | 80 | 59.83% | 91.70% | 97.79% | 85.13% | 115.38% | 125.32%
 | KristenAndSara | 64 | 80 | 51.75% | 81.80% | 88.03% | 67.49% | 97.33% | 100.58%
F | BasketballDrillText | 48 | 60 | 48.18% | 62.36% | 62.05% | 56.60% | 69.91% | 69.45%
 | ArenaOfValor | 64 | 52 | 42.81% | 51.64% | 49.91% | 42.82% | 51.60% | 50.02%
 | SlideEditing | 32 | 27 | 75.61% | 82.83% | 84.52% | 63.89% | 70.67% | 72.98%
 | SlideShow | 16 | 20 | 30.99% | 48.91% | 51.57% | 38.73% | 57.49% | 62.05%

## Slide 17: Parallel processing
Each thread encode redundant (1+C2) frames and (N*C2) frames

## Slide 18: Simulation results
Anchor: Single thread encoding
 | Sequence | C1 | Scheme 2 |  | 
 |  |  | Y | Cb | Cr
B | MarketPlace | 64 |  |  | 
 | RitualDance | 64 |  |  | 
 | Cactus | 48 |  |  | 
 | BasketballDrive | 48 |  |  | 
 | BQTerrace | 64 |  |  | 
C | BasketballDrill | 48 | -0.02% | 0.25% | 0.33%
 | BQMall | 64 | -0.02% | 0.01% | 0.11%
 | PartyScene | 48 | 0.00% | 0.09% | 0.16%
 | RaceHorses | 32 | -0.19% | -0.18% | -0.17%
D | BasketballPass | 64 | -0.20% | -0.83% | -0.23%
 | BQSquare | 48 | 0.07% | -0.28% | -0.59%
 | BlowingBubbles | 48 | 0.05% | -0.25% | -0.03%
 | RaceHorses | 32 | 0.15% | -0.13% | 0.36%
E | FourPeople | 64 |  |  | 
 | Johnny | 64 |  |  | 
 | KristenAndSara | 64 |  |  | 
F | BasketballDrillText | 48 |  |  | 
 | ArenaOfValor | 64 |  |  | 
 | SlideEditing | 32 |  |  | 
 | SlideShow | 16 |  |  | 
N = 2

## Slide 19: Conclusion
Proposals for ultra low-latency encoding
  Revised software
  Test conditions
  Parallel processing
Requests to decide CTC for ultra low-latency encoding.