## Slide 1: JVET-N0152: On motion refinement parameter derivation in BDOF
Ruoyang Yu
Ericsson
2018-03-18

## Slide 2: Bi-directional optical flow (BDOF)
BDOF derives a motion refinement parameter (Vx, Vy) for each 4x4 subblock inside a CU.
During the derivation of (Vx, Vy), a window Ω of size 6x6 is required for calculating parameters S1, S2, S3, S5 and S6.
Where,

## Slide 3: Proposal (modification #1)
Reduce the window size for calculating S1-S6 from 6x6 to 4x4.

## Slide 4: Benefit of modification #1
Reduced multiplication and addition operations.
  The following tables show the operation counts for calculating the S1, S2, S3, S5 and S6 parameters for a 128x128 CU.
    Case 1: Calculate ,, , and on the fly.
    Case 2: Pre-calculate ,, , and .
More friendly for software SIMD optimization.
 | Multiplications | Additions
Anchor (VTM-4.0) | 1024 * 36 * 5 = 184320 | 1024 * 35 * 5 = 179200
Proposed | 1024 * 16 * 5 = 81920 | 1024 * 15 * 5 = 76800
 | Multiplications | Additions
Anchor (VTM-4.0) | (128 + 2) * (128 + 2) * 5 = 84500 | 1024 * 35 * 5 = 179200
Proposed | 128 * 128 * 5 = 81920 | 1024 * 15 * 5 = 76800

## Slide 5: Proposal (modification #2)
As the window gets reduced, the right-shift for parameters and can be reduced by 1 to keep the parameters at a higher precision.

## Slide 6: Bit-width comparison between VTM and the proposal
Parameter | bit-width (VTM-4) | bit-width (Proposal)
, | 16 | 16
, | bitDepth + 3 | bitDepth + 3
 | 21 - bitDepth | 22 – bitDepth
, | 11 | 12
, , | 27 | 27
, | 37 - bitDepth | 37 - bitDepth
Parameter | bit-width (VTM-4) | bit-width (Proposal)
 | 16 | 16
 | bitDepth + 3 | bitDepth + 3
 | 21 - bitDepth | 22 – bitDepth
 | 11 | 12
 | 27 | 27
 | 37 - bitDepth | 37 - bitDepth

## Slide 7: Results
Proposed method (modification #1 and #2)

## Slide 8: Results
Proposed method (modification #1 and #2) + both SAD block level and sub-block level early termination off

## Slide 9: Conclusion
The proposed method reduces the amount of multiplication and addition operations.
The proposed method is more friendly for software SIMD optimization.
The impact on the BD-rate performance is asserted to be marginal.
Propose to consider further studying in a CE.

## Slide 11: Results
Modification #1 only (4x4 window)