## Slide 1: Non-CE8: IBC Reference Memory for Arbitrary CTU Size
H. Gao, S. Esenlik, B. Wang, A. M. Kotra, J. Chen

## Slide 2
Problem Statement
The IBC reference memory is optimized for 128x128 CTU size
For smaller CTU, hardware reference memory is not fully used.
For example for 64x64 CTU, 1/4 of the hardware reference memory is occupied.

## Slide 3
Proposed Method 1
Instead of left 1 CTU, left ((128/CTUsize)2 - 1) CTUs are used as IBC reference area
  For 64x64 CTU size, left 3 CTUs and current CTU are used as IBC reference area
  For 32x32 CTU size, left 15 CTUs and current CTU are used as IBC reference area

## Slide 4
Proposed Method 1
 |  |  | Y | U | V | EncT | DecT
CTU 64x64 | AI | ClassF | -4.36% | -4.36% | -4.20% | 104% | 100%
 |  | TGM | -13.37% | -13.47% | -13.52% | 99% | 96%
 | RA | ClassF | -3.44% | -3.41% | -3.52% | 101% | 99%
 |  | TGM | -6.72% | -6.96% | -7.01% | 99% | 99%
CTU 32x32 | AI | ClassF | -7.32% | -7.27% | -7.24% | 104% | 98%
 |  | TGM | -21.63% | -21.74% | -21.83% | 94% | 92%
 | RA | ClassF | -5.49% | -5.54% | -5.19% | 101% | 99%
 |  | TGM | -10.97% | -11.29% | -11.42% | 99% | 98%

## Slide 5
Proposed Method 2
Instead of left 1 CTU, left ((128/CTUsize)2 - 1) CTUs are used as IBC reference area
  For 64x64 CTU size, left 3 CTUs and current CTU are used as IBC reference area
  For 32x32 CTU size, left 15 CTUs and current CTU are used as IBC reference area
Additional discontinues vertical edge, because of the hardware memory discontinuity
  If NumofCtu % (128/Ctusize) = 0, set as discontinue, where NumofCtu is number of CTUs from left picture boundary

## Slide 6
Proposed Method 2
 |  |  | Y | U | V | EncT | DecT
CTU 64x64 | AI | ClassF | -4.07% | -4.07% | -4.00% | 105% | 100%
 |  | TGM | -12.40% | -12.50% | -12.54% | 100% | 96%
 | RA | ClassF | -3.17% | -3.17% | -3.22% | 101% | 100%
 |  | TGM | -6.09% | -6.44% | -6.44% | 99% | 98%
CTU 32x32 | AI | ClassF | -7.10% | -7.04% | -6.98% | 106% | 98%
 |  | TGM | -21.06% | -21.20% | -21.28% | 96% | 93%
 | RA | ClassF | -5.34% | -5.31% | -5.19% | 102% | 100%
 |  | TGM | -10.63% | -10.92% | -11.05% | 100% | 99%

## Slide 7
Conclusion
IBC reference area is extended for smaller CTU case, without increase the hardware reference memory
Method 1 achieves -4.36%/-3.44% AI/RA and -13.37%/-6.72% coding gain for ClassF and TGM when CTU size is 64x64
Method 2 achieves -4.07%/-3.17% AI/RA and -12.40%/-6.09% coding gain for ClassF and TGM when CTU size is 64x64
Proposed to be adopted into next version of VVC draft