## Slide 1: JVET-N0183 AHG16/Non-CE3: Shared MPM list
Anand Meher Kotra, Semih Esenlik, Jianle Chen, Biao Wang, Han Gao

## Slide 2: Overview
Problem
  In VTM-4.0.1, Luma MPM list construction is down to 4 x 4 block level
    Complex MPM list constructions make it difficult for hardware implementations
Solution
  “Shared” MPM list
  Extend the concept of shared Merge/IBC lists also to MPM list construction
  Advantage:
    Worst case of 1 MPM list per 32 samples
    All blocks in shared MPM region can derive Intra mode in parallel
Result:
  Negligible BD-Rate change with no complexity increase

## Slide 3: Shared MPM list (worst case of 1 list per 32 samples)

## Slide 4: Shared MPM list (worst case of 3 list per 32 samples but all MPM lists can be constructed in parallel)

## Slide 5: Spec text changes (very minimal)
8.4.2 Derivation process for luma intra prediction mode
The variables xSmr, ySmr, smrWidth, smrHeight, and smrNumHmvpCand are derived as follows:
xSmr = IsInSmr[ xCb ][ yCb ] ? SmrX[ xCb ][ yCb ] : xCb (8‑xxx)
ySmr = IsInSmr[ xCb ][ yCb ] ? SmrY[ xCb ][ yCb ] : yCb (8‑xxx)
smrWidth = IsInSmr[ xCb ][ yCb ] ? SmrW[ xCb ][ yCb ] : cbWidth (8‑xxx)
smrHeight = IsInSmr[ xCb ][ yCb ] ? SmrH[ xCb ][ yCb ] : cbHeight (8‑xxx)
Note: If IsInSmr[ xCb ][ yCb ] is true, then IntraLumaRefLineIdx[ xCb ][ yCb ] is inferred as 0 and IntraSubPartitionsSplitType is inferred as ISP_NO_SPLIT
The neighbouring locations ( xNbA, yNbA ) and ( xNbB, yNbB ) are set equal to (xSmr xCb − 1, yCb ySmr + cbHeight smrHeight − 1 ) and ( xCb xSmr + smrWidth cbWidth − 1, yCb ySmr − 1 ), respectively.

## Slide 6: Conclusion
Shared MPM list construction proposed
  Extension of Shared Merge/IBC concept present in VTM-4.0.1 also to MPM list construction
Main advantage:
  Worst case of 1 MPM list per 32 samples
  All child nodes in the shared MPM region can derive intra mode in parallel
  No BD-Rate change with no increase in EncT and DecT
Suggest for adoption in next version of working draft text and reference software
Thanks to MediaTek for cross check