## Slide 1: JVET-N0294 CE9-related: Adaptive search pattern for DMVR
S. Sethuraman
Ittiam Systems

## Slide 2: 25-point Exhaustive Search
Though this was not used in any core experiments, this was a condition enforced at the time of adoption of DMVR
Given N SAD execution units, evaluating all 25-points will require ceil(25/N) stages.
  N = 9, 3 stages
  N = 13, 2 stages
  N = 25, 1 stage
In software implementations, computing all 25 costs nearly triples the number of cost computations done with the adaptive search pattern studied in CEs.
Given the parametric error surface based sub-pixel accurate MV refinement, multiple cost values need to be stored anyways

## Slide 3: Earlier adaptive search pattern studied in CEs
Step-1: Compute the costs on 5 points (center + left, top, right, bottom)
Step-2: Compute the cost of 1 diagonal point where the coordinate for the diagonal point is obtained based on the minimum between left and right, and the minimum between top and bottom.
Compute the minimum cost among these 6 points and repeat steps 1 and 2 if center cost is not the minimum.
Total cost evaluations: 5 + 1 + 2 + 1 = 9 (if diagonal point wins) or 5 + 1 + 1 + 1 = 8 (if non-diagonal point wins)
In hardware, this can be realized by evaluating 5 points in a stage and 8 points in a second stage
  Requires max 8 SAD units for 2-stages (compared to 13 for 25-point exh. Search)

## Slide 4: Results – VTM4 vs. 25-position exhaustive search
0.04% average luma BD-RATE gain seen
  UHD gets higher gain
EncT ratio increases to 101%; DecT ratio increases to 102%
  Instead of just 9 cost evaluations with adaptive search pattern, 25 cost evaluations are performed

## Slide 5: Modified adaptive search pattern
To reduce the BD-RATE gap against the 25-point exhaustive search
Step-1: Compute the costs on 5 points (center + left, top, right, bottom)
Step-2: Compute the cost of 2 diagonal points that flank the position with the lowest cost among the 5 points in step-1.
Obtain the positions with the lowest cost among the 7 and repeat step-1 and step-2 if center cost is not the minimum
Total number of costs evaluated: 5 + 2 + 2 + 2 = 11 (if diagonal point is chosen) or 5 + 2 + 1 + 2 = 10 (if non-diagonal point is chosen)
In hardware, a 2-stage design can first evaluate 5+2=7 points and then evaluate cost at 5 or 3 points
  Requires only 7 SAD execution units (compared to 13 for 25-point exh. Search)

## Slide 6: Results – VTM4 vs. Proposed modified adaptive search
0.03% average luma BD-RATE gain seen
DecT ratio increases to 101%
  2 additional cost evaluations only are performed relative to the earlier adaptive search pattern

## Slide 7: Conclusions
Adaptive search patterns help reduce both hardware gate-count and average decoding time in software implementations
  Adaptive search pattern studied in CE9 has a 0.04% BD-RATE gap w.r.t 25-point exhaustive search
    Cost evaluated only at up to 9 search points
    But, requires only 8 SAD units for a 2-stage cost evaluation design (compared to 13 for exhaustive search)
    Reduces DecT by 2%
  Modified adaptive search pattern proposed
    Bridges 0.03% out of the 0.04% (i.e. off by only 0.01% w.r.t exhaustive 25-point)
    Cost evaluated only at up to 11 search points
    Requires only 7 SAD units for a 2-stage cost evaluation design
    Reduces DecT by 1+%
It is requested that adaptive search patterns be further studied

## Slide 8: Thanks to Qualcomm for Cross-checking!