## Slide 1: JVET-N0295 CE9-related: Using extended samples during DMVR SAD cost evaluations
S. Sethuraman
Ittiam Systems

## Slide 2: Proposed Method
Compute SAD cost using a block larger than the current sub-block
  Increases aperture
  Uses samples from adjacent sub-blocks
  Has the potential to reduce sub-block boundary discontinuities after refinement at the sub-block level
  Extension can be different in the horizontal (Ex) and vertical (Ey) directions
Bilinear interpolation needs to produce additional samples
  (sbW + 2*Sx + 2*Ex) x (sbH + 2*Sy + 2*Ey)
Cost computation complexity increases
  (sbW + 2*Ex) x (sbH + 2*Ey)
No impact on DCTIF

## Slide 3: Bilinear interpolated samples with extension

## Slide 4: Extended block of samples for matching cost evaluation

## Slide 5: Worst-case Complexity Analysis
So, it is preferable to disable the extension for 4x16 and 8x8 sub-block sizes

## Slide 6: Results for Ex = Ey = 2
Offers 0.11% BD-RATE gain over VTM4.0
Small increases in EncT (1%) and DecT (2%)

## Slide 7: Results for Ex = Ey = 1
Gain reduces by 0.04%

## Slide 8: Results for Ex = Ey = 2 – Extension disabled for 4x16, 8x8
Very little BD-RATE impact with disabling extension for 4x16 and 8x8 sub-block sizes
Worst-case bounded
Good to consider along with vertical decimation of predicted samples proposed in JVET-N0179 to further reduce the worst-case complexity

## Slide 9: Conclusions
Using extended samples during SAD cost evaluations in DMVR offers the potential to improve the coding efficiency of DMVR
  0.11% average luma BDRATE gain with Ex = Ey = 2
  0.07% average luma BDRATE gain with Ex = Ey =1
  To limit worst-case complexity, disabling use of extended samples based matching for 4x16 and 8x8 sub-blocks
    0.10% average luma BDRATE gain with Ex = Ey = 2
It is requested that extended samples based matching be studied further in CE with the proposed restriction
  Can also be combined with JVET-N0179 to reduce the worst-case complexity further

## Slide 10: Thanks to ETRI for Cross-checking!