## Slide 1: JVET-N0380 CE4-related Fix of MMVD signalling
G. Li, X. Xu, X. Li, S. Liu
2019/03

## Slide 2: Introduction
MMVD can use up to 2 base candidates
mmvd_merge_flag is signalled
  Specifying whether 1st or 2nd merge candidate is used as base
When allowed max number of merge candidate is 1 (MaxNumMergeCand=1)
  The second base becomes undefined
  Current VTM uses zero MV as the 2nd base, NOT aligned with VVC Working Draft

## Slide 3: Proposed Method
Conditional signalling of mmvd_merge_flag
  Only signalled when MaxNumMergeCand > 1
  Otherwise, inferred as 0
Zero MV filling in software can be removed

## Slide 4: Text Changes
7.3.6.7 Merge data syntax
7.4.7.7 Merge data semantics
When mmvd_merge_flag[ x0 ][ y0 ] is not present, it is inferred to be equal to 0.
merge_data( x0, y0, cbWidth, cbHeight ) { | Descriptor
if ( CuPredMode[ x0 ][ y0 ] = = MODE_IBC ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { | 
mmvd_flag[ x0 ][ y0 ] | ae(v)
if( mmvd_flag[ x0 ][ y0 ] = = 1 ) { | 
if( MaxNumMergeCand > 1 ) | 
mmvd_merge_flag[ x0 ][ y0 ] | ae(v)
mmvd_distance_idx[ x0 ][ y0 ] | ae(v)
mmvd_direction_idx[ x0 ][ y0 ] | ae(v)
} else { | 
… | 

## Slide 5: Simulation results
Anchor: VTM-4.0.1, MaxNumMergeCand = 1
 | Low delay B Main10 |  |  | 
 | Over VTM 4.0.1 |  |  | 
Y | U | V | EncT | DecT
-0.09% | -0.21% | 0.00% | 96% | 97%
-0.19% | -0.33% | -0.24% | 98% | 100%
-0.24% | -0.68% | -1.08% | 97% | 97%
-0.16% | -0.37% | -0.35% | 97% | 98%
-0.16% | -0.10% | 0.14% | 100% | 105%
-0.06% | 0.21% | -0.15% | 99% | 103%
 |  | Random access Main10 |  |  | 
 |  | Over VTM 4.0.1 |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.02% | -0.05% | 93% | 99%
Class A2 | 0.05% | -0.05% | 0.02% | 94% | 100%
Class B | 0.01% | -0.03% | -0.03% | 93% | 100%
Class C | 0.03% | 0.09% | 0.11% | 94% | 101%
Class E |  |  |  |  | 
Overall | 0.02% | 0.00% | 0.01% | 93% | 100%
Class D | 0.12% | 0.08% | 0.04% | 94% | 99%
Class F | -0.01% | 0.04% | 0.09% | 93% | 100%

## Slide 6: Conclusion
When max number of merging candidate is set to 1
  0.02% BD-rate on RA, 93% encoding time,
  -0.16% BD-rate on LDB, 97% encoding time.
Solved undefined Affine MMVD behavior in VVC specification
Thanks to Samsung for crosschecking!

## Slide 7
Thank you!