## Slide 1: JVET-N0417: Simplified luma dependent chroma residual scaling of in-loop reshaper
Nan Hu, Vadim Seregin, Marta Karczewicz

## Slide 2: luma dependent chroma residual scaling of in-loop reshaper (decoder)
avgluma
Average value of luma block
LUT
c(avgluma)
resic’ = resic * c(avgluma)
VTM4
Proposed
avgluma
Average value of sub-sampled luma block
LUT
c(avgluma)
resic’ = resic * c(avgluma)

## Slide 3: Results
Subsample step size = 2 Subsample step size = 4
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.03% | 0.04% | 100% | 101%
Class A2 | 0.00% | -0.03% | 0.00% | 99% | 100%
Class B | 0.01% | -0.02% | 0.07% | 101% | 101%
Class C | 0.00% | -0.06% | -0.11% | 100% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | -0.03% | 0.00% | 100% | 101%
Class D | -0.03% | 0.05% | -0.08% | 100% | 99%
Class F | 0.01% | -0.02% | -0.01% | 100% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.07% | -0.07% | 100% | 100%
Class C | -0.01% | 0.13% | -0.11% | 100% | 100%
Class E | 0.03% | -0.10% | -0.03% | 101% | 100%
Overall | 0.00% | 0.05% | -0.07% | 100% | 100%
Class D | -0.04% | -0.40% | -0.82% | 100% | 99%
Class F | -0.03% | -0.11% | 0.19% | 100% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.01% | 0.00% | 101% | 100%
Class A2 | 0.00% | -0.03% | 0.07% | 100% | 101%
Class B | -0.01% | -0.03% | 0.04% | 100% | 100%
Class C | 0.01% | 0.04% | -0.05% | 99% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | -0.01% | 0.02% | 100% | 100%
Class D | -0.02% | -0.13% | -0.07% | 100% | 100%
Class F | -0.01% | 0.02% | -0.02% | 99% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.02% | 0.04% | 0.18% | 100% | 100%
Class C | 0.02% | 0.33% | 0.06% | 100% | 98%
Class E | 0.01% | 0.58% | -0.18% | 100% | 98%
Overall | 0.00% | 0.27% | 0.05% | 100% | 99%
Class D | -0.01% | 0.18% | -0.63% | 101% | 100%
Class F | -0.10% | -0.16% | -0.07% | 98% | 97%