## Slide 1: JVET-N0432: AHG16/Non-CE3: On 1xN and 2xN subpartitions in intra subpartition coding
A. K. Ramasubramonian, G. Van der Auwera, T. Hsieh, V. Seregin, L. Pham Van, M. Karczewicz
Qualcomm

## Slide 2: Problem statement
Intra subpartition coding (ISP)
  Some vertical partitions result in 1xN and 2xN subpartitions
    Coding blocks 4xN (N > 8) and 8xN (N > 4) in size
  ISP subpartitions depend on reconstructed samples of preceding subpartitions
    Exacerbates worst-case delay
  Prediction of 1xN and 2xN subpartitions
    May result in read/write overhead

## Slide 3: Proposal
To mitigate problems arising due to 1xN and 2xN subpartitions of ISP
  For vertical ISP, minimum prediction region width of four samples
    One prediction region reconstructed before next prediction region
  For 4xN coding blocks and vertical ISP, restrict prediction to VER intra mode
Negligible BD rate loss: 0.04% (AI), 0.01% (RA)
Coding block sizes | Partition sizes for prediction | Transform sizes
4x8 | 4x8 (vertical mode only) | 2xN
4xN (N > 8) | 4xN (vertical mode only) | 1xN
8xN (N > 4) | 4xN | 2xN
Coding block sizes | Partition sizes for prediction | Transform sizes
4x8 | 2xN | 2xN
4xN (N > 8) | 1xN | 1xN
8xN (N > 4) | 2xN | 2xN
Current
Proposed

## Slide 4: Proposal
For vertical ISP, minimum prediction region width of four samples
For 4xN (N >= 8) coding blocks and vertical ISP, restrict prediction to VER intra mode
4xN prediction region

## Slide 5: Simulation results
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.02% | 0.05% | 101% | 102%
Class A2 | 0.02% | 0.20% | 0.00% | 102% | 102%
Class B | 0.02% | 0.08% | 0.03% | 101% | 103%
Class C | 0.07% | 0.04% | 0.12% | 101% | 102%
Class E | 0.09% | 0.15% | 0.10% | 101% | 101%
Overall | 0.04% | 0.09% | 0.06% | 101% | 102%
Class D | 0.07% | 0.19% | -0.04% | 100% | 100%
Class F | 0.04% | 0.00% | -0.12% | 101% | 102%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.08% | -0.01% | 100% | 100%
Class A2 | 0.00% | -0.03% | -0.01% | 97% | 95%
Class B | 0.02% | 0.00% | -0.20% |  | 
Class C | 0.02% | -0.09% | -0.23% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.01% | -0.01% | -0.13% |  | 
Class D | 0.06% | -0.04% | -0.09% | 100% | 99%
Class F | -0.03% | 0.00% | -0.08% |  | 

## Slide 6: Conclusions
Proposal to mitigate problems arising due to 1xN and 2xN subpartitions of ISP
Negligible BD rate loss: 0.04% (AI), 0.01% (RA)
Proposed to include it in the VVC specification