## Slide 1: JVET-N0468 AhG2 : Editorial Suggestion on the text specification for Inter and IBC mode
H. Jang, J. Nam, N. Park, J. Lim, S. Kim

## Slide 2: Introduction
In this contribution, Only editorial change is suggested for inter prediction and intra block copy.
In VTM-4.0,
  IBC is signaled as a separate prediction mode
  Inter and IBC prediction mode has separate candidate list.
  Spatial candidates for inter prediction are derived from inter coded neighbor block.
  Spatial candidates for intra block copy are derived from IBC coded neighbor block.
However, current text specification is not described distinctly for above constraint.

## Slide 3: Proposed editorial part
#1. Derivation process for spatial merging candidates from the neighboring spatial blocks which is coded MODE_INTER.
#2. Derivation process for spatial motion vector predictor candidates from the neighboring spatial blocks which is coded MODE_INTER.
#3. Derivation process for IBC spatial merging candidates from the neighboring spatial blocks which is coded MODE_IBC.

## Slide 4
The variable CurrPicIsOnlyRef, specifying that the current decoded picture is the only reference picture for the current tile group, is derived as follows: CurrPicIsOnlyRef = sps_cpr_enabled_flag && ( tile_group_type = = P ) && (7‑39) ( num_ref_idx_active_minus1[ 0 ] = = 0 )
#4. Unreferenced text specification clean-up