## Slide 1: JVET-N0491 Transform Candidate Ordering
Christopher Hollmann, Davood Saffar,
Per Wennersten, Jacob Ström
Christopher Hollmann
Ericsson
2019-03-19

## Slide 2: Proposed changes (1)
Remove combination DCT-8 horizontal and vertical
Replace size 32 DCT-8 with existing DCT-2
These changes are identical to the ones in CE6-2.3.
mts_index
DCT-2 hor
DCT-2 ver
DST-7 hor
DST-7 ver
DST-7 ver
DCT-8 hor
DST-7 ver
DCT-8 hor

## Slide 3: Proposed changes (2)
Candidate ordering
(DCT-8, DST-7) and (DST-7, DCT-8) are evaluated and coded in order depending on intra prediction mode or shape
Small difference for CTC, but larger difference if fewer candidates are evaluated
Change to CTC: Reduce MTSIntraMaxCand and MTSInterMaxCand to 2
Prediction | Condition | First candidate | Second candidate
Intra MTS | Intra mode > 34 | (DCT-8, DST-7) | (DST-7, DCT-8)
 | Intra mode <= 34 | (DST-7, DCT-8) | (DCT-8, DST-7)
Inter MTS | Height > Width | (DCT-8, DST-7) | (DST-7, DCT-8)
 | Height <= Width | (DST-7, DCT-8) | (DCT-8, DST-7)
mts_index
DCT-2 hor
DCT-2 ver
DST-7 hor
DST-7 ver
First candidate
Second candidate

## Slide 4: Results T1: (3, 4) vs (3, 4)
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 with MTS Inter On |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.08% | -0.24% | -0.30% | 94% | 92%
Class C | 0.05% | -0.03% | -0.06% | 94% | 97%
Class E | 0.00% | 0.25% | 1.82% | 98% | 97%
Overall | 0.05% | -0.05% | 0.31% | 95% | 95%
Class D | 0.02% | 0.47% | 0.23% | 93% | 94%
Class F | 0.08% | 0.36% | -0.01% | 95% | 91%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 with MTS Inter On |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.06% | -0.10% | 91% | 91%
Class A2 | 0.04% | 0.05% | -0.12% | 93% | 96%
Class B | -0.02% | 0.03% | -0.12% | 96% | 96%
Class C | 0.03% | 0.11% | -0.03% | 95% | 99%
Class E |  |  |  |  | 
Overall | 0.01% | 0.04% | -0.09% | 94% | 96%
Class D | -0.01% | -0.09% | -0.11% | 96% | 96%
Class F | -0.08% | -0.19% | -0.03% | 93% | 96%
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.09% | 0.09% | 0.01% | 100% | 104%
Class A2 | -0.04% | 0.08% | 0.02% | 97% | 101%
Class B | -0.04% | 0.02% | 0.04% | 99% | 106%
Class C | -0.01% | -0.04% | -0.08% | 98% | 99%
Class E | -0.05% | -0.07% | 0.04% | 96% | 97%
Overall | -0.04% | 0.01% | 0.01% | 98% | 102%
Class D | -0.01% | 0.12% | -0.04% | 96% | 94%
Class F | 0.01% | -0.05% | -0.08% | 98% | 104%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.16% | 0.05% | 96% | 94%
Class A2 | -0.04% | -0.04% | -0.02% | 97% | 95%
Class B | 0.00% | 0.03% | -0.13% | 96% | 94%
Class C | 0.02% | 0.01% | -0.11% | 97% | 97%
Class E |  |  |  |  | 
Overall | -0.01% | -0.03% | -0.07% | 97% | 95%
Class D | 0.02% | -0.10% | -0.09% | 97% | 96%
Class F | -0.06% | -0.21% | -0.03% | 100% | 96%
CTC with MTS = 1
CTC with MTS = 3
LDB: -0.04% -0.09% 0.08% 98% 95%

## Slide 5: Results T3: (2, 2) vs (2, 2)
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 with MTS Inter On |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | 0.04% | -0.21% | 97% | 93%
Class C | 0.01% | 0.29% | -0.01% | 98% | 98%
Class E | -0.18% | -0.63% | -0.85% | 99% | 100%
Overall | -0.03% | -0.04% | -0.31% | 98% | 96%
Class D | 0.07% | 0.17% | -0.49% | 103% | 103%
Class F | -0.20% | 0.20% | 0.13% | 97% | 95%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 with MTS Inter On |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.01% | 0.05% | 98% | 99%
Class A2 | -0.03% | -0.09% | -0.14% | 97% | 98%
Class B | -0.02% | -0.13% | -0.06% | 99% | 99%
Class C | -0.03% | -0.20% | -0.03% | 103% | 101%
Class E |  |  |  |  | 
Overall | -0.02% | -0.11% | -0.05% | 99% | 99%
Class D | -0.01% | -0.21% | 0.31% | 98% | 101%
Class F | 0.02% | 0.09% | 0.06% | 94% | 100%
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | -0.03% | -0.01% | 96% | 97%
Class A2 | -0.07% | -0.08% | 0.04% | 97% | 95%
Class B | -0.06% | 0.01% | 0.04% | 97% | 99%
Class C | -0.03% | 0.11% | -0.06% | 97% | 97%
Class E | -0.10% | -0.02% | -0.07% | 98% | 99%
Overall | -0.07% | 0.00% | -0.01% | 97% | 98%
Class D | -0.04% | -0.02% | 0.10% | 101% | 98%
Class F | -0.01% | -0.01% | 0.02% | 98% | 95%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.02% | -0.08% | 98% | 99%
Class A2 | -0.02% | -0.01% | -0.03% | 99% | 93%
Class B | -0.01% | -0.12% | 0.02% | 101% | 100%
Class C | -0.05% | -0.23% | -0.08% | 99% | 99%
Class E |  |  |  |  | 
Overall | -0.02% | -0.11% | -0.04% | 100% | 98%
Class D | -0.02% | -0.46% | 0.19% | 101% | 99%
Class F | 0.01% | -0.02% | -0.03% | 94% | 99%
CTC with MTS = 1
CTC with MTS = 3
LDB: -0.03% -0.15% -0.21% 99% 99%

## Slide 6: Results T2: (3, 4) vs (2, 2)
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 with MTS Inter On |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.16% | -0.29% | -0.67% | 90% | 90%
Class C | 0.14% | 0.34% | -0.08% | 90% | 97%
Class E | 0.13% | -0.57% | 0.36% | 93% | 95%
Overall | 0.15% | -0.15% | -0.22% | 91% | 93%
Class D | 0.17% | 0.19% | -0.56% | 93% | 99%
Class F | -0.11% | -0.27% | -0.07% | 93% | 93%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 with MTS Inter On |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.10% | -0.04% | -0.08% | 89% | 94%
Class A2 | 0.18% | -0.02% | -0.28% | 91% | 97%
Class B | 0.15% | -0.22% | -0.09% | 93% | 98%
Class C | 0.12% | -0.26% | -0.11% | 94% | 98%
Class E |  |  |  |  | 
Overall | 0.14% | -0.15% | -0.13% | 92% | 97%
Class D | 0.12% | -0.41% | -0.04% | 90% | 96%
Class F | 0.07% | -0.08% | -0.18% | 89% | 97%
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | -0.10% | -0.05% | 87% | 101%
Class A2 | 0.09% | -0.02% | -0.06% | 86% | 100%
Class B | 0.06% | -0.08% | -0.04% | 86% | 103%
Class C | 0.10% | -0.14% | -0.14% | 87% | 101%
Class E | 0.02% | -0.06% | -0.20% | 87% | 100%
Overall | 0.06% | -0.08% | -0.09% | 87% | 101%
Class D | 0.12% | -0.10% | -0.25% | 87% | 98%
Class F | 0.05% | -0.13% | -0.04% | 92% | 103%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.15% | -0.05% | 96% | 95%
Class A2 | -0.01% | 0.02% | -0.04% | 98% | 95%
Class B | 0.05% | -0.15% | -0.11% | 99% | 96%
Class C | 0.05% | -0.21% | -0.25% | 98% | 95%
Class E |  |  |  |  | 
Overall | 0.03% | -0.13% | -0.12% | 98% | 95%
Class D | 0.05% | -0.48% | -0.04% | 100% | 95%
Class F | 0.05% | -0.14% | -0.20% | 107% | 95%
CTC with MTS = 1
CTC with MTS = 3
LDB: 0.02% -0.08% -0.16% 97% 94%

## Slide 7: Summary & Recommendation
Recommendation:
Set the default values for MTSIntraMaxCand and MTSInterMaxCand to 2
Adopt this proposal into VTM-5.0 as very similar technology has been part of CE6
3 changes:
No DCT-8 horizontal and vertical
Replace size-32 DCT-8 with DCT-2
Dynamic candidate ordering

## Slide 9: VTM-4.0 CTC (3, 4) vs (2, 2)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0. MTS = 3 (3. 4) [T2] |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.12% | -0.04% | -0.13% | 91% | 94%
Class A2 | 0.21% | 0.07% | -0.14% | 94% | 99%
Class B | 0.16% | -0.09% | -0.03% | 94% | 99%
Class C | 0.15% | -0.06% | -0.08% | 92% | 98%
Class E |  |  |  |  | 
Overall | 0.16% | -0.04% | -0.08% | 93% | 98%
Class D | 0.13% | -0.20% | -0.35% | 92% | 95%
Class F | 0.05% | -0.16% | -0.24% | 94% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0. MTS = 3 (3. 4) [T2] |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.14% | -0.33% | -0.47% | 93% | 97%
Class C | 0.13% | 0.05% | -0.06% | 92% | 100%
Class E | 0.32% | 0.05% | 1.22% | 94% | 94%
Overall | 0.18% | -0.11% | 0.09% | 93% | 97%
Class D | 0.10% | 0.02% | -0.06% | 90% | 96%
Class F | 0.10% | -0.45% | -0.20% | 95% | 98%
 | All Intra Main10 |  |  |  | 
 | Over VTM-4.0 MTS (3. 4) [T2] |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.14% | -0.06% | -0.04% | 91% | 104%
Class A2 | 0.16% | 0.06% | -0.10% | 89% | 104%
Class B | 0.12% | -0.08% | -0.07% | 88% | 104%
Class C | 0.13% | -0.25% | -0.08% | 90% | 104%
Class E | 0.12% | -0.04% | -0.14% | 90% | 102%
Overall | 0.13% | -0.09% | -0.08% | 89% | 104%
Class D | 0.16% | -0.08% | -0.34% | 86% | 99%
Class F | 0.06% | -0.12% | -0.06% | 94% | 108%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 MTS (3. 4) [T2] |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.06% | -0.13% | 0.04% | 99% | 95%
Class A2 | 0.01% | 0.03% | -0.01% | 99% | 103%
Class B | 0.06% | -0.02% | -0.13% | 98% | 96%
Class C | 0.09% | 0.01% | -0.16% | 98% | 96%
Class E |  |  |  |  | 
Overall | 0.06% | -0.02% | -0.08% | 98% | 97%
Class D | 0.06% | -0.02% | -0.23% | 99% | 96%
Class F | 0.04% | -0.11% | -0.17% | 114% | 96%
LDB: 0.05% 0.07% 0.05% 98% 95%