## Slide 1: JVET-P0082: BDPCM for Lossless
Alican Nalci, Hongtao Wang, Hilmi E. Egilmez
Muhammed Coban, Vadim Seregin
and Marta Karczewicz
  Qualcomm Inc.
Date: 10/6/2019
Geneva, CH

## Slide 2: Introduction
In VTM-6.0-lossless branch, BDPCM related flags are signalled but BDPCM is not applied when CU level transquant bypass mode is enabled.
BDPCM is used in VTM-6.0 with transform skip (TS) residual coding.
We propose to enable BDPCM for lossless.
We assess BDPCM performance with TS or transform residual (TR) coding.
Proposal #1
Proposal #2
Proposal #3
Proposal #4
Proposal #5
Proposal
TR BDPCM
TR BDPCM
TS BDPCM
TS BDPCM
TR BDPCM
TS BDPCM
TR Chroma BDPCM
TR BDPCM
TS BDPCM
TR & TS Chroma BDPCM

## Slide 3
Enable BDPCM for both TR and TS residual coding.
As in VVC, we only signal only Horizontal or Vertical mode ( intra_bdpcm_dir_flag % 2 )
We signal the TS flag for lossless to distinguish between TR and TS coding:
Proposal #1
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex, chType ) { | Descriptor
…. | 
if( sps_transform_skip_enabled_flag && ( cu_transquant_bypass_flag ¦ ¦ !BdpcmFlag[ x0 ][ y0 ] ) && tbWidth <= MaxTsSize && tbHeight <= MaxTsSize ) | 
transform_skip_flag[ x0 ][ y0 ] | ae(v)
…. | 
  0
  1
Horizontal TS BDPCM
Vertical TS BDPCM
  2
  3
Horizontal TR BDPCM
Vertical TR BDPCM
Two TR BDPCM modes for lossless.
intra_bdpcm_dir_flag:

## Slide 4
Enable BDPCM for both TS and TR residual coding.
Results – Proposal #1
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | AHG18 LL | Proposal 1 |  | AHG18 LL | Proposal 1 |  | AHG18 LL | Proposal 1 | 
Class A1 | 2.2 | 2.2 | -0.87% | 2.3 | 2.3 | -0.36% |  |  | 
Class A2 | 1.7 | 1.8 | -1.18% | 1.9 | 1.9 | -0.27% |  |  | 
Class B | 2.1 | 2.1 | -1.34% | 2.3 | 2.3 | -0.26% | 2.3 | 2.3 | -0.29%
Class C | 2.1 | 2.1 | -1.45% | 2.6 | 2.6 | -0.34% | 2.6 | 2.6 | -0.38%
Class D | 1.9 | 2.0 | -2.66% | 2.8 | 2.8 | -0.52% | 2.7 | 2.8 | -0.47%
Class E | 2.9 | 3.0 | -1.86% |  |  |  | 3.3 | 3.4 | -0.99%
Class F | 5.5 | 5.7 | -3.80% | 39.4 | 41.3 | -2.75% | 60.7 | 64.4 | -3.16%
TGM | 12.3 | 12.7 | -3.54% | 112.6 | 115.7 | -2.67% | 142.4 | 146.4 | -2.61%
Overall (A1, A2, B, C, E) | 2.2 | 2.2 | -1.34% | 2.3 | 2.3 | -0.30% | 2.6 | 2.7 | -0.49%
Overall | 4.0 | 4.1 | -2.14% | 25.1 | 25.8 | -1.05% | 35.6 | 36.9 | -1.29%
Enc Time[%] | 113% |  |  | 110% |  |  | 113% |  | 
Dec Time[%] | 91% |  |  | 99% |  |  | 100% |  | 
Table 1. Results with BDPCM enabled both for TS and transform residual coding.

## Slide 5
We use BDPCM only with TR residual coding for lossless.
Lossless always uses TR residual coding.
Proposal #2
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex, chType ) { | Descriptor
…. | 
if( tu_cbf_luma[ x0 ][ y0 ] ) { | 
if( !transform_skip_flag[ x0 ][ y0 ] ¦ ¦ cu_transquant_bypass_flag ) | 
residual_coding( x0, y0, Log2( tbWidth ), Log2( tbHeight ), 0 ) | 
else | 
residual_ts_coding( x0, y0, Log2( tbWidth ), Log2( tbHeight ), 0 ) | 
} | 
… | 
7.3.8.10 Transform unit syntax

## Slide 6
Results – Proposal #2
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | AHG18 LL | Proposal 2 |  | AHG18 LL | Proposal 2 |  | AHG18 LL | Proposal 2 | 
Class A1 | 2.2 | 2.2 | -0.67% | 2.3 | 2.3 | -0.25% |  |  | 
Class A2 | 1.7 | 1.8 | -1.14% | 1.9 | 1.9 | -0.25% |  |  | 
Class B | 2.1 | 2.1 | -1.31% | 2.3 | 2.3 | -0.24% | 2.3 | 2.3 | -0.27%
Class C | 2.1 | 2.1 | -1.38% | 2.6 | 2.6 | -0.31% | 2.6 | 2.6 | -0.33%
Class D | 1.9 | 2.0 | -2.54% | 2.8 | 2.8 | -0.50% | 2.7 | 2.8 | -0.45%
Class E | 2.9 | 3.0 | -1.85% |  |  |  | 3.3 | 3.4 | -0.99%
Class F | 5.5 | 5.7 | -2.75% | 39.4 | 40.2 | -1.14% | 60.7 | 61.2 | -0.81%
TGM | 12.3 | 12.5 | -1.58% | 112.6 | 113.4 | -0.57% | 142.4 | 142.8 | -0.26%
Overall (A1, A2, B, C, E) | 2.2 | 2.2 | -1.28% | 2.3 | 2.3 | -0.26% | 2.6 | 2.7 | -0.47%
Overall | 4.0 | 4.1 | -1.68% | 25.1 | 25.3 | -0.47% | 35.6 | 35.8 | -0.49%
Enc Time[%] | 102% |  |  | 102% |  |  | 103% |  | 
Dec Time[%] | 93% |  |  | 100% |  |  | 100% |  | 
Table 2. Results with BDPCM enabled only for transform residual coding.
Use BDPCM only with TR residual coding for lossless.

## Slide 7
This is the same as the current VVC.
BDPCM is used only with TS residual coding.
Non-BDPCM TR and TS coding can still be used.
Proposal #3
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | AHG18 LL | Proposal 3 |  | AHG18 LL | Proposal 3 |  | AHG18 LL | Proposal 3 | 
Class A1 | 2.2 | 2.2 | -0.32% | 2.3 | 2.3 | -0.17% |  |  | 
Class A2 | 1.7 | 1.7 | -0.30% | 1.9 | 1.9 | -0.13% |  |  | 
Class B | 2.1 | 2.1 | -0.25% | 2.3 | 2.3 | -0.08% | 2.3 | 2.3 | -0.10%
Class C | 2.1 | 2.1 | -0.60% | 2.6 | 2.6 | -0.20% | 2.6 | 2.6 | -0.24%
Class D | 1.9 | 2.0 | -1.53% | 2.8 | 2.8 | -0.35% | 2.7 | 2.8 | -0.36%
Class E | 2.9 | 3.0 | -0.92% |  |  |  | 3.3 | 3.3 | -0.50%
Class F | 5.5 | 5.7 | -3.15% | 39.4 | 41.1 | -2.52% | 60.7 | 64.3 | -3.01%
TGM | 12.3 | 12.7 | -3.16% | 112.6 | 115.5 | -2.54% | 142.4 | 146.3 | -2.57%
Overall (A1, A2, B, C, E) | 2.2 | 2.2 | -0.46% | 2.3 | 2.3 | -0.14% | 2.6 | 2.6 | -0.25%
Overall | 4.0 | 4.1 | -1.32% | 25.1 | 25.8 | -0.88% | 35.6 | 36.9 | -1.11%
Enc Time[%] | 105% |  |  | 108% |  |  | 110% |  | 
Dec Time[%] | 95% |  |  | 98% |  |  | 96% |  | 
Table 3. Results with BDPCM enabled only for TS residual coding and TS is enabled for lossless.

## Slide 8
Proposal 1: BDPCM is enabled for both TS and TR residual coding.
Chroma BDPCM is enabled for TR coding (e.g. on top of CE-8.4.1 with TR coding).
Proposal #4
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | AHG18 LL | Proposal 4 |  | AHG18 LL | Proposal 4 |  | AHG18 LL | Proposal 4 | 
Class A1 | 2.2 | 2.3 | -1.69% | 2.3 | 2.3 | -0.72% |  |  | 
Class A2 | 1.7 | 1.8 | -1.64% | 1.9 | 1.9 | -0.31% |  |  | 
Class B | 2.1 | 2.1 | -1.98% | 2.3 | 2.3 | -0.39% | 2.3 | 2.3 | -0.40%
Class C | 2.1 | 2.1 | -2.22% | 2.6 | 2.6 | -0.50% | 2.6 | 2.6 | -0.50%
Class D | 1.9 | 2.0 | -3.81% | 2.8 | 2.8 | -0.74% | 2.7 | 2.8 | -0.64%
Class E | 2.9 | 3.0 | -3.66% |  |  |  | 3.3 | 3.4 | -1.15%
Class F | 5.5 | 5.9 | -5.37% | 39.4 | 41.8 | -3.53% | 60.7 | 64.9 | -3.71%
TGM | 12.3 | 13.2 | -6.63% | 112.6 | 117.0 | -3.68% | 142.4 | 147.3 | -3.30%
Overall (A1, A2, B, C, E) | 2.2 | 2.2 | -2.21% | 2.3 | 2.3 | -0.47% | 2.6 | 2.7 | -0.62%
Overall | 4.0 | 4.2 | -3.43% | 25.1 | 26.1 | -1.44% | 35.6 | 37.2 | -1.58%
Enc Time[%] | 115% |  |  | 112% |  |  | 114% |  | 
Dec Time[%] | 88% |  |  | 100% |  |  | 99% |  | 
Table 4. Results with BDPCM enabled both for TS and transform residual coding.
Additionally chroma BDPCM is enabled for TR residual coding.

## Slide 9
Results – Proposal #5 (CE-8.4.1 related)
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | AHG18 LL | Proposal 5 |  | AHG18 LL | Proposal 5 |  | AHG18 LL | Proposal 5 | 
Class A1 | 2.2 | 2.3 | -1.66% | 2.3 | 2.3 | -0.70% |  |  | 
Class A2 | 1.7 | 1.8 | -1.63% | 1.9 | 1.9 | -0.30% |  |  | 
Class B | 2.1 | 2.1 | -1.99% | 2.3 | 2.3 | -0.40% |  |  | 
Class C | 2.1 | 2.1 | -2.26% | 2.6 | 2.6 | -0.54% | 2.6 | 2.6 | -0.54%
Class D | 1.9 | 2.0 | -3.81% | 2.8 | 2.8 | -0.78% | 2.7 | 2.8 | -0.68%
Class E | 2.9 | 3.0 | -3.70% |  |  |  | 3.3 |  | 
Class F | 5.5 | 5.9 | -5.44% | 39.4 | 41.9 | -3.67% | 60.7 | 84.6 | 
TGM | 12.3 | 13.4 | -7.64% | 112.6 | 117.5 | -4.12% | 142.4 | 125.0 | 
Overall (A1, A2, B, C, E) | 2.2 | 2.2 | -2.22% | 2.3 | 2.3 | -0.48% | 2.6 | 0.9 | 
Overall | 4.0 | 4.3 | -3.58% | 25.1 | 26.2 | -1.53% | 35.6 | 21.9 | 
Enc Time[%] | 128% |  |  | 119% |  |  |  |  | 
Dec Time[%] | 88% |  |  | 100% |  |  |  |  | 
Table 5. Results with BDPCM enabled both for TS and transform residual coding.
Additionally chroma BDPCM is enabled for both TR and TS residual coding.
Proposal 1: BDPCM is enabled for both TS and TR residual coding.
( Chroma TS is enabled ) + Chroma BDPCM is enabled for TR and TS residual coding.

## Slide 10
Thanks to MediaTek and Sony
for crosschecking.
Conclusion
 |  | Bit Rate Savings |  | 
 |  | All Intra | Random Access | Low Delay B
Proposal #1 BDPCM is enabled for TR and TS | Class F | -3.80% | -2.75% | -3.16%
 | TGM | -3.54% | -2.67% | -2.61%
 | Overall (A1, A2, B, C, E) | -1.34% | -0.30% | -0.49%
Proposal #2 BDPCM is enabled for TR | Class F | -2.75% | -1.14% | -0.81%
 | TGM | -1.58% | -0.57% | -0.26%
 | Overall (A1, A2, B, C, E) | -1.28% | -0.26% | -0.47%
Proposal #3 BDPCM is enabled for TS | Class F | -3.15% | -2.52% | -3.01%
 | TGM | -3.16% | -2.54% | -2.57%
 | Overall (A1, A2, B, C, E) | -0.46% | -0.14% | -0.25%
Proposal #4 Proposal #1 + Chroma TR BDPCM. | Class F | -5.37% | -3.53% | -3.71%
 | TGM | -6.63% | -3.68% | -3.30%
 | Overall (A1, A2, B, C, E) | -2.21% | -0.47% | -0.62%
Proposal #5 Proposal #1 + Chroma TS + Chroma BDPCM | Class F | -5.44% | -3.67% | 
 | TGM | -7.64% | -4.12% | 
 | Overall (A1, A2, B, C, E) | -2.22% | -0.48% | 
We proposed to enable BDPCM for lossless.
We experimented with BDPCM performance with combinations of TS or transform residual (TR) coding.
We recommend adoption of BDPCM for lossless.

## Slide 11
 | All Intra |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | HM-16.20 RExt | AHG18 LL |  | HM-16.20 RExt | AHG18 LL | 
Class A1 | 2.2 | 2.2 | -0.75% | 2.3 | 2.3 | -0.83%
Class A2 | 1.8 | 1.7 | 2.41% | 1.9 | 1.9 | 1.44%
Class B | 2.1 | 2.1 | 0.71% | 2.3 | 2.3 | -1.21%
Class C | 2.1 | 2.1 | -0.13% | 2.6 | 2.6 | -1.62%
Class D | 2.0 | 1.9 | 1.95% | 2.7 | 2.8 | -1.25%
Class E | 3.0 | 2.9 | 0.62% |  |  | 
Class F | 5.2 | 5.5 | -5.07% | 35.5 | 39.4 | -4.80%
TGM | 8.2 | 12.3 | -29.76% | 106.3 | 112.6 | -10.17%
Overall | 2.2 | 2.2 | 0.55% | 2.3 | 2.3 | -0.71%
Enc Time[%] | 6022% |  |  | 1529% |  | 
Dec Time[%] | 205% |  |  | 167% |  | 
RExt vs. VTM-6.0 AHG18 Lossless
 | All Intra |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | HM-16.20 RExt | AHG18 LL + P#1 |  | HM-16.20 RExt | AHG18 LL + P#1 | 
Class A1 | 2.2 | 2.2 | -1.61% | 2.3 | 2.3 | -1.19%
Class A2 | 1.8 | 1.8 | 1.19% | 1.9 | 1.9 | 1.16%
Class B | 2.1 | 2.1 | -0.65% | 2.3 | 2.3 | -1.46%
Class C | 2.1 | 2.1 | -1.58% | 2.6 | 2.6 | -1.95%
Class D | 2.0 | 2.0 | -0.79% | 2.7 | 2.8 | -1.76%
Class E | 3.0 | 3.0 | -1.26% |  |  | 
Class F | 5.2 | 5.7 | -8.70% | 35.5 | 41.3 | -7.36%
TGM | 8.2 | 12.7 | -32.24% | 106.3 | 115.7 | -12.46%
Overall | 2.2 | 2.2 | -0.81% | 2.3 | 2.3 | -1.02%
Enc Time[%] | 6180% |  |  | 1463% |  | 
Dec Time[%] | 167% |  |  | 146% |  | 
RExt vs. Proposal #1
 | All Intra |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | HM-16.20 RExt | AHG18 LL + P#4 |  | HM-16.20 RExt | AHG18 LL + P#4 | 
Class A1 | 2.2 | 2.3 | -2.45% | 2.3 | 2.3 | -1.54%
Class A2 | 1.8 | 1.8 | 0.71% | 1.9 | 1.9 | 1.12%
Class B | 2.1 | 2.1 | -1.30% | 2.3 | 2.3 | -1.60%
Class C | 2.1 | 2.1 | -2.36% | 2.6 | 2.6 | -2.11%
Class D | 2.0 | 2.0 | -1.97% | 2.7 | 2.8 | -1.99%
Class E | 3.0 | 3.0 | -3.07% |  |  | 
Class F | 5.2 | 5.9 | -10.16% | 35.5 | 41.8 | -8.07%
TGM | 8.2 | 13.2 | -34.33% | 106.3 | 117.0 | -13.39%
Overall | 2.2 | 2.2 | -1.69% | 2.3 | 2.3 | -1.18%
Enc Time[%] | 6279% |  |  | 1484% |  | 
Dec Time[%] | 161% |  |  | 148% |  | 
RExt vs. Proposal #4