## Slide 1: AHG17/Non-CE5: on loop filter processing for subpicture treated as a picture (JVET-P0246)
Hyeonmun Jang, Junghak Nam, Seunghwan Kim, Jaehyun Lim

## Slide 2: Summary
Background and problem statement
  For subpicture boundary which is treated as picture boundary
  If the subpicture is extracted from bitstream and merging with other subpicture from different bitstream and allowed loop filter across subpicture.
  If loop filter is enabled,
    How to handle bottom/Right boundary of the subpicture which is treated as subpicture.
    How to do conformance test.
    How to prevent error propagation.
Proposed method
  Aspect 1: signal “loop_filter_across_subpic_enabled_flag[i]” depending on “subpic_treated_as_pic_flag[ i ]”
  Aspect 2: modifying pixels across subpicture that has subpic_treated_as_pic_flag is equal to 1 should be disallowed. ( for bottom / right subpicture boundary)

## Slide 3: Method 1
seq_parameter_set_rbsp( ) { | Descriptor
sps_decoding_parameter_set_id | u(4)
sps_video_parameter_set_id | u(4)
… | 
subpics_present_flag | u(1)
if( subpics_present_flag ) { | 
max_subpics_minus1 | u(8)
subpic_grid_col_width_minus1 | u(v)
subpic_grid_row_height_minus1 | u(v)
for( i = 0; i < NumSubPicGridRows; i++ ) | 
for( j = 0; j < NumSubPicGridCols; j++ ) | 
subpic_grid_idx[ i ][ j ] | u(v)
for( i = 0; i <= NumSubPics; i++ ) { | 
subpic_treated_as_pic_flag[ i ] | u(1)
if( !subpic_treated_as_pic_flag[ i ] ) | 
loop_filter_across_subpic_enabled_flag[ i ] | u(1)
} | 
} | 
… | 
} | 
To prevent mismatch on the subpicture boundary, loop filtering across subpicture boundary should be signaled depend on “subpic_treated_as_pic_flag”

## Slide 4: Method 2
Claimed problem case,

## Slide 5: Method 2
Below behavior is required for Luma and Chroma filtering,
When nDp is greater than 0 and one or more of the following conditions are true, nDp is set equal to 0:
cu_transquant_bypass_flag of the coding unit that includes the coding block containing the sample p0 is equal to 1.
pred_mode_plt_flag of the coding unit that includes the coding block containing the sample p0 is equal to 1.
Edges that coincide with the boundaries of the subpicture and subpic_treated_as_pic_flag [ SubPicIdx] of the coding unit that includes the coding block containing the sample p0 ] is equal to 1,
When nDq is greater than 0 and one or more of the following conditions are true, nDq is set equal to 0:
cu_transquant_bypass_flag of the coding unit that includes the coding block containing the sample q0 is equal to 1.
pred_mode_plt_flag of the coding unit that includes the coding block containing the sample q0 is equal to 1.
Edges that coincide with the boundaries of the subpicture and subpic_treated_as_pic_flag [ SubPicIdx] of the coding unit that includes the coding block containing the sample q0 ] is equal to 1,

## Slide 6: Conclusion
It is recommended to adopt at next VTM