## Slide 1
Non-CE4: Coding of interpolation filter index in non-merge inter
JVET-P0341
P. Bordes, F. Galpin, F. Le-Léannec, E. François

## Slide 2: Problems JVET_P0341
Switchable interpolation-filter index is inferred from AMVR
  This reduces the flexibility in selecting hpelIfIdx
  It may happens the reconstructed mv is FULL_PEL then AIF is not used actually
  …but still propagated for further merge
  hpelIfIdx = (amvr == HALF_PEL) ? 1 : 0

## Slide 3: Proposal: coding of hpelIfIdx JVET_P0341
Encode the adaptive interpolation filter (AIF) index (hpelIfIdx) in case of amvr_precision_idx is equal to HALF_PEL
Provides encoder/spec flexibility to select optimal filter:
If coded value is always 1 (no RDO) the complexity is unchanged compared to VTM-6.0
If RDO is enabled for selecting hpelIfIdx, the BD-rate gains are improved compared to VTM-6.0

## Slide 4: Results: AIF index coding JVET_P0341
No RDO
With RDO

## Slide 5: Results: combination P0341+ P0340 + P0621
P0341: Coding AIF index if amvr is equal to HALF_PEL
P0340: Enabling AIF for triangle-merge
P0340: Derivation of AIF index in pairwise-average
  hpelIfIdx = max ( hpelIfIdx-0 , hpelIfIdx-1 )
P0621: use AIF index for motion comparison

## Slide 6: Results: combination P0341+ P0340 + P0621
With RDO
Thanks to Sharp for cross-checking