## Slide 1
JVET-P0353
CE1-related: Reference picture resampling filters
2019/10/4

## Slide 2
Proposed down-sample filter
is the cut-off frequency, r is the down-sampling ratio
Follow SHM down-sampling filter design: cosine windowed sinc filter

## Slide 3
Proposed down-sample filter
No change to filter length and precision form MCIF in VVC
For MC with reference picture larger than current picture:
Replace 8-tap MCIF with 8-tap proposed filter
Replace 6-tap MCIF with 6-tap proposed filter
- Supplemental test for excluding 6-tap is running
Replace 4-tap MCIF with 4-tap proposed filter
Select from 2 sets of filters depending on resampling ratio
if ratio > 1.75
use 2x proposed filter
else if 1.25 < ratio <= 1.75
use 1.5x proposed filters
else
use existing MCIF
The use of hpel-If is not changed from existing VVC
- Supplemental test for replacing hpel-If is running

## Slide 4
Proposed down-sample filter frequency response
Frequency response of 2x filter at phase 0

## Slide 5
Simulation results
2x | Low delay Main 10 PSNR1 |  |  |  |  | Low delay B Main10 PSNR2 |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CE1 Lanczos2 | -4.45% | -2.70% | -2,47% | 100% | 100% | -2.89% | -1.79% | -1.72% | 100% | 100%
CE1 SHM2x | -6.47% | -4.55% | -4.62% | 99% | 102% | -3.98% | -2.67% | -3.00% | 99% | 102%
P0353 2x | -5.96% | -3.31% | -2.99% | 99% | 101% | -3.80% | -2.31% | -2.19% | 99% | 101%
P0390 | -5.28% | -2.38% | -2.58% | 98% | 105% | -2.93% | -1.35% | -1.72% | 98% | 105%
1.5x | Low delay Main 10 PSNR1 |  |  |  |  | Low delay B Main10 PSNR2 |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CE1 Lanczos2.67 | -2.23% | -1.23% | -1.06% | 100% | 102% | -1.85% | -1.68% | -1.34% | 100% | 102%
CE1 SHM1.5x | -3.13% | -2.50% | -2.28% | 99% | 101% | -2.23% | -2.21% | -1.87% | 99% | 101%
P0353 1.5x | -2.44% | -1.29% | -1.09% | 99% | 99% | -1.78% | -1.92% | -1.60% | 99% | 99%

## Slide 6
Simulation results
2x | CE1-1.1 |  |  | Proposed 2x |  | 
 | Over CE1 anchor |  |  |  |  | 
 | Y | U | V | Y | U | V
Class A1 | - | - | - | - | - | -
Class A2 | - | - | - | - | - | -
Class B | -2,37% | -1,49% | -1,64% | -3.16% | -1.73% | -1.67%
Class C | -5,63% | -4,02% | -3,76% | -6.65% | -4.37% | -4.10%
Class E | -6,34% | -2,96% | -2,12% | -9.71% | -4.54% | -3.71%
Overall | -4,45% | -2,70% | -2,47% | -5.96% | -3.31% | -2.99%
Class D | - | - | - | - | - | -
Class F | - | - | - | - | - | -
PSNR1
1.5x | CE1-1.3 |  |  | Proposed 1.5x |  | 
 | Over CE1 anchor |  |  |  |  | 
 | Y | U | V | Y | U | V
Class A1 | - | - | - | - | - | -
Class A2 | - | - | - | - | - | -
Class B | -1,02% | -0,46% | -0,75% | -1.12% | -0.62% | -0.69%
Class C | -3,28% | -2,06% | -2,05% | -3.65% | -2.30% | -1.94%
Class E | -2,82% | -1,40% | -0,26% | -3.04% | -1.06% | -0.63%
Overall | -2,23% | -1,23% | -1,06% | -2.44% | -1.29% | -1.09%
Class D | - | - | - | - | - | -
Class F | - | - | - | - | - | -

## Slide 7
Simulation results
2x | CE1-1.1 |  |  | Proposed 2x |  | 
 | Over CE1 anchor |  |  |  |  | 
 | Y | U | V | Y | U | V
Class A1 | - | - | - | - | - | -
Class A2 | - | - | - | - | - | -
Class B | -1,55% | -1,05% | -1,14% | -2.16% | -1.24% | -1.22%
Class C | -3,50% | -2,32% | -2,26% | -4.07% | -2.53% | -2.46%
Class E | -4,30% | -2,31% | -1,96% | -6.19% | -3.80% | -3.45%
Overall | -2,89% | -1,79% | -1,72% | -3.80% | -2.31% | -2.19%
Class D | - | - | - | - | - | -
Class F | - | - | - | - | - | -
PSNR2
1.5x | CE1-1.3 |  |  | Proposed 1.5x |  | 
 | Over CE1 anchor |  |  |  |  | 
 | Y | U | V | Y | U | V
Class A1 | - | - | - | - | - | -
Class A2 | - | - | - | - | - | -
Class B | -0,77% | -0,59% | -0,92% | -0.80% | -0.86% | -1.03%
Class C | -2,57% | -2,06% | -1,97% | -2.68% | -2.24% | -1.95%
Class E | -2,67% | -2,98% | -1,21% | -2.23% | -3.26% | -2.08%
Overall | -1,85% | -1,68% | -1,34% | -1.78% | -1.92% | -1.60%
Class D | - | - | - | - | - | -
Class F | - | - | - | - | - | -

## Slide 8
Proposed filter for 2x
Fractional sample position p | interpolation filter coefficients |  |  |  |  |  |  | 
 | fL[ p ][ 0 ] | fL[ p ][ 1 ] | fL[ p ][ 2 ] | fL[ p ][ 3 ] | fL[ p ][ 4 ] | fL[ p ][ 5 ] | fL[ p ][ 6 ] | fL[ p ][ 7 ]
0 | -4 | 2 | 20 | 28 | 20 | 2 | -4 | 0
1 | -4 | 0 | 19 | 29 | 21 | 5 | -4 | -2
2 | -4 | -1 | 18 | 29 | 22 | 6 | -4 | -2
3 | -4 | -1 | 16 | 29 | 23 | 7 | -4 | -2
4 | -4 | -1 | 16 | 28 | 24 | 7 | -4 | -2
5 | -4 | -1 | 14 | 28 | 25 | 8 | -4 | -2
6 | -3 | -3 | 14 | 27 | 26 | 9 | -3 | -3
7 | -3 | -1 | 12 | 28 | 25 | 10 | -4 | -3
8 | -3 | -3 | 11 | 27 | 27 | 11 | -3 | -3
Filter length = 8-taps
Fractional sample position p | interpolation filter coefficients |  |  |  |  |  |  | 
 | fL[ p ][ 0 ] | fL[ p ][ 1 ] | fL[ p ][ 2 ] | fL[ p ][ 3 ] | fL[ p ][ 4 ] | fL[ p ][ 5 ] | fL[ p ][ 6 ] | fL[ p ][ 7 ]
0 | 0 | 0 | 19 | 26 | 19 | 0 | 0 | 0
1 | 0 | -1 | 18 | 27 | 20 | 2 | -2 | 0
2 | 0 | -1 | 16 | 27 | 21 | 3 | -2 | 0
3 | 0 | -2 | 15 | 27 | 22 | 5 | -3 | 0
4 | 0 | -2 | 14 | 26 | 23 | 6 | -3 | 0
5 | 0 | -2 | 13 | 26 | 24 | 6 | -3 | 0
6 | 0 | -3 | 12 | 25 | 25 | 8 | -3 | 0
7 | 0 | -3 | 11 | 25 | 25 | 9 | -3 | 0
8 | 0 | -3 | 10 | 25 | 25 | 10 | -3 | 0
Fractional sample position p | interpolation filter coefficients |  |  | 
 | fC[ p ][ 0 ] | fC[ p ][ 1 ] | fC[ p ][ 2 ] | fC[ p ][ 3 ]
0 | 17 | 30 | 17 | 0
1 | 17 | 30 | 18 | -1
2 | 16 | 30 | 18 | 0
3 | 16 | 30 | 18 | 0
4 | 15 | 30 | 18 | 1
5 | 14 | 30 | 18 | 2
6 | 13 | 29 | 19 | 3
7 | 13 | 29 | 19 | 3
8 | 12 | 29 | 20 | 3
9 | 11 | 28 | 21 | 4
10 | 10 | 28 | 22 | 4
11 | 10 | 27 | 22 | 5
12 | 9 | 27 | 23 | 5
13 | 9 | 26 | 24 | 5
14 | 8 | 26 | 24 | 6
15 | 7 | 26 | 25 | 6
16 | 7 | 25 | 25 | 7
Filter length = 6-taps
Filter length = 4-taps

## Slide 9
Proposed filter for 1.5x
Fractional sample position p | interpolation filter coefficients |  |  |  |  |  |  | 
 | fL[ p ][ 0 ] | fL[ p ][ 1 ] | fL[ p ][ 2 ] | fL[ p ][ 3 ] | fL[ p ][ 4 ] | fL[ p ][ 5 ] | fL[ p ][ 6 ] | fL[ p ][ 7 ]
0 | -1 | -6 | 20 | 38 | 20 | -6 | -1 | 0
1 | 1 | -7 | 18 | 37 | 22 | -5 | -4 | 2
2 | 1 | -7 | 16 | 37 | 23 | -4 | -4 | 2
3 | 1 | -7 | 14 | 36 | 26 | -3 | -5 | 2
4 | 1 | -7 | 12 | 36 | 27 | -2 | -5 | 2
5 | 2 | -7 | 11 | 35 | 28 | -1 | -6 | 2
6 | 2 | -7 | 9 | 34 | 30 | 0 | -6 | 2
7 | 2 | -7 | 7 | 33 | 31 | 2 | -6 | 2
8 | 2 | -7 | 5 | 32 | 32 | 5 | -7 | 2
Fractional sample position p | interpolation filter coefficients |  |  |  |  |  |  | 
 | fL[ p ][ 0 ] | fL[ p ][ 1 ] | fL[ p ][ 2 ] | fL[ p ][ 3 ] | fL[ p ][ 4 ] | fL[ p ][ 5 ] | fL[ p ][ 6 ] | fL[ p ][ 7 ]
0 | 0 | -5 | 18 | 38 | 18 | -5 | 0 | 0
1 | 0 | -5 | 16 | 39 | 20 | -4 | -2 | 0
2 | 0 | -5 | 14 | 39 | 22 | -4 | -2 | 0
3 | 0 | -5 | 13 | 38 | 24 | -3 | -3 | 0
4 | 0 | -5 | 11 | 37 | 26 | -2 | -3 | 0
5 | 0 | -5 | 9 | 36 | 28 | -1 | -3 | 0
6 | 0 | -5 | 8 | 35 | 30 | -1 | -3 | 0
7 | 0 | -4 | 6 | 34 | 31 | 1 | -4 | 0
8 | 0 | -4 | 3 | 33 | 33 | 3 | -4 | 0
Fractional sample position p | interpolation filter coefficients |  |  | 
 | fC[ p ][ 0 ] | fC[ p ][ 1 ] | fC[ p ][ 2 ] | fC[ p ][ 3 ]
0 | 13 | 38 | 13 | 0
1 | 13 | 38 | 14 | -1
2 | 12 | 38 | 15 | -1
3 | 11 | 37 | 17 | -1
4 | 10 | 38 | 18 | -2
5 | 9 | 38 | 19 | -2
6 | 8 | 38 | 20 | -2
7 | 7 | 38 | 21 | -2
8 | 6 | 37 | 22 | -1
9 | 6 | 36 | 24 | -2
10 | 5 | 36 | 25 | -2
11 | 4 | 35 | 26 | -1
12 | 4 | 34 | 27 | -1
13 | 3 | 34 | 28 | -1
14 | 3 | 33 | 29 | -1
15 | 2 | 32 | 30 | 0
16 | 1 | 31 | 31 | 1
Filter length = 8-taps
Filter length = 6-taps
Filter length = 6-taps