## Slide 1
JVET-P0369
MPM flag signaling with MRL

## Slide 2: Intra prediction with MRL in VTM 6.0
planar, mpm1, mpm2, mpm3, mpm4, mpm5
Possible 5 intra modes with
Ref line #1 and #3
6 MPM modes:
61 non-MPM modes:
non-mpm1, non-mpm2, …., non-mpm61
67 intra modes with Ref line #0
No ISP with Ref line #1 and #3
Notes: Background: intra prediction

## Slide 3
Intra mode coding in VTM6
Ref Line
#0
#1 or #3
Encode
ispMode
Encode
mpmFlag
Encode
mpm mode
Encode
non-mpm mode
0
1
mpmFlag context encoded
By CABAC
(truncated binary)
Candidate Index | code
planar | 0 (only if Ref Line #0)
mpm1 | 1 0
mpm2 | 1 10
mpm3 | 1 110
mpm4 | 1 1110
mpm5 | 1 1111
1st bin context coded for planar
(or inferred to 1 if Ref Line != #0)
other 4 bins bypass coded
Notes: Intra mode coding in VTM6

## Slide 4
Intra mode coding in VTM6
Ref Line
#0
#1 or #3
Encode
ispMode
Encode
mpmFlag
Encode
mpm mode
Encode
non-mpm mode
Candidate Index | code
planar | 0 (only if Ref Line #0)
mpm1 | 1 0
mpm2 | 1 10
mpm3 | 1 110
mpm4 | 1 1110
mpm5 | 1 1111
1st bin context coded for planar
(or inferred to 1 if Ref Line != #0)
other 4 bins bypass coded
0
1
mpmFlag context encoded
By CABAC
(truncated binary)
Ref Line #1 or #3 incompatible with non-mpm mode
But no restrictions on mpm directions for Ref Line #1 or #3
Notes: Restriction are not justified at the decoder side (historically the goal is to limit the simulation time)

## Slide 5
Proposed mpmFlag signaling
Ref Line
#0
#1 or #3
Encode
ispMode
Encode
mpmFlag
0
mpmFlag context encoded
By CABAC
(truncated binary)
Encode
non-mpm mode
Encode
mpm mode
1
Candidate Index | code
planar | 0 (only if Ref Line #0)
mpm1 | 1 0
mpm2 | 1 10
mpm3 | 1 110
mpm4 | 1 1110
mpm5 | 1 1111
1st bin context coded for planar
(or inferred to 1 if Ref Line != #0)
other 4 bins bypass coded
Notes: We propose to offer more flexibility at no coding cost

## Slide 6
Simulation Results
Thank you!