## Slide 1
JVET-P0373
CE7-related: Decouple level mapping from transform skip residual coding
2019/10/3

## Slide 2
Introduction
In VVC6, transform-skip residual levels ( only non-zero levels) are mapped before residual coding.
Predict a value from top and left neighbors
Predicted value is mapped to 1.
Level mapping is not applied for BDPCM mode

## Slide 3
Problem statement
Rice parameter derivation process depends on the actual level, computation of actual level (which requires inverse mapping) need to be implemented within the CABAC parsing loop.
Such interleaved manner of parsing and level decoding may be undesirable as it reduces the throughput for decoder hardware implementation.
VVC 6

## Slide 4
Proposed method
Derive Rice parameter based on mapped value
Process level mapping outside of the parsing loop
Unified process flow of transform skip and BDPCM mode
VVC 6
Proposed

## Slide 5
Simulation results
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.01% | -0.02% | 101% | 101%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 101%
Class B | 0.00% | -0.01% | -0.01% | 101% | 102%
Class C | 0.00% | 0.01% | 0.01% | 100% | 104%
Class E | 0.00% | 0.00% | 0.00% | 101% | 103%
Overall | 0.00% | 0.00% | 0.00% | 101% | 102%
Class D | 0.00% | -0.01% | 0.00% | 99% | 106%
Class F | 0.00% | -0.02% | -0.01% | 100% | 101%
Class SCC | 0.01% | -0.01% | 0.00% | 101% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class B | 0.00% | 0.02% | 0.00% | 101% | 101%
Class C | 0.01% | 0.01% | -0.02% | 101% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.01% | 0.00% | 100% | 100%
Class D | -0.01% | -0.08% | 0.10% | 101% | 100%
Class F | 0.00% | 0.06% | -0.01% | 101% | 103%
Class SCC | 0.05% | -0.02% | -0.02% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.15% | -0.02% | 100% | 100%
Class C | -0.01% | 0.01% | -0.02% | 101% | 104%
Class E | -0.01% | -0.01% | 0.01% | 101% | 102%
Overall | 0.00% | 0.06% | -0.01% | 101% | 102%
Class D | 0.04% | 0.14% | 0.00% | 101% | 106%
Class F | 0.14% | 0.16% | 0.71% | 100% | 100%
Class SCC | 0.01% | 0.02% | -0.04% | 101% | 105%
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 98%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 98%
Class B | 0.00% | 0.00% | 0.00% | 100% | 98%
Class C | 0.00% | 0.01% | 0.00% | 98% | 100%
Class E | 0.00% | -0.01% | 0.01% | 100% | 99%
Overall | 0.00% | 0.00% | 0.00% | 100% | 99%
Class D | 0.00% | 0.01% | 0.00% | 101% | 102%
Class F | 0.03% | 0.03% | 0.00% | 100% | 100%
Class SCC | 0.12% | 0.08% | 0.08% | 100% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 99%
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.01% | 0.00% | 100% | 100%
Class C | 0.00% | -0.03% | 0.04% | 100% | 101%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0.00% | -0.02% | 0.00% | 100% | 101%
Class F | -0.07% | -0.18% | -0.18% | 101% | 100%
Class SCC | 0.19% | 0.13% | 0.13% | 102% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | -0.01% | 101% | 98%
Class C | -0.01% | 0.00% | -0.01% | 101% | 100%
Class E | 0.00% | 0.01% | 0.04% | 100% | 98%
Overall | -0.01% | 0.00% | 0.00% | 101% | 98%
Class D | -0.03% | 0.04% | 0.02% | 100% | 100%
Class F | -0.02% | 0.00% | 0.06% | 101% | 100%
Class SCC | 0.19% | 0.17% | 0.18% | 101% | 98%
CTC QP
Low QP

## Slide 6
Conclusion
It is reported that the BD-rate impact of the proposed method is 0.00% (AI), 0.05% (RA), 0.01% (LB) for the TGM sequences under CTC test conditions, which is negligible.
Completely decouple level mapping from residual parsing process
Unify the processing flow between BDPCM mode and transform skip mode

## Slide 7
Additional results
Anchor : VTM-6.0
Test : Proposed + max ctx bins 1.75 bin/coeff
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.10% | 0.13% | 0.19% | 102% | 98%
Class SCC | 0.27% | 0.22% | 0.24% | 102% | 97%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F |  |  |  |  | 
Class SCC | 0.23% | 0.14% | 0.11% | 101% | 88%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.11% | 0.01% | 0.39% | 102% | 89%
Class SCC | 0.05% | 0.09% | 0.12% | 102% | 90%
CTC QP
low QP