## Slide 1: AHG8/AHG17: On the role of nuh_layer_id in the layer design
E. Thomas (TNO), M. Hannuksela (Nokia), L. Chen (MediaTek), Y. He (InterDigital), S. Wenger, B. Choi (Tencent)

## Slide 2: Motivations
Layer design in VVC draft v6 for independent layers
Issues around the nuh_layer_id handling
  nuh_layer_id of the VPS
  Bug in sub-bitstream extraction process
  Ordering by increasing value of nuh_layer_id in access unit

## Slide 3: Layer design in VVC draft v6
The cardinality of a concept (rectangle) is indicated by a symbol at the bottom right corner of the rectangle with the convention of :
  '1': single occurrence
  '+': one ore more occurrences
Figure 1 - Conceptual model of VVC bitstream concept

## Slide 4: Layer design in VVC draft v6
Figure 2 - Bitstream arrangement of CVS and CLVS

## Slide 5: Draft v6: nuh_layer_id of the VPS must be the one of the lowest layer id
Problem
This makes the sub-bitstream extraction more complex by requiring rewriting the NAL unit header of the VPS when:
inserting a new layer with a lower layer id
removing the layer containing the VPS

## Slide 6: Draft v6: bug in the sub-picture extraction process
Problem
If the layer id of the current VPS is not in lIdTargetList, the VPS is absent from the output sub-bitstream.

## Slide 7: Draft v6: ordering by increasing value of nuh_layer_id in access unit
Problem
Since the concept of independent layers in the VVC draft does not express any hierarchy between the layers, it seems odd to require a specific ordering of the layer access units in the access unit.
This complexifies the merging operation function which cannot simply be appending layer access units to the last one in each access unit, but one must care of where to put them.

## Slide 8: Summaries of issues around nuh_layer_id
VVC draft v6 defines:
  nuh_layer_id of the VPS must be the one of the lowest layer id
  the sub-bitstream extraction process allows the dropping of VPS from the input bitstream
  The layer access unit are ordered by increased value of nuh_layer_id while independent layers have no hierarchy by nature

## Slide 9: Proposal to solve problems 1 and 2
Problems
  nuh_layer_id of the VPS must be the one of the lowest layer id
  the sub-bitstream extraction process allows dropping VPS from the input bitstream
Proposal
Define a special value for nul_layer_id equal to '0'. Every NAL units having the value '0’ of nul_layer_id shall:
  be invariant to layer operation, i.e. sub-bitstream extraction of layers.
  only contain non-VCL NAL units that apply to all the layers, e.g. VPS, EOS, EOB, SEI messages when related to all the layers, etc…

## Slide 10: Proposal to solve problem 3
Problem
  The layer access unit are ordered by increased value of nuh_layer_id while independent layers have no hierarchy by nature
Proposal
Since the ordering of independent layers is not motivated, it is proposed to remove the ordering and to keep it for dependent layers.

## Slide 11: Conclusion
Proposed to solve issues with
  nuh_layer_id of the VPS must be the one of the lowest layer id
  the sub-bitstream extraction process allows the dropping of VPS from the input bitstream
  The layer access unit are ordered by increased value of nuh_layer_id while independent layers have no hierarchy by nature
Proposals
  Every NAL unit having the value '0' for nul_layer_id shall:
    be invariant to layer operation, i.e. layer extraction/merging.
    only contain non-VCL NAL units that apply to all the layers, e.g. VPS, EOS, EOB, SEI messages when related to all the layers, etc…
  Removing independent layers ordering by increasing value of nuh_layer_id in access unit