## Slide 1
JVET-P0391
Non-CE6: A clean-up of SPS maximum SBT size signaling
2019/10/3

## Slide 2
Problem statement
The SPS syntax sps_sbt_max_size_64_flag specifies the maximum CU width and height for allowing SBT.
The variable MaxSbtSize
  MaxSbtSize = Min( MaxTbSizeY, sps_sbt_max_size_64_flag ? 64 : 32 )
  If MaxTbSizeY = 32, MaxSbtSize is 32 regardless the value of sps_sbt_max_size_64_flag

## Slide 3
Proposed Method 1: conditionally signal maximum SBT size
seq_parameter_set_rbsp( ) { | Descriptor
sps_max_luma_transform_size_64_flag | u(1)
. | 
. | 
sps_sbt_enabled_flag | u(1)
if( sps_sbt_enabled_flag && sps_max_luma_transform_size_64_flag ) | 
sps_sbt_max_size_64_flag | u(1)

## Slide 4
Proposed Method 2: Remove maximum SBT size signaling
Allow maximum SBT size to maximum transform size
If sps_max_luma_transform_size_64_flag is equal to 1, max SBT size = 64, otherwise, max SBT size is 32.
seq_parameter_set_rbsp( ) { | Descriptor
sps_max_luma_transform_size_64_flag | u(1)
. | 
. | 
sps_sbt_enabled_flag | u(1)
if( sps_sbt_enabled_flag ) | 
sps_sbt_max_size_64_flag | u(1)