## Slide 1: CABAC zero word thresholds
JVET-P0395
Advanced Technology Team
European Professional Engineering
Sony Europe BV.
Adrian Browne / Steve Keating / Karl Sharman
Sony Corp.

## Slide 2: Introduction
The bit stream is defined in terms of a bit rate (bits/second)
CABAC zero words limit the bit / bin ratio by adding padding bits
  Effectively defines the bin/second rate
  Limit is important aspect in hardware design
From the specification, the formula for the number of bins is given as:
n = ( 32 ÷ 3 ) * NumBytesInVclNalUnits + ( RawMinCuBits * PicSizeInMinCbsY )  32
or n = ( 32 ÷ 3 ÷ 8 ) * NumBitsInVclNalUnits + ( RawMinCuBits * PicSizeInMinCbsY )  32
For the purposes of this presentation we are rewriting this as:
n = β * b + c ÷ α
    n is the number of bins allowed in the stream
    b is the number of bits in the stream
    c is the number of bits in the image or image region
    α and β are two constants with default values of 32 and 4 ÷ 3 respectively

## Slide 3: Introduction
In Gothenburg there was support for JVET-O0517 which suggested:
“The limit is made for each slice/independently decodable region
to allow splicing and to simplify parallel decoding”
  Asked to investigate thresholds of CABAC zero word equation
    These are carried over from HEVC, unchanged since AVC

## Slide 4: Study
Studied the following configurations:
  VTM 6.1
  HM 16.20 as reference
  VTM 6.1 without trellis / dependent quantization
    Previously highlighted as having a significant impact on bin / bit ratio
  VTM 6.1 without bin limits for coefficient coding
    To understand effect of these limits on bin / bit ratio and CABAC zero words
      JVET-N0280 and JVET-O0052
  VTM 6.1 without trellis / dependent quantization and without bin limits
Produced results for CTC and low QP for each configuration
  AI, RA, LDB

## Slide 5: Results
 |  |  | AI |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 3.33% | 0.29% | 0.43% | 98% | 104%
Class A2 | 4.36% | -0.24% | -0.27% | 94% | 104%
Class B | 2.54% | 0.11% | -0.02% | 93% | 103%
Class C | 2.00% | 1.17% | 0.92% | 88% | 104%
Class E | 1.84% | 0.59% | 0.35% | 93% | 100%
Overall | 2.74% | 0.40% | 0.29% | 93% | 103%
Class D | 2.04% | 1.10% | 0.77% | 87% | 103%
Class F | 1.13% | 0.62% | 0.63% | 93% | 102%
Class TGM | 0.78% | 0.19% | 0.31% | 89% | 100%
 |  |  | RA |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 2.61% | 0.76% | -0.27% | 102% | 102%
Class A2 | 2.50% | 0.50% | 0.50% | 99% | 102%
Class B | 2.52% | 0.08% | -0.04% | 99% | 102%
Class C | 1.81% | 1.48% | 1.13% | 96% | 101%
Class E |  |  |  |  | 
Overall | 2.34% | 0.67% | 0.34% | 99% | 102%
Class D | 1.80% | 1.12% | 1.33% | 96% | 101%
Class F | 1.03% | 1.42% | 1.53% | 97% | 101%
Class TGM | 0.34% | 1.07% | 1.05% | 92% | 101%
 |  |  | AI (low QP) |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 1.33% | 3.72% | 3.69% | 80% | 109%
Class A2 | 2.88% | 4.83% | 4.90% | 78% | 109%
Class B | 2.78% | 4.12% | 4.21% | 83% | 109%
Class C | 1.88% | 4.34% | 4.28% | 77% | 104%
Class E | 2.94% | 4.77% | 4.81% | 82% | 110%
Overall | 2.38% | 4.33% | 4.35% | 80% | 108%
Class D | 1.84% | 3.92% | 3.88% | 80% | 104%
Class F | 1.41% | 3.15% | 3.01% | 84% | 98%
Class TGM | 0.91% | 1.92% | 2.02% | 88% | 99%
 |  |  | RA (low QP) |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 3.37% | 4.83% | 4.07% | 81% | 115%
Class A2 | 3.99% | 5.59% | 5.68% | 81% | 109%
Class B | 3.72% | 5.21% | 4.49% | 85% | 105%
Class C | 4.18% | 6.68% | 5.48% | 83% | 102%
Class E |  |  |  |  | 
Overall | 3.83% | 5.60% | 4.91% | 83% | 107%
Class D | 3.60% | 6.57% | 5.78% | 84% | 99%
Class F | 1.39% | 4.56% | 4.12% | 88% | 100%
Class TGM | 0.31% | 3.81% | 4.13% | 87% | 99%
VTM 6.1 without dependent quantization versus VTM 6.1

## Slide 6: Results
 |  |  | AI |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.02% | -0.01% | 102% | 102%
Class A2 | 0.00% | -0.01% | 0.03% | 98% | 98%
Class B | 0.01% | 0.03% | -0.02% | 100% | 100%
Class C | -0.05% | -0.20% | -0.09% | 100% | 102%
Class E | 0.01% | 0.05% | 0.04% | 99% | 98%
Overall | -0.01% | -0.03% | -0.02% | 100% | 100%
Class D | -0.04% | -0.08% | -0.24% | 101% | 101%
Class F | -0.18% | -0.34% | -0.23% | 99% | 99%
Class TGM | -0.43% | -0.41% | -0.38% | 100% | 99%
 |  |  | RA |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.06% | 0.07% | 100% | 100%
Class A2 | 0.03% | 0.11% | -0.02% | 101% | 101%
Class B | -0.01% | 0.19% | 0.09% | 100% | 100%
Class C | -0.02% | 0.03% | -0.04% | 99% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.10% | 0.03% | 100% | 100%
Class D | -0.05% | -0.41% | -0.14% | 100% | 100%
Class F | -0.21% | -0.35% | -0.14% | 100% | 101%
Class TGM | -0.38% | -0.33% | -0.35% | 101% | 101%
 |  |  | AI (low QP) |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.40% | -0.47% | -0.49% | 100% | 103%
Class A2 | -0.34% | -0.53% | -0.54% | 100% | 103%
Class B | -0.06% | -0.07% | -0.11% | 102% | 105%
Class C | -0.03% | -0.10% | -0.09% | 102% | 106%
Class E | -0.10% | -0.26% | -0.21% | 100% | 103%
Overall | -0.16% | -0.25% | -0.26% | 101% | 104%
Class D | -0.04% | -0.13% | -0.11% | 103% | 105%
Class F | -1.69% | -0.83% | -0.85% | 100% | 101%
Class TGM | -2.24% | -1.83% | -1.81% | 102% | 102%
 |  |  | RA (low QP) |  | 
 |  |  | Over VTM6.1 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.36% | -0.40% | -0.46% | 100% | 102%
Class A2 | -0.57% | -0.85% | -0.85% | 101% | 103%
Class B | -0.29% | -0.34% | -0.40% | 101% | 102%
Class C | -0.20% | -0.36% | -0.41% | 101% | 103%
Class E |  |  |  |  | 
Overall | -0.33% | -0.46% | -0.50% | 101% | 102%
Class D | -0.23% | -0.43% | -0.40% | 101% | 103%
Class F | -2.46% | -0.86% | -0.74% | 101% | 101%
Class TGM | -2.49% | -1.65% | -1.66% | 102% | 100%
VTM 6.1 without coefficient coding bin limits versus VTM 6.1

## Slide 7: Results
 |  |  | AI |  | 
 |  |  | Over VTM6.1 NoDepQuant |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.01% | 0.02% | 101% | 101%
Class A2 | 0.00% | 0.01% | 0.01% | 101% | 101%
Class B | 0.01% | -0.01% | 0.00% | 101% | 102%
Class C | -0.07% | -0.08% | 0.08% | 101% | 100%
Class E | 0.00% | -0.13% | -0.01% | 100% | 100%
Overall | -0.01% | -0.04% | 0.02% | 101% | 101%
Class D | -0.06% | -0.13% | 0.02% | 100% | 99%
Class F | -0.23% | -0.06% | -0.17% | 99% | 99%
Class TGM | -0.45% | -0.38% | -0.41% | 100% | 100%
 |  |  | RA |  | 
 |  |  | Over VTM6.1 NoDepQuant |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.01% | -0.04% | 99% | 99%
Class A2 | -0.01% | 0.05% | -0.07% | 99% | 99%
Class B | 0.00% | 0.04% | 0.07% | 100% | 100%
Class C | -0.04% | 0.16% | 0.07% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.01% | 0.06% | 0.02% | 100% | 100%
Class D | 0.01% | -0.03% | -0.46% | 99% | 100%
Class F | -0.19% | -0.23% | -0.15% | 100% | 99%
Class TGM | -0.31% | -0.25% | -0.22% | 100% | 100%
 |  |  | AI (low QP) |  | 
 |  |  | Over VTM6.1 NoDepQuant |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.37% | -0.42% | -0.41% | 102% | 103%
Class A2 | -0.32% | -0.35% | -0.35% | 103% | 105%
Class B | -0.15% | -0.09% | -0.10% | 101% | 104%
Class C | -0.17% | -0.20% | -0.22% | 102% | 105%
Class E | -0.17% | -0.16% | -0.23% | 100% | 101%
Overall | -0.22% | -0.23% | -0.24% | 101% | 104%
Class D | -0.20% | -0.25% | -0.24% | 100% | 103%
Class F | -1.77% | -0.94% | -1.01% | 104% | 106%
Class TGM | -2.28% | -1.98% | -2.00% | 101% | 102%
 |  |  | RA (low QP) |  | 
 |  |  | Over VTM6.1 NoDepQuant |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.28% | -0.29% | -0.30% | 101% | 101%
Class A2 | -0.36% | -0.44% | -0.45% | 102% | 102%
Class B | -0.21% | -0.19% | -0.21% | 101% | 103%
Class C | -0.18% | -0.21% | -0.25% | 101% | 102%
Class E |  |  |  |  | 
Overall | -0.24% | -0.27% | -0.29% | 101% | 102%
Class D | -0.16% | -0.33% | -0.21% | 101% | 103%
Class F | -2.23% | -0.77% | -0.80% | 101% | 101%
Class TGM | -2.52% | -1.74% | -1.77% | 103% | 101%
VTM 6.1 without coefficient limits versus VTM 6.1 (both without dependent quantization)

## Slide 8: Method
Initially studied frame-based results
Then studied CTU-based results
  Number of square CTUs > 100 * number of frames
    More than 13 million CTUs examined for VTM
    Diversity of data points analysed increased
  Areas in pictures with different bin / bit characteristics can be analysed
  Classes can be compared as each data point is the same size
  It is not safe to rely on the averaging effect over a large image
    Likely that the initial tuning of CABAC increases the bin-to-bit ratio
      As observed, bin-to-bit ratio issues are more prevalent in larger formats
  Results on a per CTU basis can be scaled up to pictures
    Picture and CTU trends are closely aligned
    A constraint which is suitable for all CTUs in an image must also be applicable to the picture made up of these CTUs

## Slide 9: Frame-based results
QPs under test | Percent of frames over cabac_zero_word_threshold |  |  |  | 
 | VTM 6.1 | HM 16.20 | VTM 6.1 without dependent quantization | VTM 6.1 without coefficient bin limits | VTM 6.1 without both
22, 27, 32,37 | 0.001% | 0.000% | 0.000% | 0.003% | 0.000%
2, 7, 12, 17 | 0.713% | 0.000% | 0.000% | 1.196% | 0.000%
Many more frames over cabac_zero_word threshold in low QP
VTM without dependent quantization performs similarly to HM
cabac_zero_words only required when dependent quantization enabled
Even with coefficient bin limits removed, disabling dependent quantization prevents cabac_zero_word usage

## Slide 10: CTU-based results
QPs under test | Percent of CTUs over cabac_zero_word_threshold |  |  |  | 
 | VTM 6.1 | HM 16.20 | VTM 6.1 without dependent quantization | VTM 6.1 without coefficient bin limits | VTM 6.1 without both
22, 27, 32,37 | 0.226% | <0.001% | 0.000% | 0.229% | 0.000%
2, 7, 12, 17 | 3.701% | 0.001% | 0.001% | 4.091% | 0.002%
Many more CTUs over cabac_zero_word threshold in low QP
VTM without dependent quantization performs similarly to HM
cabac_zero_words very rarely required when dependent quantization disabled
Even with coefficient bin limits removed, disabling dependent quantization almost completely removes cabac_zero_word usage
Percentages are higher for CTUs than frames due to the averaging effect of many CTUs in a frame

## Slide 11: Scatter graph results
HM 16.20
Hue indicates dominant QP
Brightness indicates number of datapoints
Graph of bins vs bits in encoded stream for all square CTUs in CTC and low QP
Red line represents existing cabac_zero_word threshold
Very few points in red region representing CTUs above this threshold

## Slide 12: Scatter graph results
VTM 6.1
Hue indicates dominant QP
Brightness indicates number of datapoints
Graph of bins vs bits in encoded stream for all square CTUs in CTC and low QP
Red line represents existing cabac_zero_word threshold
Points in red region represent CTUs above this threshold

## Slide 13: Scatter graph results
VTM 6.1 without dependent quantization
Hue indicates dominant QP
Brightness indicates number of datapoints
Graph of bins vs bits in encoded stream for all square CTUs in CTC and low QP
Red line represents existing cabac_zero_word threshold
Almost no points in red region representing CTUs above this threshold

## Slide 14: Summary of scatter graphs
Clear from the scatter graphs that CTUs coded using VTM 6.1
  can exceed the cabac_zero_word threshold for CTUs coded at slice QP16-23
    86% of square CTUs that exceed the limit are in this range
  rarely exceed the limit for CTUs otherwise
  very rarely exceed the limit if dependent quantization is disabled.

## Slide 15: Alternative graphical representation
Scatter graphs presented so far plot bins (n) versus bits (b)
Red threshold from previous graphs represents n = β * b + c ÷ α
  α = 32
  β = 4 ÷ 3
To determine alternative α
  Need to compute n – β * b for each CTU
  Generate scatter plot of this computed value versus bits
New scatter plots indicate three threshold values of α
  32 (current value)
  64 ÷ 3
  16

## Slide 16: Alternative graph
HM 16.20
Graph of required bin offset vs bits in encoded stream
β = 4 ÷ 3
1 (CTC) and 90 (low QP) points in red region represent CTUs above the α = 32 threshold

## Slide 17: Alternative graph
VTM 6.1
Graph of required bin offset vs bits in encoded stream
β = 4 ÷ 3
Points in red region represent CTUs above the α = 32 threshold
Some points exist in purple region representing CTUs above α = 64 ÷ 3 threshold
Negative gradient implies current bin-to-bit ratio (β) is too high

## Slide 18: Alternative graph
VTM 6.1 without dependent quantization
Graph of required bin offset vs bits in encoded stream
β = 4 ÷ 3
No points in red region representing CTUs above the α = 32 threshold

## Slide 19: Summary of results 1
For VTM 6.1 without dependent quantization
  Graph is very similar to HM 16.20
    α and β do not need to be changed
For VTM 6.1 with dependent quantization
  α needs to be decreased – we selected α = 16
  β (currently 4 ÷ 3) may be too high
Can plot further scatter graphs which plot bin-to-bit ratio against bits in data stream to determine β
  computed value for y axis becomes (n – c ÷ α) ÷ b

## Slide 20: Ratio graph
HM 16.20
Graph of bin-to-bit ratio vs bits in encoded stream
α = 32
Some points exceed and others very close to β = 4 ÷ 3

## Slide 21: Ratio graph
VTM 6.1
Graph of bin-to-bit ratio vs bits in encoded stream
α = 16
No points close to β = 4 ÷ 3. β can be reduced to 5 ÷ 4
Ratio almost flat as encoded stream length increases.

## Slide 22: Ratio graph
VTM 6.1 without dependent quantization
Graph of bin-to-bit ratio vs bits in encoded stream
α = 32
Some points very close to
β = 4 ÷ 3

## Slide 23: Summary of results 2
For VTM 6.1 without dependent quantization
  Ratio graph is very similar to HM 16.20
    No need to change formula
      α = 32
      β = 4 ÷ 3
For VTM 6.1 with dependent quantisation
  Change suggested
    α = 16
    β = 5 ÷ 4
It is proposed that two different formulae are used
  One when dependent quantization is available
  One when dependent quantization is unavailable

## Slide 24: Impact of coefficient coding limits
Slide 6/7 gave results which indicated that removing the coefficient coding limits in JVET-N0480 and JVET-O052 gave coding gains.
  For screen content across CTC (-0.38% RA) and low QP (-2.49% RA).
  For all classes in low QP (-0.33% for RA overall)
  Similar gains were achieved with dependent quantization disabled (slide 6)
Study assessed the effect of removing these limits on the cabac_zero_word threshold.

## Slide 25: Impact of coefficient coding limits
VTM 6.1
Existing threshold formula
Hue indicates dominant QP
Brightness indicates number of datapoints
Graph of bins vs bits in encoded stream for all square CTUs in CTC and low QP

## Slide 26: Impact of coefficient coding limits
VTM 6.1 without limits
Existing threshold formula
Hue indicates dominant QP
Brightness indicates number of datapoints
Graph of bins vs bits in encoded stream for all square CTUs in CTC and low QP
Effect noticeable for longer bit streams
Not close to threshold
Much less effect for moderate length bit streams near threshold

## Slide 27: Impact of coefficient coding limits
VTM 6.1
Proposed threshold formula
Hue indicates dominant QP
Brightness indicates number of datapoints
Graph of bins vs bits in encoded stream for all square CTUs in CTC and low QP

## Slide 28: Impact of coefficient coding limits
VTM 6.1 without limits
Proposed threshold formula
Hue indicates dominant QP
Brightness indicates number of datapoints
Graph of bins vs bits in encoded stream for all square CTUs in CTC and low QP
Effect noticeable for longer bit streams
Not close to threshold
Less effect for moderate length bit streams. None exceed threshold

## Slide 29: Impact of coefficient coding limits
VTM 6.1 without dependent quantization
Hue indicates dominant QP
Brightness indicates number of datapoints
Graph of bins vs bits in encoded stream for all square CTUs in CTC and low QP

## Slide 30: Impact of coefficient coding limits
VTM 6.1 without limits and dependent quantization
Hue indicates dominant QP
Brightness indicates number of datapoints
Graph of bins vs bits in encoded stream for all square CTUs in CTC and low QP
Effect noticeable for longer bit streams
Not close to threshold
Less effect for moderate length bit streams.

## Slide 31: Bugfix for HM and VTM
During this study the following inconsistency was discovered:
  In the specification 7-39 gives:
RawMinCuBits = MinCbSizeY * MinCbSizeY * ( BitDepthY + 2 * BitDepthC / ( SubWidthC * SubHeightC ) )
i.e. multiply BitDepthC by 2 then divide by ( SubWidthC * SubHeightC )
  In VTM 6.1 and HM 16.20 this is implemented as:
const int rawBits = paddedWidth * paddedHeight * (sps.getBitDepth(CHANNEL_TYPE_LUMA) + 2*(sps.getBitDepth(CHANNEL_TYPE_CHROMA)>>log2subWidthCxsubHeightC));
i.e. divide sps.getBitDepth(CHANNEL_TYPE_CHROMA) by subWidthCxsubHeightC then
multiply by 2.
Code changes have been merged into both VTM and HM.
The change makes no substantive changes to this proposal.
Software coordinator has suggested a further change for odd bit depths (e.g. 9 bit)
RawMinCuBits = MinCbSizeY * MinCbSizeY * BitDepthY + 2 * MinCbSizeY * MinCbSizeY * BitDepthC / ( SubWidthC * SubHeightC )

## Slide 32: Conclusion 1/2
The Bin-to-bit ratios for HM, VTM and VTM without various tools were studied.
  VTM differs significantly from HM only when dependent / trellis quantization is enabled.
We propose the following change to VTM
  To adopt two different formulas for the cabac_zero_word threshold
    When dependent quantization is available:
    10 * NumBytesInVclNalUnits + ( RawMinCuBits * PicSizeInMinCbsY )  16
    or (32 ÷ 3 ) * NumBytesInVclNalUnits + ( RawMinCuBits * PicSizeInMinCbsY ) * 3  64
    When dependent quantization is not available (the existing formula) :
    ( 32 ÷ 3 ) * NumBytesInVclNalUnits + ( RawMinCuBits * PicSizeInMinCbsY )  32
  Thus in future, profiles where dependent quantization is available could use a different threshold.
.

## Slide 33: Conclusion 2/2
By analysing the bit-to-bin ratio with coefficient coding limits enabled and disabled it is not apparent that they provide a benefit in keeping a CTU/frame level bit-to-bin ratio.
As presented previously, we would still suggest that the cabac_zero_word threshold is applied for each slice / independently decodable region to allow splicing (e.g. for 360 viewports).

## Slide 34: Addendum
The impact of not coding cabac-zero words is shown in the following tables.
  Note that these tables were generated by adjusting the per-POC and total amounts of each sequence according to the reported numbers of stuffing bytes.
  (There was not enough time to re-run the simulations)
  Of note:
    RA: Daylight road: -0.39%.
    LB: Cactus: -0.20%
 | Random Access |  |  |  | 
 | Over VTM6.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class A2 | -0.13% | -0.07% | -0.09% | 100% | 100%
Class B | -0.01% | 0.00% | 0.00% | 100% | 100%
Class C | -0.01% | -0.01% | -0.01% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.03% | -0.02% | -0.02% | 100% | 100%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | 0.00% | 0.00% | 0.00% | 100% | 100%
Class TGM | 0.00% | 0.00% | 0.00% | 100% | 100%
 | Low delay B |  |  |  | 
 | Over VTM6.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | -0.05% | -0.04% | -0.04% | 100% | 100%
Class E | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | -0.02% | -0.01% | -0.01% | 100% | 100%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | 0.00% | 0.00% | 0.00% | 100% | 100%
Class TGM | 0.00% | 0.00% | 0.00% | 100% | 100%

## Slide 35: Addendum
The change in alpha is only really useful at high bit rates.
  Depending on the definition of profiles/levels/tiers, such high bit rates may not always be reachable.
    Therefore, if there is a “main” tier, the current equation may suffice.
      In HEVC, Level 5.1 (4K 60P), Main10, MaxBR=40Mbps[Main Tier], 160Mbps[High Tier]
    But for a “high” tier, one of the proposed equations would then be recommended.
    E.g. cabac-zero words occur at the frame level for:
      RA: DaylightRoad (QHD) - QP22 (58Mbps), 17 (428Mbps), 12 (916Mbps)
      RA: Cactus (HD) - QP12 (185Mbps)
      LD: BasketballDrill (832x480) - QP7 (43 Mbps), 12 (18Mbps)
      RA: BasketballDrill (832x480) - QP7 (35Mbps)
      LD: BQMall (832x480), QP12 (37Mbps)
      RA: BlowingBubbles (416x240), QP7 (13Mbps)
      RA: BasketballDrillText (416x240), QP7 (32Mbps)

## Slide 36: Addendum
However, note the CTUs start to exceed the threshold at higher QPs, and therefore potentially in the bit rates of the main tier.
  Also, one of the problem sequences, DaylightRoad shows an issue at QP 22 (@58Mbps), but at QP27 (@10Mbps), there are no instances.
    But 10Mbps is << the 40Mbps MaxBR for main tier.
    It is therefore not safe to say that there is no issue in the main tier.
The losses of the coefficient-level constraint are higher than the losses of coding cabac-zero-words.
Finally, HM kept below the ratio on a frame and CTU basis; should VTM?

## Slide 37: Additional results
 |  | Picture |  | CTU | 
Divisor (α) | Multiplier (β/8) | CTC | Low QP | CTC | Low QP
32 | 1.33 | 0.001% | 0.713% | 0.228% | 3.701%
32 | 1.25 | 0.080% | 6.812% | 0.493% | 11.046%
24 | 1.33 | 0.000% | 0.000% | 0.009% | 0.288%
24 | 1.25 | 0.000% | 0.298% | 0.103% | 2.794%
64 / 3 | 1.33 | 0.000% | 0.000% | 0.000% | 0.009%
64 / 3 | 1.25 | 0.000% | 0.000% | 0.018% | 0.774%
16 | 1.33 | 0.000% | 0.000% | 0.000% | 0.000%
16 | 1.25 | 0.000% | 0.000% | 0.000% | 0.000%