## Slide 1: JVET-P0411 Non-CE5: Fixes for long luma deblocking filter decision K. Andersson, J. Enhorn (Ericsson)
Kenneth Andersson
Ericsson
2019-07-08

## Slide 2: Problem statement
Long luma deblocking is very good in combating large block artifacts
Two problems observed regarding long luma deblocking decision for both SDR and HDR:
  Long luma deblocking is unaware of samples at p6 and q6 since no gradient check include them.
    This can enable long luma deblocking although it should not be used
  Threshold for ramp insensitive long luma filter decision is too high.
    This can enable long deblocking although it should not be used

## Slide 3: Proposed solution 1
Add additional gradient calculation when maxFilterLengthP or maxFilterLengthQ is equal to 7
sp0 = maxFilterLengthP==7 ? Abs( p3,0 − p0,0 ) + Abs( p7,0 – p6,0 – p5,0 + p4,0): Abs( p3,0 − p0,0 ) (8‑1081)
sq0 = maxFilterLengthQ==7 ? Abs( q0,0 − q3,0 ) + Abs( q4,0 – q5,0 – q6,0 + q7,0 ): Abs( q0,0 − q3,0 ) (8‑1082)
spq0 = Abs( p0,0 − q0,0 ) (8‑1083)
sp3 = maxFilterLengthP==7 ? Abs( p3,3 − p0,3 ) + Abs( p7,3 – p6,3 – p5,3 + p4,3): Abs( p3,3 − p0,3 ) (8‑1084)
sq3 = maxFilterLengthQ==7 ? Abs( q0,3 − q3,3 ) + Abs( q4,3 – q5,3 – q6,3 + q7,3 ): Abs( q0,3 − q3,3 ) (8‑1085)

## Slide 4: Proposed solution 2
Reduce beta threshold for ramp insensitive gradient calculations:
The variables sThr1 and sThr2 are derived as follows:
If sidePisLargeBlk is equal to 1 or sideQisLargeBlk is equal to 1, the following applies:
  sThr1 = 3 * β >> 5 (8‑1160)
  sThr2 = β >> 4 (8‑1160)
Otherwise, the following applies:
  sThr1 = β >> 3 (8‑1161)
  sThr2 = β >> 2 (8‑1161)
The variable dSam is specified as follows:
If all of the following conditions are true, dSam is set equal to 1:
  dpq is less than ( β >> 2 )sThr2,
  sp + sq is less than sThr1,
  spq is less than ( 5 * tC + 1 ) >> 1.
Otherwise, dSam is set equal to 0.

## Slide 5: Subjective example (ALF on)
Figure: Daystreet, POC 133, RA QP 37, ALF ON. Left: VTM-6.0, Right: Proposed threshold

## Slide 6: Subjective example (ALF on)
Figure: DayStreet, POC 111, RA QP 37, ALF ON. Left: VTM-6.0, Right: Proposed gradient calculation

## Slide 7: Subjective example (ALF on)
Figure: Daystreet, POC 111, RA QP 37, ALF ON. Left: VTM-6.0, Right: Proposed gradient calculation and threshold

## Slide 8: Subjective example (ALF on)
Figure: Hurdles POC 76, RA QP 37, ALF ON. Left: VTM-6.0, Right: Proposed gradient calculation

## Slide 9: Subjective example (ALF on)
Figure: Hurdles POC 76, RA QP 37, ALF ON. Left: VTM-6.0, Right: Proposed threshold

## Slide 10: Subjective example (ALF on)
Figure: Hurdles POC 76, RA QP 37, ALF ON. Left: VTM-6.0, Right: Proposed gradient calculation and threshold

## Slide 11: Objective results SDR
 | Random access Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,12% | -0,01% | -0,02% | 103% | 99%
Class A2 | -0,05% | 0,03% | -0,05% | 101% | 104%
Class B | -0,08% | 0,10% | -0,02% | 101% | 100%
Class C | -0,04% | 0,02% | -0,05% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0,07% | 0,04% | -0,03% | 101% | 101%
Class D | -0,04% | 0,04% | 0,21% | 100% | 102%
Class F | -0,05% | 0,04% | 0,02% | 99% | 100%
 | Random access Over VTM-6.0 without ALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,08% | 0,12% | 0,03% | 101% | 100%
Class A2 | -0,06% | 0,03% | 0,05% | 100% | 102%
Class B | -0,06% | -0,07% | -0,08% | 100% | 100%
Class C | -0,03% | 0,00% | 0,01% | 98% | 100%
Class E |  |  |  |  | 
Overall | -0,06% | 0,01% | -0,01% | 100% | 100%
Class D | -0,04% | -0,01% | 0,05% | 99% | 96%
Class F | -0,03% | 0,01% | 0,03% | 92% | 100%
 | Low delay Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,12% | -0,12% | -0,08% | 101% | 100%
Class C | -0,08% | 0,13% | 0,02% | 104% | 102%
Class E | -0,24% | -0,25% | 0,30% | 98% | 100%
Overall | -0,14% | -0,07% | 0,05% | 102% | 101%
Class D | -0,01% | 0,03% | 0,22% | 101% | 97%
Class F | -0,05% | -0,24% | 0,66% | 100% | 100%
 | Low delay Over VTM-6.0 without ALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,14% | -0,27% | -0,28% | 103% | 98%
Class C | -0,06% | 0,03% | -0,04% | 103% | 100%
Class E | -0,17% | -0,18% | 0,15% | 105% | 100%
Overall | -0,12% | -0,15% | -0,09% | 102% | 99%
Class D | 0,01% | 0,15% | -0,16% | 104% | 98%
Class F | -0,10% | -0,13% | 0,77% | 102% | 99%

## Slide 12: Objective results SDR
 | Intra Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,06% | 0,01% | 0,00% | 104% | 100%
Class A2 | -0,01% | 0,00% | 0,00% | 105% | 101%
Class B | -0,02% | -0,01% | -0,01% | 104% | 101%
Class C | 0,00% | 0,00% | 0,00% | 104% | 101%
Class E | 0,00% | 0,00% | 0,00% | 102% | 100%
Overall | -0,02% | 0,00% | 0,00% | 104% | 101%
Class D | 0,00% | 0,00% | 0,00% | 103% | 103%
Class F | -0,01% | 0,00% | 0,01% | 105% | 102%
 | Intra Over VTM-6.0 without ALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,02% | 0,01% | 0,00% | 100% | 99%
Class A2 | -0,01% | 0,00% | 0,00% | 101% | 100%
Class B | -0,01% | 0,00% | 0,00% | 101% | 101%
Class C | 0,00% | 0,00% | 0,00% | 97% | 100%
Class E | 0,01% | 0,00% | 0,00% | 96% | 100%
Overall | -0,01% | 0,00% | 0,00% | 99% | 100%
Class D | 0,00% | 0,00% | 0,00% | 99% | 96%
Class F | 0,00% | -0,01% | 0,00% | 99% | 98%

## Slide 13: Objective results HDR
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-6.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | -0,08% | -0,16% | -0,09% | 0,09% | -0,06% | -0,07% | 0,14% | 0,11% | #VALUE! | 102%
Class H2 |  |  |  |  |  | -0,07% | 0,03% | 0,04% | #VALUE! | 98%
Overall | -0,08% | -0,16% | -0,09% | 0,09% | -0,06% | -0,07% | 0,10% | 0,08% | #VALUE! | 100%

## Slide 14: Conclusion
Proposed to add gradient calculation and reduce beta threshold for long filter decisions
The fixes improves visual quality on both SDR and HDR content.
Minor BDR impact.
It is proposed include the fixes for next version of VVC.
If time allows a demo may be available at EBU