## Slide 1: JVET-P0412 CE5-related: On further modification of Hadamard filter from CE5-3.2
S. Ikonin, V. Stepin, A. Karabutov, S. Nikolaeva

## Slide 2
Following modifications were made
  Aspect 1
In CE5-3.2.1 at in-loop filtering stage SAO and Hadamard filter has its own RDO to decide whether to apply filter at CTU and slice level. However, the result of joint work was not evaluated. In order to compensate that the following modification was made. When cost of SAO filtered frame is above than Hadamard filtered frame then SAO is disabled at the slice level.
  Aspect 2
In implementation tested in CE5-3.2.1 the averaging of SAO and Hadamard output is performed at the frame basis without consideration of whether filter is applied to particular CTU or not. This lead to degradation of joint filtering performance. This bug was fixed by averaging only for those CTUs where both filters are enabled.
  Aspect 3
This is a non-normative fix of a bug identified in CE5-3.2 software. During cost calculation in encoder RDO the padding process may touch uninitialized memory.
Fixes of CE5-3.2 on Hadamard filter test

## Slide 3
Fixes of CE5-3.2.1 on Hadamard filter test
 | All Intra |  |  |  |  |  | Random Access |  |  |  |  | 
Test# |  | Y | U | V | EncT | DecT |  | Y | U | V | EncT | DecT
CE5-3.2.1 |  | -0.33% | 0.39% | 0.37% | 107% | 108% |  | -0.37% | 0.30% | 0.31% | 104% | 103%
CE5-3.2.1 + fixes |  | -0.44% | 0.43% | 0.44% | 108% | 106% |  | -0.42% | 0.36% | 0.36% | 104% | 104%
 | Low Delay B |  |  |  |  |  | Low Delay P |  |  |  |  | 
Test# |  | Y | U | V | EncT | DecT |  | Y | U | V | EncT | DecT
CE5-3.2.1 |  | -0.08% | 0.68% | 0.64% | 103% | 103% |  | -0.16% | 0.47% | 0.73% | 104% | 103%
CE5-3.2.1 + fixes |  | -0.17%* | 1.00% | 1.02% | 103% | 102% |  | -0.22% | 0.98% | 1.09% | 104% | 102%
Anchor: VTM6.0

## Slide 4
Fixes of CE5-3.2.1 on Hadamard filter test, ALF is off
 | All Intra |  |  |  |  |  | Random Access |  |  |  |  | 
Test# |  | Y | U | V | EncT | DecT |  | Y | U | V | EncT | DecT
CE5-3.2.1 |  | -0.46% | 0.44% | 0.42% | 108% | 110% |  | -0.60% | 0.28% | 0.32% | 104% | 105%
CE5-3.2.1 + fixes |  | -0.67% | 0.61% | 0.79% | 108% | 108% |  | -0.72% | 0.59% | 0.49% | 104% | 105%
 | Low Delay B |  |  |  |  |  | Low Delay P |  |  |  |  | 
Test# |  | Y | U | V | EncT | DecT |  | Y | U | V | EncT | DecT
CE5-3.2.1 |  | -0.49% | 0.70% | 0.61% | 103% | 104% |  | -0.58% | 0.97% | 0.91% | 105% | 105%
CE5-3.2.1 + fixes |  | -0.53%* | 1.63% | 1.85% | 103% | 104% |  | -0.69% | 2.05% | 2.14% | 105% | 104%
Anchor: VTM6.0.noALF

## Slide 5
CE5-3.2.2 on Hadamard filter test + chroma filtering
Anchor: VTM6.0.noSAO
 | All Intra |  |  |  |  | Random Access |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SAO | 0.00% | -0.13% | -0.15% | 66% | 77% | -0.08% | -0.26% | -0.35% | 71% | 72%
CE5-3.2.2 | -0.42% | 0.39% | 0.36% | 108% | 105% | -0.46% | 0.11% | 0.16% | 104% | 101%
CE5-3.2.2 + chroma | -0.42% | -0.11% | 0.13% | 109% | 109% | -0.47% | -0.01% | 0.37% | 105% | 102%
 | Low Delay B |  |  |  |  | Low Delay P |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SAO | -0.10% | -0.58% | -1.13% | 72% | 70% | -0.12% | -0.28% | -0.82% | 72% | 70%
CE5-3.2.2 | -0.25% | 0.47% | 0.31% | 102% | 101% | -0.32% | 0.59% | 0.62% | 103% | 101%
CE5-3.2.2 + chroma | -0.22% | 0.20% | 0.33% | 103% | 102% | -0.30% | 0.48% | 0.84% | 104% | 102%
In CE5-3.2 Hdamard is only applied to luma samples. The effect of applying the filter to chroma samples as well was studied.

## Slide 6
CE5-3.2.2 on Hadamard filter test + chroma filtering
Anchor: VTM6.0.noSAO.noALF
 | All Intra |  |  |  |  | Random Access |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SAO | -0.32% | -0.37% | -0.70% | 100% | 104% | -0.79% | -0.80% | -0.72% | 100% | 102%
CE5-3.2.2 | -0.93% | 0.43% | 0.41% | 108% | 107% | -1.35% | 0.13% | 0.14% | 104% | 102%
CE5-3.2.2 + chroma | -0.93% | -0.82% | -0.79% | 109% | 111% | -1.36% | 0.13% | 0.70% | 106% | 103%
 | Low Delay B |  |  |  |  | Low Delay P |  |  |  | 
Test# | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SAO | -0.95% | -1.71% | -2.82% | 100% | 102% | -2.59% | -3.06% | -3.65% | 100% | 102%
CE5-3.2.2 | -1.34% | 1.00% | 0.83% | 103% | 102% | -2.65% | 0.71% | 1.10% | 105% | 103%
CE5-3.2.2 + chroma | -1.25% | 0.78% | 0.76% | 104% | 103% | -2.55% | 0.33% | 0.68% | 106% | 103%
In CE5-3.2 Hdamard is only applied to luma samples. The effect of applying the filter to chroma samples as well was studied.

## Slide 7
Acknowledgment
Thanks Ericsson for cross-checking!

## Slide 8
CE5-3.2.1 (for reference)
Simulation results of CE5-3.2.1 fixes
 | All Intra |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.28% | 0.52% | 0.49% | 108% | 110%
Class A2 | -0.38% | 0.40% | 0.31% | 107% | 109%
Class B | -0.26% | 0.50% | 0.42% | 107% | 108%
Class C | -0.42% | 0.21% | 0.35% | 107% | 107%
Class E | -0.33% | 0.34% | 0.29% | 107% | 108%
Overall | -0.33% | 0.39% | 0.37% | 107% | 108%
Class D | -0.36% | 0.48% | 0.32% | 107% | 106%
Class F | -0.17% | 0.17% | 0.06% | 105% | 107%
 | Random Access |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.17% | 0.25% | 0.17% | 103% | 105%
Class A2 | -0.60% | 0.16% | 0.06% | 104% | 104%
Class B | -0.34% | 0.38% | 0.49% | 105% | 103%
Class C | -0.38% | 0.33% | 0.36% | 104% | 103%
Class E |  |  |  |  | 
Overall | -0.37% | 0.30% | 0.31% | 104% | 103%
Class D | -0.50% | 0.06% | 0.18% | 103% | 102%
Class F | -0.09% | 0.03% | 0.15% | 103% | 103%
All Intra |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.40% | 0.63% | 0.43% | 108% | 108%
-0.50% | 0.56% | 0.39% | 107% | 106%
-0.33% | 0.50% | 0.50% | 109% | 106%
-0.56% | 0.29% | 0.51% | 108% | 106%
-0.47% | 0.15% | 0.28% | 108% | 106%
-0.44% | 0.43% | 0.44% | 108% | 106%
-0.47% | 0.39% | 0.32% | 108% | 104%
-0.25% | 0.44% | 0.38% | 106% | 106%
Random Access |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.23% | 0.38% | 0.19% | 103% | 105%
-0.59% | 0.37% | 0.36% | 103% | 104%
-0.39% | 0.38% | 0.42% | 104% | 103%
-0.47% | 0.32% | 0.41% | 103% | 102%
-0.42% | 0.36% | 0.36% | 104% | 104%
-0.63% | 0.14% | 0.35% | 104% | 102%
-0.21% | 0.27% | 0.39% | 103% | 104%
CE5-3.2.1 + 3 fixes

## Slide 9
CE5-3.2.1 (for reference)
Simulation results of CE5-3.2.1 fixes, LD
 | Low delay B |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | 1.07% | 0.57% | 103% | 103%
Class C | -0.25% | 0.30% | 0.51% | 103% | 102%
Class E | -0.05% | 0.55% | 0.93% | 101% | 103%
Overall | -0.08% | 0.68% | 0.64% | 103% | 103%
Class D | -0.36% | 0.72% | 0.78% | 103% | 102%
Class F | 0.18% | 0.37% | 1.09% | 102% | 104%
 | Low delay P |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.12% | 0.91% | 0.85% | 105% | 104%
Class C | -0.28% | 0.33% | 0.55% | 104% | 103%
Class E | -0.07% | -0.06% | 0.76% | 102% | 104%
Overall | -0.16% | 0.47% | 0.73% | 104% | 103%
Class D | -0.43% | 0.91% | 0.09% | 104% | 103%
Class F | 0.03% | 0.68% | 0.33% | 103% | 103%
Low delay B |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.07%* | 1.16% | 0.96% | 104% | 103%
-0.40% | 0.49% | 0.93% | 103% | 102%
-0.05% | 1.40% | 1.23% | 101% | 103%
-0.17%* | 1.00% | 1.02% | 103% | 102%
-0.60% | 1.03% | 1.29% | 103% | 102%
-0.01% | 0.13% | 0.81% | 102% | 103%
Low delay P |  |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.21% | 1.25% | 1.25% | 105% | 102%
-0.36% | 0.75% | 0.94% | 104% | 101%
-0.04% | 0.85% | 1.02% | 102% | 103%
-0.22% | 0.98% | 1.09% | 104% | 102%
-0.65% | 0.89% | 0.93% | 104% | 103%
-0.06% | 0.33% | 0.15% | 102% | 104%
CE5-3.2.1 + 3 fixes
*) few rate points for LDB are extrapolated

## Slide 10
CE5-3.2.1 (for reference)
Simulation results of CE5-3.2.1 fixes, ALF off test
 | All Intra |  |  |  | 
 | Over VTM-6.0.noALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.39% | 0.56% | 0.58% | 108% | 112%
Class A2 | -0.46% | 0.42% | 0.33% | 108% | 111%
Class B | -0.41% | 0.55% | 0.45% | 107% | 110%
Class C | -0.52% | 0.28% | 0.40% | 108% | 108%
Class E | -0.55% | 0.37% | 0.32% | 108% | 109%
Overall | -0.46% | 0.44% | 0.42% | 108% | 110%
Class D | -0.46% | 0.52% | 0.36% | 107% | 107%
Class F | -0.21% | 0.20% | 0.15% | 105% | 108%
 | Random Access |  |  |  | 
 | Over VTM-6.0.noALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.39% | 0.22% | 0.26% | 104% | 107%
Class A2 | -0.90% | 0.17% | 0.15% | 104% | 105%
Class B | -0.59% | 0.31% | 0.43% | 105% | 105%
Class C | -0.53% | 0.36% | 0.36% | 104% | 103%
Class E |  |  |  |  | 
Overall | -0.60% | 0.28% | 0.32% | 104% | 105%
Class D | -0.50% | 0.27% | 0.24% | 104% | 102%
Class F | -0.14% | 0.23% | 0.41% | 103% | 104%
All Intra |  |  |  | 
Over VTM-6.0.noALF |  |  |  | 
Y | U | V | EncT | DecT
-0.67% | 0.77% | 1.20% | 109% | 110%
-0.63% | 0.77% | 0.58% | 108% | 107%
-0.51% | 0.66% | 0.75% | 108% | 108%
-0.75% | 0.58% | 1.00% | 109% | 106%
-0.83% | 0.23% | 0.38% | 109% | 108%
-0.67% | 0.61% | 0.79% | 108% | 108%
-0.61% | 0.69% | 0.73% | 108% | 105%
-0.33% | 0.74% | 0.88% | 106% | 108%
Random Access |  |  |  | 
Over VTM-6.0.noALF |  |  |  | 
Y | U | V | EncT | DecT
-0.50% | 0.52% | 0.54% | 104% | 107%
-0.94% | 0.89% | 0.44% | 104% | 105%
-0.73% | 0.69% | 0.47% | 105% | 105%
-0.69% | 0.31% | 0.50% | 104% | 103%
-0.72% | 0.59% | 0.49% | 104% | 105%
-0.67% | 0.08% | 0.16% | 104% | 102%
-0.29% | 0.62% | 0.80% | 103% | 105%
CE5-3.2.1 + 3 fixes

## Slide 11
CE5-3.2.1 (for reference)
Simulation results of CE5-3.2.1 fixes, ALF off test , LD
 | Low delay B |  |  |  | 
 | Over VTM-6.0.noALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.42% | 0.83% | 0.48% | 104% | 105%
Class C | -0.65% | 0.54% | 0.46% | 104% | 103%
Class E | -0.39% | 0.71% | 1.02% | 102% | 105%
Overall | -0.49% | 0.70% | 0.61% | 103% | 104%
Class D | -0.61% | 1.43% | 0.99% | 104% | 103%
Class F | 0.16% | 0.85% | 0.32% | 103% | 105%
 | Low delay P |  |  |  | 
 | Over VTM-6.0.noALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.52% | 1.24% | 1.35% | 106% | 106%
Class C | -0.69% | 0.65% | 0.48% | 105% | 104%
Class E | -0.55% | 0.93% | 0.78% | 103% | 105%
Overall | -0.58% | 0.97% | 0.91% | 105% | 105%
Class D | -0.82% | 1.08% | 0.85% | 105% | 102%
Class F | 0.03% | 0.66% | 0.62% | 104% | 105%
Low delay B |  |  |  | 
Over VTM-6.0.noALF |  |  |  | 
Y | U | V | EncT | DecT
-0.52%* | 1.96% | 1.48% | 104% | 104%
-0.73% | 1.62% | 2.83% | 104% | 102%
-0.29% | 1.10% | 1.16% | 101% | 104%
-0.53%* | 1.63% | 1.85% | 103% | 104%
-0.84% | 2.69% | 2.22% | 105% | 103%
-0.13% | 0.88% | 0.15% | 103% | 105%
Low delay P |  |  |  | 
Over VTM-6.0.noALF |  |  |  | 
Y | U | V | EncT | DecT
-0.65% | 2.16% | 2.21% | 106% | 105%
-0.83% | 1.95% | 2.74% | 105% | 103%
-0.59% | 1.99% | 1.21% | 103% | 105%
-0.69% | 2.05% | 2.14% | 105% | 104%
-1.18% | 2.40% | 1.90% | 106% | 100%
-0.21% | 1.18% | 0.19% | 104% | 105%
CE5-3.2.1 + 3 fixes
*) few rate points for LDB are extrapolated

## Slide 12
CE5-3.2.2 + chroma
CE5-3.2.2 (no SAO) + chroma filtering
 | All Intra |  |  |  | 
 | Over VTM-6.0.noSAO |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.33% | 0.51% | 0.46% | 108% | 105%
Class A2 | -0.44% | 0.39% | 0.30% | 107% | 105%
Class B | -0.33% | 0.49% | 0.40% | 108% | 106%
Class C | -0.54% | 0.20% | 0.31% | 108% | 105%
Class E | -0.50% | 0.33% | 0.30% | 108% | 106%
Overall | -0.42% | 0.39% | 0.36% | 108% | 105%
Class D | -0.48% | 0.34% | 0.18% | 107% | 105%
Class F | -0.52% | 0.20% | 0.04% | 105% | 106%
 | Random Access |  |  |  | 
 | Over VTM-6.0.noSAO |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.24% | 0.18% | 0.19% | 103% | 102%
Class A2 | -0.73% | -0.07% | -0.06% | 104% | 102%
Class B | -0.46% | 0.16% | 0.20% | 104% | 101%
Class C | -0.43% | 0.13% | 0.25% | 103% | 101%
Class E |  |  |  |  | 
Overall | -0.46% | 0.11% | 0.16% | 104% | 101%
Class D | -0.47% | 0.05% | 0.04% | 103% | 100%
Class F | -0.44% | 0.08% | 0.21% | 103% | 101%
All Intra |  |  |  | 
Over VTM-6.0.noSAO |  |  |  | 
Y | U | V | EncT | DecT
-0.39% | 0.01% | 0.01% | 109% | 109%
-0.37% | -0.01% | -0.01% | 109% | 109%
-0.32% | 0.02% | 0.55% | 109% | 109%
-0.55% | -0.34% | -0.15% | 109% | 109%
-0.51% | -0.24% | 0.07% | 109% | 109%
-0.42% | -0.11% | 0.13% | 109% | 109%
-0.50% | -0.22% | -0.15% | 109% | 108%
-0.51% | -0.48% | -0.50% | 106% | 109%
Random Access |  |  |  | 
Over VTM-6.0.noSAO |  |  |  | 
Y | U | V | EncT | DecT
-0.27% | 0.17% | -0.03% | 105% | 103%
-0.69% | -0.24% | -0.04% | 105% | 102%
-0.46% | 0.06% | 0.82% | 106% | 102%
-0.46% | -0.06% | 0.42% | 105% | 101%
-0.47% | -0.01% | 0.37% | 105% | 102%
-0.48% | -0.05% | 0.28% | 104% | 100%
-0.44% | -0.38% | 0.12% | 104% | 101%
CE5-3.2.2 (for reference)

## Slide 13
CE5-3.2.2 + chroma
CE5-3.2.2 (no SAO) + chroma filtering, LD
 | Low delay B |  |  |  | 
 | Over VTM-6.0.noSAO |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.18% | 0.63% | 0.24% | 103% | 101%
Class C | -0.40% | 0.24% | 0.21% | 102% | 101%
Class E | -0.17% | 0.51% | 0.53% | 101% | 100%
Overall | -0.25% | 0.47% | 0.30% | 102% | 101%
Class D | -0.62% | 1.34% | 1.25% | 103% | 101%
Class F | -0.15% | 0.58% | 0.01% | 102% | 102%
 | Low delay P |  |  |  | 
 | Over VTM-6.0.noSAO |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.26% | 0.50% | 0.43% | 104% | 102%
Class C | -0.40% | 0.28% | 0.29% | 103% | 101%
Class E | -0.32% | 1.15% | 1.36% | 101% | 100%
Overall | -0.32% | 0.59% | 0.62% | 103% | 101%
Class D | -0.60% | 1.04% | 0.41% | 103% | 101%
Class F | -0.27% | 0.14% | 0.24% | 102% | 102%
Low delay B |  |  |  | 
Over VTM-6.0.noSAO |  |  |  | 
Y | U | V | EncT | DecT
-0.14% | 0.39% | 0.34% | 104% | 102%
-0.33% | 0.13% | 0.31% | 104% | 102%
0.21% | 0.00% | 0.37% | 101% | 101%
-0.22% | 0.20% | 0.33% | 103% | 102%
-0.54% | 0.95% | 0.47% | 104% | 101%
-0.15% | 0.65% | 0.01% | 103% | 102%
Low delay P |  |  |  | 
Over VTM-6.0.noSAO |  |  |  | 
Y | U | V | EncT | DecT
-0.22% | 0.57% | 0.62% | 106% | 103%
-0.40% | 0.22% | 0.34% | 105% | 102%
-0.31% | 0.68% | 1.86% | 102% | 101%
-0.30% | 0.48% | 0.84% | 104% | 102%
-0.50% | 0.69% | 0.45% | 104% | 101%
-0.36% | 0.19% | -0.29% | 103% | 102%
CE5-3.2.2 (for reference)

## Slide 14
CE5-3.2.2 + chroma
CE5-3.2.2 (no SAO) + chroma filtering, no ALF test
 | All Intra |  |  |  | 
 | Over VTM-6.0.noSAO.noALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.82% | 0.56% | 0.59% | 108% | 107%
Class A2 | -0.97% | 0.42% | 0.34% | 108% | 107%
Class B | -0.76% | 0.54% | 0.44% | 108% | 107%
Class C | -1.01% | 0.27% | 0.36% | 108% | 106%
Class E | -1.21% | 0.36% | 0.31% | 107% | 107%
Overall | -0.93% | 0.43% | 0.41% | 108% | 107%
Class D | -0.83% | 0.51% | 0.35% | 107% | 106%
Class F | -1.10% | 0.21% | 0.14% | 105% | 107%
 | Random Access |  |  |  | 
 | Over VTM-6.0.noSAO.noALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.83% | 0.23% | 0.19% | 103% | 103%
Class A2 | -2.03% | -0.06% | -0.11% | 104% | 103%
Class B | -1.58% | 0.16% | 0.12% | 105% | 102%
Class C | -0.95% | 0.14% | 0.32% | 103% | 102%
Class E |  |  |  |  | 
Overall | -1.35% | 0.13% | 0.14% | 104% | 102%
Class D | -0.71% | 0.00% | 0.08% | 103% | 101%
Class F | -1.07% | 0.13% | 0.25% | 103% | 102%
All Intra |  |  |  | 
Over VTM-6.0.noSAO.noALF |  |  |  | 
Y | U | V | EncT | DecT
-0.87% | -1.34% | -2.06% | 110% | 112%
-0.90% | -0.69% | -0.36% | 110% | 111%
-0.76% | -0.46% | 0.07% | 109% | 110%
-1.03% | -0.94% | -1.01% | 109% | 110%
-1.21% | -0.85% | -1.08% | 109% | 112%
-0.93% | -0.82% | -0.79% | 109% | 111%
-0.83% | -0.80% | -1.03% | 109% | 107%
-1.10% | -1.14% | -1.20% | 106% | 111%
Random Access |  |  |  | 
Over VTM-6.0.noSAO.noALF |  |  |  | 
Y | U | V | EncT | DecT
-0.83% | 0.38% | 0.14% | 106% | 104%
-2.02% | -0.21% | 0.12% | 106% | 103%
-1.60% | 0.24% | 1.33% | 107% | 103%
-0.99% | 0.07% | 0.77% | 105% | 102%
-1.36% | 0.13% | 0.70% | 106% | 103%
-0.66% | 0.24% | 0.58% | 105% | 102%
-1.05% | -0.49% | -0.35% | 104% | 102%
CE5-3.2.2 (for reference)

## Slide 15
CE5-3.2.2 + chroma
CE5-3.2.2 (no SAO) + chroma filtering, noALF test, LD
 | Low delay B |  |  |  | 
 | Over VTM-6.0.noSAO.noALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -1.34% | 1.08% | 0.91% | 104% | 102%
Class C | -1.45% | 0.56% | 0.60% | 103% | 102%
Class E | -1.21% | 1.47% | 1.00% | 101% | 101%
Overall | -1.34% | 1.00% | 0.83% | 103% | 102%
Class D | -1.00% | 1.13% | 0.63% | 104% | 101%
Class F | -1.42% | 0.52% | -0.14% | 102% | 102%
 | Low delay P |  |  |  | 
 | Over VTM-6.0.noSAO.noALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -2.91% | 0.82% | 1.57% | 106% | 104%
Class C | -2.40% | 0.52% | 0.82% | 105% | 102%
Class E | -2.53% | 0.79% | 0.67% | 103% | 102%
Overall | -2.65% | 0.71% | 1.10% | 105% | 103%
Class D | -1.98% | 1.52% | 0.97% | 105% | 101%
Class F | -1.64% | -0.08% | 0.11% | 103% | 103%
Low delay B |  |  |  | 
Over VTM-6.0.noSAO.noALF |  |  |  | 
Y | U | V | EncT | DecT
-1.27% | 1.00% | 1.24% | 105% | 103%
-1.37% | 0.02% | 0.50% | 104% | 102%
-1.04% | 1.42% | 0.32% | 102% | 102%
-1.25% | 0.78% | 0.76% | 104% | 103%
-0.97% | 0.53% | 1.15% | 105% | 102%
-1.30% | -0.14% | -0.03% | 103% | 103%
Low delay P |  |  |  | 
Over VTM-6.0.noSAO.noALF |  |  |  | 
Y | U | V | EncT | DecT
-2.84% | 0.49% | 1.24% | 108% | 104%
-2.29% | -0.07% | 0.35% | 106% | 103%
-2.40% | 0.59% | 0.20% | 104% | 102%
-2.55% | 0.33% | 0.68% | 106% | 103%
-1.96% | 0.72% | 0.40% | 107% | 102%
-1.54% | -0.24% | -0.45% | 105% | 102%
CE5-3.2.2 (for reference)