## Slide 1: JVET-P0436: AHG15: On CU Adaptive Chroma QP Offset Signaling
J. Zhao, S. Paluri S. Kim
LG ELECTRONICS

## Slide 2: Introduction
As background, the followings were adopted in July meeting:
  CU level Chroma QP offset signaling
  cu_qp_delta signalling is modified to facilitate VPDU-level processing, i.e. for CU larger than 64x64, send the cu_qp_delta with the first transform unit, regardless of whether that first TU has any non-zero CBF or not.
This contribution is regarding:
Unnecessary signaling of CU chroma QP offset in the case of DUAL_TREE_LUMA
Chroma QP offset signaling is not consistent with VPDU QP availability

## Slide 3: QP related syntaxes in transform_unit
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex, chType ) { | Descriptor
…. | 
if( ( CbWidth[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ CbHeight[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ tu_cbf_luma[ x0 ][ y0 ] ¦ ¦ tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ] ) && treeType != DUAL_TREE_CHROMA ) { | 
if( cu_qp_delta_enabled_flag && !IsCuQpDeltaCoded ) { | 
cu_qp_delta_abs | ae(v)
if( cu_qp_delta_abs ) | 
cu_qp_delta_sign_flag | ae(v)
} | 
} | 
if( ( tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ] ) { | 
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded) { | 
cu_chroma_qp_offset_flag | ae(v)
if( cu_chroma_qp_offset_flag && chroma_qp_offset_list_len_minus1 > 0 ) | 
cu_chroma_qp_offset_idx | ae(v)
} | 
} | 

## Slide 4: QP related in palette_coding
palette_coding( x0, y0, cbWidth, cbHeight, startComp, numComps ) { | Descriptor
….. | 
if( treeType != DUAL_TREE_CHROMA && palette_escape_val_present_flag ) { | 
if( cu_qp_delta_enabled_flag && !IsCuQpDeltaCoded ) { | 
cu_qp_delta_abs | ae(v)
if( cu_qp_delta_abs ) | 
cu_qp_delta_sign_flag | ae(v)
} | 
} | 
if( treeType != DUAL_TREE_LUMA && palette_escape_val_present_flag ) { | 
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded ) { | 
cu_chroma_qp_offset_flag | ae(v)
if( cu_chroma_qp_offset_flag ) | 
cu_chroma_qp_offset_idx | ae(v)
} | 
} | 
…… | 
} | 

## Slide 5: Issues 1 and Proposed Fixes:
No need to signal cu_chroma_qp_offset_xxx in the case of DUAL_TREE_LUMA
This restriction is already around cu_chroma_qp_offset_xxx in palette_coding, but not in transform_unit
Suggested Fix: add this condition in transform_unit
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex, chType ) { | Descriptor
…. | 
if( ( tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ]) && treeType != DUAL_TREE_LUMA ) { | 
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded) { | 
cu_chroma_qp_offset_flag | ae(v)
if( cu_chroma_qp_offset_flag && chroma_qp_offset_list_len_minus1 > 0 ) | 
cu_chroma_qp_offset_idx | ae(v)
} | 
} | 

## Slide 6: Issues 2 and Proposed Fixes:
Luma Qp is available at VPDU-level, for CU > 64x64, delta QP is signalled with first TU regardless of cbf.
But Chroma QP offset may be not be available at VPDU level. Suggest to add similar condition.
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex, chType ) {
….
if( ( CbWidth[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ CbHeight[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ tu_cbf_luma[ x0 ][ y0 ] ¦ ¦ tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ] ) && treeType != DUAL_TREE_CHROMA ) {
if( cu_qp_delta_enabled_flag && !IsCuQpDeltaCoded ) {
cu_qp_delta_abs
if( cu_qp_delta_abs )
cu_qp_delta_sign_flag
}
}
if(( CbWidth[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ CbHeight[ chType ][ x0 ][ y0 ] > 64 ) && ( tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ]) ) {
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded) {
cu_chroma_qp_offset_flag
if( cu_chroma_qp_offset_flag && chroma_qp_offset_list_len_minus1 > 0 )
cu_chroma_qp_offset_idx
}
}

## Slide 7: Combined Syntax Changes:
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex, chType ) { | Descriptor
…. | 
if( ( CbWidth[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ CbHeight[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ tu_cbf_luma[ x0 ][ y0 ] ¦ ¦ tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ] ) && treeType != DUAL_TREE_CHROMA ) { | 
if( cu_qp_delta_enabled_flag && !IsCuQpDeltaCoded ) { | 
cu_qp_delta_abs | ae(v)
if( cu_qp_delta_abs ) | 
cu_qp_delta_sign_flag | ae(v)
} | 
} | 
if(( CbWidth[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ CbHeight[ chType ][ x0 ][ y0 ] > 64 ) && ( tu_cbf_cb[ x0 ][ y0 ] ¦ ¦ tu_cbf_cr[ x0 ][ y0 ]) && treeType != DUAL_TREE_LUMA) { | 
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded) { | 
cu_chroma_qp_offset_flag | ae(v)
if( cu_chroma_qp_offset_flag && chroma_qp_offset_list_len_minus1 > 0 ) | 
cu_chroma_qp_offset_idx | ae(v)
} | 
} | 
The highlighted texts are the proposed changes