## Slide 1: JVET-P0444 non-CE4 DMVR without Padding
G. Li, X. Li, X. Xu, S. Liu
2019/10

## Slide 2: Introduction
It was previously adopted to do DMVR padding on each sub-PU
Due to complex memory copy and padding process, decoder speed is reduced

## Slide 3: Proposed Method
Use reference samples for DMVR processing
Additional reference samples can be loaded at CU or sub-PU level with equivalent result

## Slide 4: Proposed Method
Search Range
  Keep DMVR search range of 2 for size 16x16
  Use DMVR search range of 1 for size 8x16 & 16x8
Memory bandwidth requirement < 8x8 Bi
  8x8 Bi prediction
    2 * (8+7) * (8+7) / (8x8) = 7.03
  Sub-PU 16x16 with range 2
    2 * (16+7+4) * (16+7+4) / (16x16) = 5.70
  sub-PU 8x16 with range 1
    2 * (8+7+2) * (16+7+2) / (8x16) = 6.64

## Slide 5: Simulation results
Anchor: VTM-6.0
 |  |  | RA |  |  | 
 |  |  | Over VTM-6.0 |  |  | 
 | Y | U | V | EncT | DecT | DMVR Time
Class A1 | 0.02% | 0.04% | 0.07% | 100% | 95% | 70%
Class A2 | 0.08% | 0.02% | 0.06% | 100% | 95% | 72%
Class B | 0.05% | 0.10% | 0.04% | 100% | 96% | 73%
Class C | 0.04% | 0.09% | 0.04% | 100% | 97% | 76%
Class E |  |  |  |  |  | 
Overall | 0.05% | 0.07% | 0.05% | 100% | 96% | 73%
Class D | 0.05% | 0.09% | 0.10% | 100% | 98% | 71%
Class F | 0.03% | 0.05% | 0.05% | 100% | 98% | 76%

## Slide 6: Conclusion
Minor BD-rate change on RA, 0.05%
Decoding time reduction 4%
DMVR time was reduced 27%
No change on worst case memory bandwidth
It is proposed to adopt this method into VVC
Thanks to Kwai for crosschecking!

## Slide 7
Thank you!

## Slide 8: Additional Result
Result of DMVR range 2 for all sub-PU
 |  |  | RA |  |  | 
 |  |  | Vs. VTM-6.0 |  |  | 
 | Y | U | V | EncT | DecT | DMVR Time
Class A1 | 0.01% | -0.01% | 0.06% | 100% | 97% | 74%
Class A2 | 0.02% | -0.03% | -0.03% | 100% | 95% | 72%
Class B | 0.00% | 0.04% | -0.01% | 100% | 96% | 73%
Class C | -0.01% | 0.01% | 0.04% | 100% | 98% | 77%
Class E |  |  |  |  |  | 
Overall | 0.00% | 0.01% | 0.01% | 100% | 96% | 74%
Class D | 0.01% | -0.01% | 0.04% | 100% | 98% | 79%
Class F | 0.00% | -0.01% | -0.03% | 100% | 98% | 79%