## Slide 1: Non-CE8: IBC slice level on/off (JVET-P0455)
X. Xu, X. Li, S. Liu (Tencent)
2019/10

## Slide 2: Summary
Currently in VVC CD text/VTM-6.0, the use of IBC mode is controlled by an SPS flag. The following two cases may not be handled properly:
  Scene change within a sequence
  Mixed contents within the same picture
In this contribution, a slice/picture level IBC mode usage control is proposed by checking the value of MaxNumIbcMergeCand
  When MaxNumIbcMergeCand is equal to 0, IBC mode is disabled for the slice/picture
  When MaxNumIbcMergeCand is greater than 0, IBC mode is enabled for the slice/picture
An encoder algorithm using hash hit ratio is also provided to turn on IBC for SCC contents and turn off IBC for natural contents

## Slide 3: Proposed methods
Normative changes:
  Allow MaxNumIbcMergeCand to be equal to 0. When it does, use this to indicate IBC is turned off for the current slice.
Non-normative changes:
  Use slice/picture level hash hit rate ratio to determine if IBC should be turned on or off
  If the ratio is smaller than a threshold (3%), set MaxNumIbcMergeCand be equal to 0 to disable IBC for the current slice

## Slide 4: Spec Text changes
Replace sps_ibc_enabled_flag in Coding unit syntax and semantics with MaxNumIbcMergeCand
Modify the range of MaxNumIbcMergeCand to allow it be equal to 0

## Slide 5: Results
In the CTC, IBC is turned on for Class F (TGM) and turned off for the classes A~E
In the proposed method, almost no BD rate or runtime changes as compared to the CTC

## Slide 6: Conclusion
In this contribution, a slice/picture level IBC on/off control is implemented by setting MaxNumIbcMergeCand equal to non-zero or zero values.
In this way, the use of IBC can be controlled at slice/picture level, with no new syntax element needed.
Simulation results show that there is almost no impact on RD performance or runtime behavior as compared to VTM-6.0 CTC
It is recommended to include this method into the specification
Thanks LGE for performing the crosscheck!