## Slide 1: Non-CE8: On IBC merge list size signaling (JVET-P0457)
X. Xu, X. Li, S. Liu (Tencent)
2019/10

## Slide 2: Summary
Currently in VVC CD text/VTM-6.0, IBC and inter mode have independent merge size signaling at slice level.
  The merge_idx signaling at block level is shared by both inter merge and IBC merge modes.
However, the range of merge index is decided by the value of MaxNumMergeCand while the actual maximum values for the two modes can be different.
  Undefined behaviour can happen if MaxNumIbcMergeCand is greater than MaxNumMergeCand.
Accordingly, three solutions have been proposed as suggested potential fixes.

## Slide 3: Proposed methods
Solution 1:
  The merge size of IBC is limited to be no greater than the merge size of inter
Solution 2:
  The merge_idx range is set to be the larger size of the two lists
Solution 3:
  The merge idx range is switched at block level, depending on the current block’s prediction mode

## Slide 4: Results
Solution 1 vs Solution 3, inter merge size =6; IBC merge size =5
Solution 2 vs Solution 3, inter merge size =5; IBC merge size =6

## Slide 5: Conclusion
Three solutions are suggested to deal with the merge_idx range issue when two list sizes are different for IBC and inter
  Solution 1: Limit the merge size of IBC to be at most the merge size of inter
  Solution 2: The merge_idx range is set to be the larger size of the two lists
  Solution 3: The merge idx range is switched at block level, depending on the current block’s prediction mode
No significant coding performances changes are observed among the three solutions
It is recommended to include one of the three solutions into the specification
Thanks MediaTek for performing crosschecking!

## Slide 6: Additional results
Solution 1 vs solution 3, Inter merge size=6, IBC merge size=2

## Slide 7: Spec changes for solution 1

## Slide 8: Spec changes for solution 2

## Slide 9: Spec changes for solution 3