## Slide 1: CE6-related: Further simplification with new LFNST transform basis
JVET-P0493
Tianyang Zhou
Tomonori Hashimoto Tomohiro Ikai

## Slide 2: Introduction
One aspect is table reduction.
Test1: combination of three tests, CE6-2.1 and CE6-2.2a and CE6-2.3a
The other is further computation reduction by using 16x32 matrices instead of VVC6’s 16x48 and CE6-2.3a’s 16x36 matrices.
Test2: is a combination of CE6-2.2a and 16x32 matrices.
Test3: is a combination of CE6-2.2a and 16x32 matrices without
switched scan order.
Test4: is a combination of CE6-2.2a and CE6-2.1 and 16x32 matrices
without switched scan order.

## Slide 3: Proposed method
In Test2, We propose to use 16x32 matrices. The corresponding position of 32 coefficients are decided depending on lfnstIdx.
In Test3 and Test4, the 32 coefficients only use one pattern.
6
6
6
6
4
4
4
0
{5, 5, 5, 5, 4, 4, 4, 0}
32 coefficients pattern (lfnstIdx == 1)
32 coefficients pattern (lfnstIdx == 2)
8
6
6
6
4
4
1
1
6
6
6
6
4
4
4
0
Type 1 {7, 5, 5, 5, 4, 4, 1, 1}
Type 2 {5, 5, 5, 5, 4, 4, 4, 0}

## Slide 4: Method complexity and Simulation results
 | Reduce mode | Reuse matrix | Reduce matrix | Memory cost (KB) | Computation for 8xN, Nx8 | IO | RA
VTM 6 | - | - | - | 8 | 16x48 | 0 | 0
CE6-2.1 | x | - | - | 6 |  | 0.03 | -0.01
CE6-2.2a | - | X | - | 6 |  | -0.02 | -0.02
CE6-2.3a | - | - | X | 6.7 | 16x36 | 0.02 | 0.03
CE6-2.2c | x | X | - | 4.6 | 16x48 | 0.01 | -0.01
CE6-2.2d | - | X | X | 4.6 | 16x36 | -0.01 | -0.02
Test1 | X | X | X | 3.5 | 16x36 | 0.02 | -0.01
Test2 | - | X | X | 4.1 | 16x32 | 0.01 | 0.01
Test3 | - | X | x *1) | 4.1 | 16x32 | 0.01 | 0.00
Test4 | x | x | x *1) | 3.1 | 16x32 | 0.05 | 0.02
*1) without switched scan order