## Slide 1: JVET-P0497 AHG17: On LMCS Signalling
Yu-Ciao Yang
Geneva, CH
October 2019

## Slide 2: Introduction
Codeword of luma mapping piecewise linear model consists of an absolute delta codeword and a delta sign flag.
Current draft (JVET-O2001-vE) specifies the codeword (lmcsCW[ i ]) shall be in the range of (OrgCW>>3) to (OrgCW<<3 − 1), inclusive. Where OrgCW is equal to (1 << BitDepthY ) / 16
  Delta codeword can be derived in the range of ((OrgCW>>3)- OrgCW) to ((OrgCW<<3 − 1)- OrgCW)
lmcsDeltaCW[ i ] is in the range of -3584 to 28671, when the BitDepthY is equal to 16-bit.
lmcs_data () { | Descriptor
lmcs_min_bin_idx | ue(v)
lmcs_delta_max_bin_idx | ue(v)
lmcs_delta_cw_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_cw[ i ] | u(v)
if ( lmcs_delta_abs_cw[ i ] ) > 0 ) | 
lmcs_delta_sign_cw_flag[ i ] | u(1)
} | 
} | 
lmcsDeltaCW[ i ] = ( 1 − 2 * lmcs_delta_sign_cw_flag[ i ] ) * lmcs_delta_abs_cw[ i ]
lmcsCW[ i ] = OrgCW + lmcsDeltaCW[ i ]

## Slide 3: Proposed First Method – 1/2
The range of negative delta codeword is always less than the range of positive delta codeword.
The delta codeword can be directly derived as a positive value if the absolute delta codeword is greater than a threshold.
  The threshold can be set equal to the absolute minimum delta codeword.
  Threshold = Abs( ((OrgCW>>3) – OrgCW) ) = Abs( 2(BitDepthY-7) – 2(BitDepthY-4) )
The threshold also prevents the piecewise linear model is broken when the absolute delta codeword is greater than the threshold and the delta sign flag is intentionally set as negative at encoder side.
Considering that LMCS APS should be independent of SPS.
  The threshold is set equal to 3584 based on the maximum luma bit-depth.

## Slide 4: Proposed First Method – 2/2
A condition check is added to remove the signalling redundancy and keep the bitstream conformance (highlighted in yellow).
lmcs_data () { | Descriptor
lmcs_min_bin_idx | ue(v)
lmcs_delta_max_bin_idx | ue(v)
lmcs_delta_cw_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_cw[ i ] | u(v)
if ( lmcs_delta_abs_cw[ i ] ) > 0 && lmcs_delta_abs_cw[ i ] <= 3584 ) | 
lmcs_delta_sign_cw_flag[ i ] | u(1)
} | 
} | 

## Slide 5: Proposed Second Method – 1/2
In the current approach of piecewise linear model, there are 16 sign flags at most can be signalled in the LMCS APS.
The delta sign flags may be all the same. Probability is shown as follows:
Second method proposed two additional reference flags to achieve adaptive signalling in LMCS APS if all the delta sign flags are represented as positive or negative.
Test Condition | Total number of LMCS APS | Probability of sign direction |  | 
 |  | All positive | All negative | Others
All Intra | 6628 | 86.72% | 13.28% | 0.00%
Random Access | 1460 | 97.12% | 0.82% | 2.05%

## Slide 6: Proposed Second Method – 2/2
The reference sign signalled flag indicates the sign of all codewords are the same.
The reference sign flag indicates whether the sign of all codewords are positive or negative.
lmcs_data () { | Descriptor
lmcs_min_bin_idx | ue(v)
lmcs_delta_max_bin_idx | ue(v)
lmcs_delta_cw_prec_minus1 | ue(v)
lmcs_reference_sign_signalled_flag | u(1)
if (lmcs_reference_sign_signalled_flag ) | 
lmcs_reference_sign_flag | u(1)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_cw[ i ] | u(v)
if ( lmcs_delta_abs_cw[ i ] ) > 0 && !lmcs_reference_sign_signalled_flag ) | 
lmcs_delta_sign_cw_flag[ i ] | u(1)
} | 
} | 

## Slide 7: Simulation results
There is no experimental result is provided in the first method as there is no 16-bit test sequence in the current CTC. Table 2 shows the simulation results in the second method.
 | All Intra |  |  |  |  | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100% |  |  |  |  | 
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 100% |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 100% | 100% |  |  |  |  | 
Class C | -0.01% | -0.01% | -0.01% | 100% | 100% |  |  |  |  | 
Class E | -0.01% | -0.01% | -0.01% | 100% | 100% |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 100% | 100% |  |  |  |  | 
Class D | -0.02% | -0.02% | -0.02% | 100% | 101% |  |  |  |  | 
Class F | 0.00% | 0.00% | 0.00% | 100% | 99% |  |  |  |  | 

## Slide 8: Conclusion
This contribution proposes two methods on LMCS signalling.
  In the first method, a condition check is added to remove the signalling redundancy and keep the bitstream conformance.
  In the second method, additional reference flags are added to achieve adaptive signalling when all the delta sign flag are the same.
It is suggested to adopt proposed two methods into the next VVC working draft.
Thanks Bytedance for crosscheck

## Slide 9: Thank you!