## Slide 1
JVET-P0525
AHG18: Residual coding selection signaling for lossless VVC
TC Ma, Y.-W. Chen, X. Xiu, H.-J. Jhu, X. Wang (Kwai Inc.)
Z.-Y. Lin, T.-D. Chuang, C.-Y. Chen, C.-W. Hsu, Y.-W. Huang, S. Lei (MediaTek)

## Slide 2: Introduction
In AHG18 SW, residual coding for Transform Skip (TS) is applied with
  Luma BDPCM (BDPCM not implemented)
  transform_skip_flag (not signaled because cu_transquant_bypass)
In this proposal, 4 tests are proposed to select TS or TC
  CU level
  On top CE 8-2.1 (Chroma TS)
  On top CE 8-4.1 (Chroma TS and BDPCM)
  TB level

## Slide 3: Method 1
1 bit CU level signal
  cu_residual_coding_flag
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | AHG18 | TEST |  | AHG18 | TEST |  | AHG18 | TEST | 
Class A1 | 2.2 | 2.2 | -0.16% | 2.3 | 2.5 | XXX% |  |  | 
Class A2 | 1.7 | 1.7 | -0.04% | 1.9 | 1.9 | -0.01% |  |  | 
Class B | 2.1 | 2.1 | 0.07% | 2.3 | 2.3 | 0.00% | 2.3 | XX | XXX%
Class C | 2.1 | 2.1 | 0.01% | 2.6 | 2.6 | -0.05% | 2.6 | 2.6 | -0.05%
Class D | 1.9 | 2.0 | -0.17% | 2.8 | 2.8 | -0.10% | 2.7 | 2.7 | -0.13%
Class E | 2.9 | 2.9 | -0.03% |  |  |  | 3.3 | 3.3 | 0.02%
Class F | 5.5 | 5.6 | -1.18% | 39.4 | 41.1 | -2.63% | 60.6 | 84.7 | -4.15%
TGM | 12.3 | 12.5 | -2.17% | 112.6 | 129.4 | -10.50% | 142.4 | 166.6 | -12.04%
Overall | 2.2 | 2.2 | -0.02% | 2.3 | 2.3 | -0.03% | 2.6 | 1.7 | -0.01%
Enc Time[%] | 186% |  |  | 179% |  |  | #NUM! |  | 
Dec Time[%] | 102% |  |  | 100% |  |  | #NUM! |  | 

## Slide 4: Method 2
On top CE 8-2.1
  By transform_skip_flag
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | AHG18 | TEST |  | AHG18 | TEST |  | AHG18 | TEST | 
Class A1 | 2.2 | 2.2 | -0.18% | 2.3 | 2.3 | -0.10% |  |  | 
Class A2 | 1.7 | 1.7 | 0.00% | 1.9 | 1.9 | XXX% |  |  | 
Class B | 2.1 | 2.1 | -0.05% | 2.3 | 2.3 | -0.03% | 2.3 | 2.3 | -0.03%
Class C | 2.1 | 2.1 | -0.14% | 2.6 | 2.6 | -0.09% | 2.6 | 2.6 | -0.09%
Class D | 1.9 | 2.0 | -0.18% | 2.8 | 2.8 | -0.07% | 2.7 | 2.7 | -0.10%
Class E | 2.9 | 2.9 | -0.33% |  |  |  | 3.3 | 3.3 | 0.00%
Class F | 5.5 | 5.5 | -1.09% | 39.4 | 40.7 | -1.84% | 60.6 | 83.2 | -2.96%
TGM | 12.3 | 12.8 | -3.61% | 112.6 | 115.5 | -2.62% | 142.4 | 146.3 | -2.70%
Overall | 2.2 | 2.2 | -0.13% | 2.3 | 2.2 | -0.05% | 2.5 | 2.3 | -0.04%
Enc Time[%] | 111% |  |  | 113% |  |  | #NUM! |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | #NUM! |  | 

## Slide 5: Method 3
On top CE 8-4.1
  By transform_skip_flag
  Enable TC for BDPCM
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | AHG18 | TEST |  | AHG18 | TEST |  | AHG18 | TEST | 
Class A1 | 2.2 | 2.3 | -1.40% | 2.3 | 2.4 | -0.40% |  |  | 
Class A2 | 1.7 | 1.8 | -1.44% | 1.9 | XX | XXX% |  |  | 
Class B | 2.1 | 2.1 | -1.67% | 2.3 | 2.3 | -0.33% | 2.3 | XX | XXX%
Class C | 2.1 | 2.1 | -1.93% | 2.6 | 2.6 | -0.47% | 2.6 | 2.6 | -0.47%
Class D | 1.9 | 2.0 | -3.25% | 2.8 | 2.8 | -0.69% | 2.7 | 2.8 | -0.61%
Class E | 2.9 | 3.0 | -2.32% |  |  |  | 3.3 | XX | XXX%
Class F | 5.5 | 5.8 | -4.42% | 39.4 | 41.7 | -3.31% | 60.6 | XX | XXX%
TGM | 12.3 | 13.3 | -6.87% | 112.6 | 117.2 | -3.88% | 142.4 | 147.4 | -3.42%
Overall | 2.2 | 2.2 | -1.75% | 2.3 | XX | -0.26% | 2.5 | 0.9 | -0.16%
Enc Time[%] | 117% |  |  | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | 90% |  |  | #NUM! |  |  | #NUM! |  | 

## Slide 6: Method 4
TB level signal
  tb_residual_coding_flag
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | AHG18 | TEST |  | AHG18 | TEST |  | AHG18 | TEST | 
Class A1 | 2.2 | 2.2 | -0.18% | 2.3 | 2.3 | -0.06% |  |  | 
Class A2 | 1.7 | 1.7 | -0.02% | 1.9 | 1.9 | -0.01% |  |  | 
Class B | 2.1 | 2.1 | -0.01% | 2.3 | 2.3 | -0.01% | 2.3 | XX | 0.00%
Class C | 2.1 | 2.1 | -0.04% | 2.6 | 2.6 | -0.02% | 2.6 | 2.6 | -0.02%
Class D | 1.9 | 2.0 | -0.10% | 2.8 | 2.8 | 0.09% | 2.7 | 2.7 | 0.07%
Class E | 2.9 | 2.9 | -0.02% |  |  |  | 3.3 | 3.3 | 0.05%
Class F | 5.5 | 5.5 | -0.99% | 39.4 | 41.0 | -2.22% | 60.6 | 84.4 | -3.86%
TGM | 12.3 | 12.6 | -2.22% | 112.6 | 129.0 | -10.11% | 142.4 | 166.5 | -11.72%
Overall | 2.2 | 2.2 | -0.05% | 2.3 | 2.3 | -0.02% | 2.6 | 1.7 | 0.01%
Enc Time[%] | 196% |  |  | 180% |  |  | #NUM! |  | 
Dec Time[%] | 101% |  |  | 99% |  |  | #NUM! |  | 

## Slide 7: Encoder Complexity Comparison (informative)
Run time | Lossy if qp is 2 (hr) (All Intra/RA/LDB) | Proposed method in test 1 (hr) (All Intra/RA/LDB) | Ratio (%) (All Intra/RA/LDB)
A1 | 15.96/ 270.38 / N/A | 19.86 / 355.41 / N/A | 124% / 131% / N/A
A2 | 22.62/ 413 / N/A | 20.27 / 359.00 / N/A | 89% / 86% / N/A
B | 4.69/ 67.41 / 53.43 | 5.17 / 88.94 / 61.13 | 110% / 131% / 114%
C | 1.09/ 16.96 / 12.81 | 1.04 / 18.35 / 11.74 | 95% / 108% / 92%
D | 0.27/ 3.98 / 2.80 | 0.24 / 4.03 / 2.94 | 90% / 101% / 105%
E | 2.50/ / 29.94 | 2.82 / / 27.02 | 112% / / 90%
F | 2.09/ 11.05 / 9.50 | 2.09 /12.37 / 9.22 | 100% / 115% / 97%
TGM | 3.07/ 8.25 / 7.35 | 2.70/7.95 / 5.71 | 88% / 91% / 77%
Overall | 3.07/ 33.39 / 12.60 | 3.09/ 36.18 / 12.00 | 101%/ 108% / 95%
Test 1 v.s. VVC QP2
First 100 Frames
  w/o Enc Opt. for Test1
Enc Opt. in P0514
  AI: -42% runtime
  RA: -33% runtime
  LDB: -3% runtime

## Slide 8: Result Summary
CTC | AI | RA | LDB | EncT | DecT
Test 1 | -0.02% | -0.03% | -0.01% | 186%/179%/XXX% | 102%/100%/XXX%
Test 2 | -0.13% | -0.05% | -0.04% | 111%/113%/XXX% | 101%/101%/XXX%
Test 3 | -1.75% | -0.26% | -0.16% | 117%/XXX%/XXX% | 90%/XXX%/XXX%
Test 4 | -0.05% | -0.02% | 0.01% | 196%/178%/XXX% | 101%/98%/XXX%
F/TGM | AI | RA | LDB | EncT | DecT
Test 1 | -1.18% -2.17% | -2.63% -10.50% | -4.15% -12.04% | 176%/161%/XXX% | 99%/100%/XXX%
Test 2 | -1.09% -3.61% | -1.84% -2.62% | 2.96% -2.70% | 111%/116%/XXX% | 101%/102%/XXX%
Test 3 | -4.42% -6.87% | -3.31% -3.88% | -4.12% -3.21% | 115%/115%/XXX% | 90%/96% /XXX%
Test 4 | -0.99% -2.22% | -2.22% -10.11% | -3.68% -11.72% | 182%/166%/XXX% | 98%/99%/XXX%

## Slide 9: Thank you Thanks LGE/Tencent/Sony for cross-check