## Slide 1
JVET-P0561
AHG16: Context restriction on CTU boundary for line buffer reduction
Hong-Jheng Jhu, Yi-Wen Chen, Xiaoyu Xiu, Tsung-Chuan Ma, Xianglin Wang

## Slide 2: Introduction
For MIP mode
  To calculate the context index of MIP flag, the MIP flags of both the left and above neighboring blocks are used
For Intra mode
  To calculate the context index of intra mode flag, the intra mode flags of both the left and above neighboring blocks are used
For depth information
  To calculate the context index of quadtree (or called QT) split flag, the QT partition depth of both the left and above neighboring blocks are used
The information of MIP/Intra flag/QT depth needs to be stored in line buffer

## Slide 3: The Proposed Modifications
For MIP/Intra mode
  Context selection for the CABAC coding of MIP/Intra flag is not depending on the MIP/Intra flag of above CU when the above CU is not located in the same CTU as current CU
  In this case, the value of MIP/Intra flag of the above CU can be assumed as 0
For QT partition depth information
  Context selection for the CABAC coding of QT split flag is not depending on the QT partition depth of above CU when the above CU is not in the same CTU as current CU
  In this case, the above CU can be assumed as unavailable CU

## Slide 4: Results of Proposed Modifications
Anchor: VTM-6.0
Test1 : Anchor + proposed modifications
 | All Intra Main10 |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.00% | 0.04% | 98% | 101%
Class A2 | 0.00% | 0.00% | 0.00% | 101% | 105%
Class B | 0.01% | 0.05% | 0.00% | 102% | 104%
Class C | -0.01% | 0.00% | 0.01% | 93% | 93%
Class E | 0.00% | 0.05% | 0.04% | 98% | 98%
Overall | 0.00% | 0.02% | 0.01% | 98% | 100%
Class D | -0.01% | -0.04% | 0.05% | 97% | 91%
Class F | 0.00% | -0.07% | 0.03% | 97% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.08% | -0.02% | 103% | 103%
Class A2 | -0.01% | -0.01% | -0.07% | 101% | 99%
Class B | -0.01% | 0.07% | 0.09% | 99% | 101%
Class C | 0.00% | 0.08% | 0.03% | 96% | 98%
Class E |  |  |  |  | 
Overall | 0.00% | 0.03% | 0.02% | 99% | 100%
Class D | -0.05% | -0.20% | -0.12% | 93% | 94%
Class F | -0.03% | -0.10% | -0.17% | 96% | 97%

## Slide 5: Results of Proposed Modifications
Anchor: VTM-6.0
Test2 : Anchor + proposed modifications
 | Random Access Main 10 |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.06% | 0.01% | 102% | 101%
Class A2 | 0.03% | 0.03% | 0.00% | 103% | 101%
Class B | -0.01% | 0.07% | 0.06% | 102% | 101%
Class C | 0.00% | 0.06% | -0.05% | 99% | 101%
Class E |  |  |  |  | 
Overall | 0.01% | 0.06% | 0.01% | 102% | 101%
Class D | -0.01% | 0.00% | -0.04% | 97% | 95%
Class F | -0.01% | 0.00% | -0.01% | 101% | 99%
 | Low delay B |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | -0.06% | 0.00% | 99% | 98%
Class C | -0.04% | 0.03% | -0.08% | 103% | 101%
Class E | 0.03% | 0.07% | 0.03% | 99% | 104%
Overall | 0.00% | 0.00% | -0.02% | 100% | 100%
Class D | 0.04% | 0.00% | 0.53% | 101% | 103%
Class F | -0.02% | -0.17% | 0.53% | 101% | 99%

## Slide 6: Results of Proposed Modifications
Anchor: VTM-6.0
Test3 : Anchor + proposed modifications
 | All Intra Main10 |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.19% | 0.14% | 99% | 101%
Class A2 | -0.03% | 0.19% | 0.17% | 103% | 101%
Class B | 0.00% | 0.20% | -0.03% | 105% | 104%
Class C | -0.01% | 0.00% | 0.09% | 94% | 86%
Class E | 0.01% | 0.06% | 0.03% | 100% | 99%
Overall | -0.01% | 0.13% | 0.07% | 100% | 98%
Class D | 0.01% | 0.00% | -0.04% | 103% | 99%
Class F | 0.01% | 0.14% | 0.10% | 100% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.02% | 0.03% | 99% | 98%
Class A2 | 0.04% | 0.18% | 0.16% | 98% | 97%
Class B | 0.01% | 0.09% | 0.03% | 100% | 96%
Class C | -0.01% | 0.08% | 0.00% | 103% | 98%
Class E |  |  |  |  | 
Overall | 0.01% | 0.09% | 0.05% | 100% | 97%
Class D | -0.03% | -0.08% | -0.07% | 98% | 93%
Class F | -0.01% | -0.09% | 0.00% | 101% | 96%

## Slide 7: Results of Proposed Modifications
Anchor: VTM-6.0
Test4 : Anchor + proposed modifications (Test1+Test2+Test3)
 | All Intra Main10 |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.15% | 0.13% | 98% | 100%
Class A2 | -0.03% | 0.17% | 0.19% | 96% | 102%
Class B | 0.01% | 0.18% | -0.02% | 103% | 100%
Class C | -0.01% | 0.01% | 0.18% | 100% | 93%
Class E | 0.02% | 0.11% | 0.09% | 101% | 103%
Overall | 0.00% | 0.12% | 0.10% | 100% | 99%
Class D | 0.00% | -0.02% | 0.02% | 101% | 105%
Class F | 0.01% | 0.11% | 0.06% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | 0.00% | 0.05% | 98% | 96%
Class A2 | 0.06% | 0.17% | 0.16% | 98% | 96%
Class B | 0.04% | 0.19% | 0.00% | 102% | 95%
Class C | 0.02% | -0.06% | -0.09% | 111% | 102%
Class E |  |  |  |  | 
Overall | 0.04% | 0.08% | 0.02% | 102% | 97%
Class D | -0.07% | -0.09% | -0.20% | 103% | 97%
Class F | -0.02% | -0.02% | 0.11% | 104% | 98%
 | Low delay B |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.05% | 0.18% | 0.15% | 100% | 104%
Class C | 0.00% | 0.11% | -0.08% | 97% | 101%
Class E | -0.07% | 0.75% | -0.03% | 96% | 101%
Overall | 0.00% | 0.30% | 0.03% | 98% | 102%
Class D | 0.01% | 0.62% | 0.42% | 103% | 100%
Class F | -0.06% | 0.21% | 0.26% | 101% | 98%

## Slide 8: Summary
The tests reduce line buffer without major penalty in terms of coding efficiency
It is recommended to consider adoption of the proposed method into VVC

## Slide 9: Thank you