## Slide 1: JVET-P0597 AHG6/AHG17: Generalized cubemap-based projection syntax for 360-degree videos
Ya-Hsuan Lee, Jian-Liang Lin, Ying-Jui Chen, and Chi-Cheng Ju (MediaTek)
Jill Boyce, and Max Dmitrichenko (Intel)

## Slide 2: Introduction
In 360Lib, there are many cube-based projections which use adjustment functions to change the sampling distribution of the conventional CMP to achieve better compression efficiency.
  EAC, HEC, etc.
HEC
EAC
CMP

## Slide 3: Introduction (cont.)
Hemisphere cubemap projection, which consists of five faces (one full face and four half faces) representing 180⁰ x 180⁰ content, is also supported.
Front
Half Left
Half Right
Half Bottom
Half Top
CMP
HCMP

## Slide 4: Syntax and Semantics

## Slide 5: Syntax
generalized_cmp_projection( payloadSize ) { | Descriptor
generalized_cmp_cancel_flag | u(1)
if( !generalized_cmp_cancel_flag ) { | 
generalized_cmp_persistence_flag | u(1)
cmp_packing_type | u(3)
cmp_mapping_function_type | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
numFaces = ( cmp_packing_type = = 4 ¦ ¦ cmp_packing_type = = 5 ) ? 5 : 6 | 
for( i = 0; i < numFaces; i++ ) { | 
face_index[ i ] | u(3)
face_rotation[ i ] | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
if( cmp_mapping_function_type = = 2 ) { | 
cmp_x_axis_coeff[ i ] | u(7)
cmp_x_axis_y_position_related_flag[ i ] | u(1)
cmp_y_axis_coeff[ i ] | u(7)
cmp_y_axis_x_position_related_flag[ i ] | u(1)
} | 
} | 
cmp_padding_enabled_flag | u(1)
if( cmp_padding_enabled_flag ) { | 
cmp_padding_type | u(1)
cmp_padding_width_minus1 | u(4)
} | 
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
} | 
} | 

## Slide 6: Syntax
generalized_cmp_projection( payloadSize ) { | Descriptor
generalized_cmp_cancel_flag | u(1)
if( !generalized_cmp_cancel_flag ) { | 
generalized_cmp_persistence_flag | u(1)
cmp_packing_type | u(3)
cmp_mapping_function_type | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
numFaces = ( cmp_packing_type = = 4 ¦ ¦ cmp_packing_type = = 5 ) ? 5 : 6 | 
for( i = 0; i < numFaces; i++ ) { | 
face_index[ i ] | u(3)
face_rotation[ i ] | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
if( cmp_mapping_function_type = = 2 ) { | 
cmp_x_axis_coeff[ i ] | u(7)
cmp_x_axis_y_position_related_flag[ i ] | u(1)
cmp_y_axis_coeff[ i ] | u(7)
cmp_y_axis_x_position_related_flag[ i ] | u(1)
} | 
} | 
cmp_padding_enabled_flag | u(1)
if( cmp_padding_enabled_flag ) { | 
cmp_padding_type | u(1)
cmp_padding_width_minus1 | u(4)
} | 
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
} | 
} | 

## Slide 7
cmp_packing_type: [0, 5]
Semantics
cmp_packing_type | Packing type and position index | Face width in luma samples | Face height in luma samples
0 |  | pic_width_in_luma_samples - ( SubWidthC * ( conf_win_left_offset + conf_win_right_offset ) ) | ( pic_height_in_luma_samples - ( SubWidthC * ( conf_win_top_offset + conf_win_bottom_offset ) ) ) / 6
1 |  | ( pic_width_in_luma_samples - ( SubWidthC * ( conf_win_left_offset + conf_win_right_offset ) ) ) / 2 | ( pic_height_in_luma_samples - ( SubWidthC * ( conf_win_top_offset + conf_win_bottom_offset ) ) ) / 3
2 |  | ( pic_width_in_luma_samples - ( SubWidthC * ( conf_win_left_offset + conf_win_right_offset ) ) ) / 3 | ( pic_height_in_luma_samples - ( SubWidthC * ( conf_win_top_offset + conf_win_bottom_offset ) ) ) / 2
3 |  | ( pic_width_in_luma_samples - ( SubWidthC * ( conf_win_left_offset + conf_win_right_offset ) ) ) / 6 | pic_height_in_luma_samples - ( SubWidthC * ( conf_win_top_offset + conf_win_bottom_offset ) )
0
1
2
3
4
5
0
1
2
3
4
5
0
1
2
3
4
5
1
3
5
0
2
4

## Slide 8
cmp_packing_type: [0, 5]
  4 and 5 are hemisphere cubemap
Semantics
cmp_packing_type | Packing type and position index | Face width in luma samples | Face height in luma samples
4 |  | For position 0, 1, 3 and 4, ( pic_width_in_luma_samples - ( SubWidthC * ( conf_win_left_offset + conf_win_right_offset ) ) ) / 6 For position 2, ( pic_width_in_luma_samples - ( SubWidthC * ( conf_win_left_offset + conf_win_right_offset ) ) ) / 3 | pic_height_in_luma_samples - ( SubWidthC * ( conf_win_top_offset + conf_win_bottom_offset ) )
5 |  | pic_width_in_luma_samples - ( SubWidthC * ( conf_win_left_offset + conf_win_right_offset ) ) | For position 0, 1, 3 and 4, ( pic_height_in_luma_samples - ( SubWidthC * ( conf_win_top_offset + conf_win_bottom_offset ) ) ) / 6 For position 2, ( pic_height_in_luma_samples - ( SubWidthC * ( conf_win_top_offset + conf_win_bottom_offset ) ) ) / 3
2
3
4
1
0
1
3
0
4
2

## Slide 9: Syntax
generalized_cmp_projection( payloadSize ) { | Descriptor
generalized_cmp_cancel_flag | u(1)
if( !generalized_cmp_cancel_flag ) { | 
generalized_cmp_persistence_flag | u(1)
cmp_packing_type | u(3)
cmp_mapping_function_type | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
numFaces = ( cmp_packing_type = = 4 ¦ ¦ cmp_packing_type = = 5 ) ? 5 : 6 | 
for( i = 0; i < numFaces; i++ ) { | 
face_index[ i ] | u(3)
face_rotation[ i ] | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
if( cmp_mapping_function_type = = 2 ) { | 
cmp_x_axis_coeff[ i ] | u(7)
cmp_x_axis_y_position_related_flag[ i ] | u(1)
cmp_y_axis_coeff[ i ] | u(7)
cmp_y_axis_x_position_related_flag[ i ] | u(1)
} | 
} | 
cmp_padding_enabled_flag | u(1)
if( cmp_padding_enabled_flag ) { | 
cmp_padding_type | u(1)
cmp_padding_width_minus1 | u(4)
} | 
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
} | 
} | 

## Slide 10
cmp_mapping_function_type: [0, 2]
Semantics
cmp_mapping_function_type | Projection format
0 | CMP
1 | EAC
2 | other mapping functions, signal: cmp_x_axis_coeff[ i ], cmp_y_axis_coeff[ i ], cmp_x_axis_y_position_related_flag[ i ] and cmp_y_axis_x_position_related_flag[ i ]

## Slide 11: Syntax
generalized_cmp_projection( payloadSize ) { | Descriptor
generalized_cmp_cancel_flag | u(1)
if( !generalized_cmp_cancel_flag ) { | 
generalized_cmp_persistence_flag | u(1)
cmp_packing_type | u(3)
cmp_mapping_function_type | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
numFaces = ( cmp_packing_type = = 4 ¦ ¦ cmp_packing_type = = 5 ) ? 5 : 6 | 
for( i = 0; i < numFaces; i++ ) { | 
face_index[ i ] | u(3)
face_rotation[ i ] | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
if( cmp_mapping_function_type = = 2 ) { | 
cmp_x_axis_coeff[ i ] | u(7)
cmp_x_axis_y_position_related_flag[ i ] | u(1)
cmp_y_axis_coeff[ i ] | u(7)
cmp_y_axis_x_position_related_flag[ i ] | u(1)
} | 
} | 
cmp_padding_enabled_flag | u(1)
if( cmp_padding_enabled_flag ) { | 
cmp_padding_type | u(1)
cmp_padding_width_minus1 | u(4)
} | 
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
} | 
} | 

## Slide 12: Semantics
face_index[ i ]: [0, 5]
  same as 360Lib
face_rotation[ i ]: [0, 3]
  same as 360Lib
face_index[ i ] | Corresponding cube face | X | Y | Z
0 | Front face with positive X axis value | 1.0 | −v | −u
1 | Back face with negative X axis value | −1.0 | −v | u
2 | Top face with positive Y axis value | u | 1.0 | v
3 | Bottom face with negative Y axis value | u | −1.0 | −v
4 | Right face with positive Z axis value | u | −v | 1.0
5 | Left face with negative Z axis value | −u | −v | −1.0
face_rotation[ i ] | Rotation angle (counterclockwise)
0 | 0
1 | 90
2 | 180
3 | 270

## Slide 13: Syntax
generalized_cmp_projection( payloadSize ) { | Descriptor
generalized_cmp_cancel_flag | u(1)
if( !generalized_cmp_cancel_flag ) { | 
generalized_cmp_persistence_flag | u(1)
cmp_packing_type | u(3)
cmp_mapping_function_type | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
numFaces = ( cmp_packing_type = = 4 ¦ ¦ cmp_packing_type = = 5 ) ? 5 : 6 | 
for( i = 0; i < numFaces; i++ ) { | 
face_index[ i ] | u(3)
face_rotation[ i ] | u(2)
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
if( cmp_mapping_function_type = = 2 ) { | 
cmp_x_axis_coeff[ i ] | u(7)
cmp_x_axis_y_position_related_flag[ i ] | u(1)
cmp_y_axis_coeff[ i ] | u(7)
cmp_y_axis_x_position_related_flag[ i ] | u(1)
} | 
} | 
cmp_padding_enabled_flag | u(1)
if( cmp_padding_enabled_flag ) { | 
cmp_padding_type | u(1)
cmp_padding_width_minus1 | u(4)
} | 
while( !byte_aligned( ) ) | 
alignment_bit_equal_to_zero /* equal to 0 */ | f(1)
} | 
} | 

## Slide 14: Semantics
cmp_padding_enabled_flag: [0, 1]
cmp_padding_type: [0, 1]
  0: discontinuous edges
  1: discontinuous edges and frame boundaries
cmp_padding_width_minus1: [0, 15]
cmp_packing_type | cmp_padding_type | Location of padding
2 | 0 | 
2 | 1 | 
0
1
2
3
4
5
0
1
2
3
4
5

## Slide 15: Conclusions
The syntax for signaling a generalized cubemap projection is proposed.
  CMP, EAC, and others
Padding of the cubemap projection is also designed in the syntax.