## Slide 1
JVET-P0653
Non-CE4: On BDOF and PROF parameter derivation
Xiaoyu Xiu, Yi-Wen Chen, Tsung-chuan Ma, Hong-Jheng Jhu, Xianglin Wang

## Slide 2: Problem Statement
In VVC draft 6, the bitwise right shifts applied to calculate gradients, correlation parameters and motion refinements, are dependent on the internal bit-depth
The variable bitDepth is set equal to BitDepthY.
The variable shift1 is set to equal to Max( 6, bitDepth − 6 ).
The variable shift2 is set to equal to Max( 4, bitDepth − 8 ).
The variable shift3 is set to equal to Max( 1, bitDepth − 11 ).
The variable shift4 is set equal to Max( 3, 15 − bitDepth ) and the variable offset4 is set equal to 1 << ( shift4 − 1 ).
The variable mvRefineThres is set equal to 1 << Max( 5, bitDepth − 7 ).

## Slide 3: Problem Statement
After the adoption of JVET-O0304, the multiplications during the BDOF correlation derivation are removed
sGx2 = ij Abs( tempH[ xSb + i ][ ySb + j ] ) with i, j = −1..4 (8‑810)
sGy2 = ij Abs( tempV[ xSb + i ][ ySb + j ] ) with i, j = −1..4 (8‑811)
sGxGy = ij( Sign( tempV[ xSb + i ][ ySb + j ] ) * tempH[ xSb + i ][ ySb + j ] ) with i, j = −1..4 (8‑812)
sGxGym = sGxGy >> 12 (8‑813)
sGxGys = sGxGy & ( ( 1 << 12 ) − 1 ) (8‑814)
sGxdI = ij( − Sign( tempH[ xSb + i ][ ySb + j ] ) * diff[ xSb + i ][ ySb + j ] ) with i, j = −1..4 (8‑815)
sGydI = ij( − Sign( tempV[ xSb + i ][ ySb + j ] ) * diff[ xSb + i ][ ySb + j ] ) with i, j = −1..4 (8‑816)
Such change not only reduces computational complexity but also lower the dynamic range of BDOF derivation

## Slide 4: Proposal
Two modifications are proposed
  Remove the dependency of internal bit-depth on calculating the bitwise right shifts for the BDOF and PROF parameter calculation
The variable bitDepth is set equal to BitDepthY.
The variable shift1 is set to equal to Max( 6, bitDepth − 6 )6.
The variable shift2 is set to equal to Max( 4, bitDepth − 8 )4.
The variable shift3 is set to equal to Max( 1, bitDepth − 11 )1.
The variable shift4 is set equal to Max( 3, 15 − bitDepth ) and the variable offset4 is set equal to 1 << ( shift4 − 1 ).
The variable mvRefineThres is set equal to 1 << Max( 5, bitDepth − 7 )5.
  CE4-2.1: change the precision of the PROF motion refinement from 1/64-pel to 1/32-pel and clip to the range [-32, 31]

## Slide 5: Proposal
Operation | Parameter | BDOF |  | PROF | 
 |  | Range | Bit-width | Range | Bit-width
Prediction samples | predSampleL0, predSampleL1 | [-25085, 25079] | 16 | [-25085, 25079] | 16
Gradient calculation | gradientHL0, gradientVL0 gradientHL1, gradientVL1 | [-784, 783] | 11 | [-784, 783] | 11
Correlation parameter calculation | diff | [-3135, 3135] | 13 | N/A | N/A
 | tempH, tempV | [-784, 783] | 11 | N/A | N/A
 | sGx2, sGy2 | [0, 28224] | 16 | N/A | N/A
 | sGxGy | [-28224, 28224] | 16 | N/A | N/A
 | sGxdI, sGydI | [-112860, 112860] | 18 | N/A | N/A
Motion refinement | vx, vy | [-32, 31] | 6 | [-32, 31] | 6
Sample refinement | dI | [-50144, 48576] | 17 | [-50144, 48576] | 17
Table 1 Bit-widths of internal parameters of BDOF and PROF, internal bit-depth 8- to 12-bit

## Slide 6: Proposal
Operation | Parameter | BDOF |  | PROF | 
 |  | Range | Bit-width | Range | Bit-width
Prediction samples | predSampleL0, predSampleL1 | [-75773, 124919] | 18 | [-75773, 124919] | 18
Gradient calculation | gradientHL0, gradientVL0 gradientHL1, gradientVL1 | [-3136, 3135] | 13 | [-3136, 3135] | 13
Correlation parameter calculation | diff | [-12543, 12543] | 15 | N/A | N/A
 | tempH, tempV | [-3136,3135] | 13 | N/A | N/A
 | sGx2, sGy2 | [0,112896] | 18 | N/A | N/A
 | sGxGy | [-112896, 112896] | 18 | N/A | N/A
 | sGxdI, sGydI | [-451548, 451548] | 20 | N/A | N/A
Motion refinement | vx, vy | [-32, 31] | 6 | [-32, 31] | 6
Sample refinement | dI | [-50144, 48576] | 19 | [-50144, 48576] | 19
Table 2 Bit-widths of internal parameters of BDOF and PROF, internal bit-depth 14-bit

## Slide 7: Proposal
Operation | Parameter | BDOF |  | PROF |  | 
 |  | Range | Bit-width | Range | Bit-width | 
Prediction samples | predSampleL0, predSampleL1 | [-278525, 524279] | 20 | [-278525, 524279] | 20 | 
Gradient calculation | gradientHL0, gradientVL0 gradientHL1, gradientVL1 | [-12544, 12543] | 15 | [-12544, 12543] | 15 | 
Correlation parameter calculation | diff | [-50175, 50175] | 17 | N/A | N/A | 
 | tempH, tempV | [-12544, 12543] | 15 | N/A | N/A | 
 | sGx2, sGy2 | [0, 451584] | 20 | N/A | N/A | 
 | sGxGy | [-451584, 451584] | 20 | N/A | N/A | 
 | sGxdI, sGydI | [-1806300, 1806300] | 22 | N/A | N/A | 
Motion refinement | vx, vy | [-32, 31] | 6 | [-32, 31] | 6 | 
Sample refinement | dI | [-802784, 777696] | 21 | [-802784, 777696] | 21 | 
Table 3 Bit-widths of internal parameters of BDOF and PROF, internal bit-depth 16-bit

## Slide 8: Simulation
Removal of the dependency of right shifts on bitdepth for BDOF

## Slide 9: Simulation
Removal of the dependency of right shifts on bitdepth + CE4-2.1

## Slide 10: Thank you