## Slide 1: CE5 Subjective test results
Andrey Norkin

## Slide 2: Test Setup
Procedure as CE5 test at last meeting [JVET-O1118]
LG OLED 55” display used, three test subjects per session at 1.6 × screen height distance
A-B-A-B presentation, assessment:
  “A was much better than B”
  “A was better than B”
  “B was better than A”
  “B was much better than A”.
Test cell design
  “A” – Video A – “B” – Video B – “A” – Video A – “B” – Video B – “Vote N”
  “A” / “B” presentation for 0.5sec
  Voting for 5sec

## Slide 3: Test Design
Placement of anchor and proposal as “A” and “B” randomized
Fixed order of sequences, looped over available test cells
QP values and tests have been randomized
Mix of sequences which have various resolutions
  All sequences have been up-scaled to UHD screen resolution using nearest neighbor interpolation

## Slide 4: Test Evaluation
Viewing votes mapping
  +3 : “Proposal much better than anchor”
  +1 : “Proposal better than anchor”
  -1 : “Anchor better than proposal”
  -3 : “Anchor much better than proposal”
Calculation of Mean Opinion Score (MOS) on this scale
Calculation of 95% confidence intervals based on MOS and standard deviation

## Slide 5: Overview of viewing sessions
CE5-2.1 Cross component ALF, in-loop filter
DMVR boundaries deblocking: CE5-1.1.2 (DMVR filtering + restriction on hor. CTU boundary) CE5-1.1.3 (DMVR off)
CE5-1.2: Aligning deblocking chroma decisions CE5-1.3: Longer tap deblocking at hor. CTU boundaries
CE5-3.1 Bilateral filter + SAO, RDO on CE5-3.2 Hadamard filter + SAO, RDO on

## Slide 6: CE5 Viewing Results
Test conducted on Sun. 2019-10-06
8 groups of three experts (4 groups for session 1 and 2, different 4 groups for sessions 3 and 4)
10-12 min viewing time per one viewing session, two sessions per group
12 test subjects total for each test case

## Slide 7: 1. CE5-2.1 Cross-component ALF

## Slide 8
Chart: 
| Redkayak | Cactus | KristenAndSara | FourPeople | Kimono YCbCr 4:4:4
 | -0.16667 | 0.16667 | -0.16667 | 0.66667 | 0.16667

## Slide 9
Chart: 
| Redkayak | Cactus | KristenAndSara | FourPeople | Kimono YCbCr 4:4:4
 | 0 | -0.33333 | -0.83333 | -0.33333 | -0.33333

## Slide 10: 2. DMVR boundaries deblocking
CE5-1.1.2 (DMVR filtering + restriction on hor. CTU boundary)
CE5-1.1.3 (DMVR off)

## Slide 11
Chart: 
| CE05-1-1-2 | CE05-1-1-3
 | -0.5 | -0.16667

## Slide 12
Chart: 
| CE05-1-1-2 | CE05-1-1-3
 | -0.33333 | 0

## Slide 13
Chart: 
| CE05-1-1-2 | CE05-1-1-3
 | 0.33333 | -0.5

## Slide 14
Chart: 
| CE05-1-1-2 | CE05-1-1-3
 | 0.66667 | -0.33333

## Slide 15
Chart: 
| CE05-1-1-2 | CE05-1-1-3
 | -0.33333 | 0.33333

## Slide 16
Chart: 
| CE05-1-1-2 | CE05-1-1-3
 | 0.33333 | -0.33333

## Slide 17: 3. Chroma deblocking
CE5-1.2: Aligning deblocking chroma decision
CE5-1.3: Longer tap chroma deblocking at hor. CTU boundaries

## Slide 18
Chart: 
| Campfire | Cactus | KristenAndSara
 | -0.5 | -0.16667 | 0.16667

## Slide 19
Chart: 
| Campfire | Cactus | KristenAndSara
 | 0.66667 | -1.1667 | -0.33333

## Slide 20
Chart: 
| Campfire | Kimono YCbCr 4:4:4 | CrowdRun YCbCr 4:4:4
 | -0.16667 | 0.5 | -0.16667

## Slide 21
Chart: 
| Campfire | Kimono YCbCr 4:4:4 | CrowdRun YCbCr 4:4:4
 | 0.33333 | 0.5 | 0.16667

## Slide 22: 4. Loop filters
CE5-3.1 Bilateral filter (+ SAO, RDO on)
CE5-3.2 Hadamard filter (+SAO, RDO on)

## Slide 23
Chart: 
| CE05-3-1 | CE05-3-2
 | -0.16667 | 0

## Slide 24
Chart: 
| CE05-3-1 | CE05-3-2
 | 0.33333 | 0.16667

## Slide 25
Chart: 
| CE05-3-1 | CE05-3-2
 | 0.5 | -0.33333

## Slide 26
Chart: 
| CE05-3-1 | CE05-3-2
 | 0.66667 | 0.16667

## Slide 27
Chart: 
| CE05-3-1 | CE05-3-2
 | 0 | 0

## Slide 28
Chart: 
| CE05-3-1 | CE05-3-2
 | -0.16667 | 0.66667