## Slide 1
JVET-Q0124 CE5-related:
JC-CCALF with Power of 2 Weight Values
Che-Wei Kuo, Jingya Li, Chong Soon Lim

## Slide 2: Introduction
JC-CCALF in CE5-3.2
  removes multiplication in CCALF refinement value derivation
  halves filtering operations by weight multiplication in Cr refinement value derivation
SAO Luma
ALF Luma
SAO Cb
SAO Cr
Joint chroma
CC ALF
ALF Cb
Y
Cb
Cr
w
ALF Cr

## Slide 3: Introduction
Weight candidates in P0372 & CE5-3.2
Applying these weights requires multiplication or division, and they can be replaced by power of 2 values without coding loss
Sign | Index | 1 | 2 | 3 | 4 | 5 | 6 | 7
± | ¦ w ¦ | 1/4 | 1/2 | 3/4 | 1 | 4 | 2 | 4/3
Sign | Index | 1 | 2 | 3 | 4 | 5 | 6 | 7
± | ¦ w ¦ | 1/4 | 1/2 | 3/4 | 1 | 4 | 2 | 3/2

## Slide 4: Proposal
Propose to use power of 2 values for JC-CCALF weight candidates, to avoid multiplication or division in Cr refinement value derivation
  Method 1: w = ±1
  Method 2: w = ±1/8, ±1/4, ±1/2, ±1, ±2, ±4, ±8, and ±16
Simulation results
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV | Y | U | V | YUV
CCALF (CE5 anchor) | 0.17% | -8.31% | -7.06% | -1.40% | 0.14% | -10.14% | -9.82% | -1.88% | 0.12% | -13.00% | -9.48% | -2.15%
JC-CCALF (CE5-3.2) | 0.10% | -5.84% | -4.87% | -0.99% | 0.16% | -8.63% | -8.27% | -1.56% | 0.12% | -12.71% | -9.47% | -2.12%
weights = ±1 | 0.10% | -6.15% | -5.02% | -1.04% | 0.15% | -9.05% | -8.73% | -1.66% | 0.12% | -12.86% | -9.89% | -2.18%
weights = ±1/8 to ±16 | 0.10% | -6.06% | -5.09% | -1.04% | 0.14% | -8.91% | -8.56% | -1.64% | 0.12% | -12.88% | -9.83% | -2.17%

## Slide 5: Simulation Results
CE5-3.2 v.s. Method 1
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.12% | -3.87% | -3.37% | -0.63% | 101% | 101%
Class A2 | 0.08% | -4.89% | -9.46% | -1.37% | 101% | 102%
Class B | 0.08% | -10.03% | -6.87% | -1.62% | 101% | 101%
Class C | 0.08% | -2.97% | -2.79% | -0.51% | 101% | 101%
Class E | 0.12% | -7.50% | -2.14% | -0.87% | 101% | 101%
Overall | 0.10% | -6.15% | -5.02% | -1.04% | 101% | 101%
Class D | 0.07% | -3.02% | -1.86% | -0.43% | 101% | 99%
Class F | 0.07% | -4.63% | -4.99% | -0.91% | 101% | 101%
TGM | 0.04% | -3.97% | -3.78% | -0.75% | 100% | 101%
 | Random Access Main 10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.14% | -5.11% | -4.66% | -0.87% | 101% | 101%
Class A2 | 0.14% | -9.31% | -13.97% | -2.21% | 102% | 102%
Class B | 0.21% | -15.34% | -12.37% | -2.61% | 101% | 101%
Class C | 0.09% | -3.93% | -3.28% | -0.65% | 100% | 101%
Class E |  |  |  |  |  | 
Overall | 0.15% | -9.05% | -8.73% | -1.66% | 101% | 101%
Class D | 0.08% | -4.07% | -3.30% | -0.68% | 100% | 101%
Class F | 0.10% | -3.52% | -3.60% | -0.63% | 100% | 101%
TGM | 0.26% | -4.55% | -4.74% | -0.72% | 101% | 101%
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.14% | -18.70% | -16.89% | -3.45% | 100% | 101%
Class C | 0.15% | -5.41% | -4.43% | -0.86% | 100% | 100%
Class E | 0.07% | -13.07% | -5.50% | -1.80% | 100% | 100%
Overall | 0.12% | -12.86% | -9.89% | -2.18% | 100% | 101%
Class D | 0.02% | -5.16% | -4.20% | -0.92% | 100% | 100%
Class F | 0.00% | -7.93% | -6.58% | -1.45% | 100% | 100%
TGM | -0.14% | -6.33% | -5.86% | -1.33% | 100% | 101%
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.12% | -2.97% | -3.95% | -0.60% | 99% | 99%
Class A2 | 0.07% | -3.76% | -9.08% | -1.23% | 99% | 99%
Class B | 0.09% | -9.55% | -6.23% | -1.51% | 99% | 98%
Class C | 0.10% | -2.96% | -2.91% | -0.51% | 99% | 90%
Class E | 0.14% | -8.42% | -1.90% | -0.92% | 99% | 94%
Overall | 0.10% | -5.84% | -4.87% | -0.99% | 99% | 96%
Class D | 0.07% | -2.57% | -1.85% | -0.39% | 99% | 94%
Class F | 0.06% | -4.30% | -4.75% | -0.86% | 100% | 94%
 | Random access Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.13% | -4.86% | -4.50% | -0.83% | 100% | 100%
Class A2 | 0.16% | -7.88% | -13.37% | -2.00% | 100% | 101%
Class B | 0.22% | -15.02% | -11.45% | -2.47% | 100% | 99%
Class C | 0.10% | -4.01% | -3.31% | -0.65% | 100% | 100%
Class E |  |  |  |  |  | 
Overall | 0.16% | -8.63% | -8.27% | -1.56% | 100% | 100%
Class D | 0.04% | -4.17% | -2.79% | -0.66% | 100% | 100%
Class F | 0.11% | -2.92% | -3.06% | -0.51% | 100% | 100%
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.16% | -18.38% | -16.05% | -3.32% | 100% | 101%
Class C | 0.11% | -5.26% | -4.33% | -0.87% | 100% | 99%
Class E | 0.09% | -13.18% | -5.35% | -1.78% | 100% | 100%
Overall | 0.12% | -12.71% | -9.47% | -2.12% | 100% | 100%
Class D | 0.09% | -5.71% | -4.43% | -0.94% | 100% | 98%
Class F | 0.17% | -7.89% | -6.17% | -1.27% | 100% | 100%

## Slide 6: Simulation Results
Method 1 & Method 2
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.12% | -3.87% | -3.37% | -0.63% | 101% | 101%
Class A2 | 0.08% | -4.89% | -9.46% | -1.37% | 101% | 102%
Class B | 0.08% | -10.03% | -6.87% | -1.62% | 101% | 101%
Class C | 0.08% | -2.97% | -2.79% | -0.51% | 101% | 101%
Class E | 0.12% | -7.50% | -2.14% | -0.87% | 101% | 101%
Overall | 0.10% | -6.15% | -5.02% | -1.04% | 101% | 101%
Class D | 0.07% | -3.02% | -1.86% | -0.43% | 101% | 99%
Class F | 0.07% | -4.63% | -4.99% | -0.91% | 101% | 101%
TGM | 0.04% | -3.97% | -3.78% | -0.75% | 100% | 101%
 | Random Access Main 10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.14% | -5.11% | -4.66% | -0.87% | 101% | 101%
Class A2 | 0.14% | -9.31% | -13.97% | -2.21% | 102% | 102%
Class B | 0.21% | -15.34% | -12.37% | -2.61% | 101% | 101%
Class C | 0.09% | -3.93% | -3.28% | -0.65% | 100% | 101%
Class E |  |  |  |  |  | 
Overall | 0.15% | -9.05% | -8.73% | -1.66% | 101% | 101%
Class D | 0.08% | -4.07% | -3.30% | -0.68% | 100% | 101%
Class F | 0.10% | -3.52% | -3.60% | -0.63% | 100% | 101%
TGM | 0.26% | -4.55% | -4.74% | -0.72% | 101% | 101%
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.14% | -18.70% | -16.89% | -3.45% | 100% | 101%
Class C | 0.15% | -5.41% | -4.43% | -0.86% | 100% | 100%
Class E | 0.07% | -13.07% | -5.50% | -1.80% | 100% | 100%
Overall | 0.12% | -12.86% | -9.89% | -2.18% | 100% | 101%
Class D | 0.02% | -5.16% | -4.20% | -0.92% | 100% | 100%
Class F | 0.00% | -7.93% | -6.58% | -1.45% | 100% | 100%
TGM | -0.14% | -6.33% | -5.86% | -1.33% | 100% | 101%
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.12% | -3.48% | -3.79% | -0.63% | 101% | 102%
Class A2 | 0.08% | -4.87% | -9.75% | -1.40% | 101% | 102%
Class B | 0.08% | -9.47% | -6.68% | -1.55% | 101% | 102%
Class C | 0.09% | -3.01% | -2.89% | -0.52% | 101% | 102%
Class E | 0.13% | -8.24% | -2.01% | -0.92% | 101% | 101%
Overall | 0.10% | -6.06% | -5.09% | -1.04% | 101% | 102%
Class D | 0.07% | -2.54% | -1.86% | -0.39% | 100% | 99%
Class F | 0.06% | -4.53% | -4.70% | -0.87% | 101% | 101%
TGM | 0.03% | -4.14% | -3.69% | -0.76% | 100% | 101%
 | Random Access Main 10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.13% | -5.00% | -4.73% | -0.87% | 101% | 101%
Class A2 | 0.14% | -9.02% | -13.96% | -2.19% | 100% | 101%
Class B | 0.18% | -15.13% | -11.84% | -2.55% | 100% | 101%
Class C | 0.08% | -3.96% | -3.27% | -0.66% | 100% | 101%
Class E |  |  |  |  |  | 
Overall | 0.14% | -8.91% | -8.56% | -1.64% | 100% | 101%
Class D | 0.05% | -3.99% | -2.95% | -0.65% | 100% | 100%
Class F | 0.10% | -3.10% | -3.06% | -0.53% | 100% | 101%
TGM | 0.19% | -4.04% | -4.44% | -0.70% | 100% | 101%
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.16% | -18.70% | -16.56% | -3.40% | 101% | 101%
Class C | 0.12% | -5.42% | -4.33% | -0.87% | 100% | 100%
Class E | 0.07% | -13.12% | -5.94% | -1.85% | 101% | 100%
Overall | 0.12% | -12.88% | -9.83% | -2.17% | 101% | 101%
Class D | 0.11% | -5.90% | -4.38% | -0.94% | 100% | 100%
Class F | 0.03% | -7.67% | -5.76% | -1.32% | 100% | 100%
TGM | -0.14% | -6.20% | -5.70% | -1.30% | 101% | 101%

## Slide 7: Simulation Results
Method 1 & 2 on CE5 Anchor
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | -0.05% | 1.16% | 2.08% | 0.29% | 87% | 90%
Class A2 | -0.03% | 3.45% | 3.29% | 0.65% | 85% | 90%
Class B | -0.07% | 3.76% | 4.41% | 0.77% | 86% | 87%
Class C | -0.11% | 0.99% | 0.85% | 0.10% | 85% | 77%
Class E | -0.12% | 2.34% | 0.33% | 0.17% | 81% | 74%
Overall | -0.08% | 2.43% | 2.36% | 0.42% | 85% | 83%
Class D | -0.03% | 0.43% | -0.13% | 0.01% | 80% | 64%
Class F | -0.09% | 1.36% | 1.15% | 0.18% | 87% | 78%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Random Access Main 10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.01% | 0.66% | 1.52% | 0.23% | 84% | 100%
Class A2 | 0.03% | 1.95% | 2.40% | 0.46% | 87% | 102%
Class B | 0.03% | 2.48% | 1.48% | 0.42% | 84% | 99%
Class C | -0.04% | -0.04% | 0.06% | -0.03% | 84% | 96%
Class E |  |  |  |  |  | 
Overall | 0.01% | 1.34% | 1.30% | 0.27% | 85% | 99%
Class D | -0.02% | -0.19% | -0.41% | -0.08% | 89% | 105%
Class F | -0.06% | 0.44% | 0.26% | 0.02% | 100% | 103%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | -0.03% | 0.83% | 0.52% | 0.11% | 87% | 98%
Class C | 0.06% | -0.15% | -0.65% | -0.03% | 77% | 93%
Class E | -0.03% | -0.26% | -1.56% | -0.20% | 78% | 93%
Overall | 0.00% | 0.23% | -0.39% | -0.02% | 81% | 95%
Class D | -0.06% | -0.56% | -1.17% | -0.22% | 82% | 95%
Class F | -0.09% | 0.10% | -0.09% | -0.07% | 82% | 94%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | -0.05% | 1.58% | 1.62% | 0.28% | 88% | 91%
Class A2 | -0.03% | 3.50% | 2.90% | 0.61% | 85% | 90%
Class B | -0.07% | 4.40% | 4.67% | 0.86% | 86% | 88%
Class C | -0.10% | 0.95% | 0.75% | 0.09% | 85% | 78%
Class E | -0.11% | 1.53% | 0.46% | 0.11% | 81% | 74%
Overall | -0.07% | 2.54% | 2.29% | 0.42% | 85% | 84%
Class D | -0.03% | 0.98% | -0.12% | 0.06% | 79% | 64%
Class F | -0.10% | 1.46% | 1.46% | 0.21% | 87% | 78%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Random Access Main 10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.01% | 0.78% | 1.45% | 0.23% | 84% | 100%
Class A2 | 0.02% | 2.31% | 2.45% | 0.49% | 85% | 101%
Class B | 0.01% | 2.72% | 2.24% | 0.50% | 84% | 98%
Class C | -0.05% | -0.07% | 0.07% | -0.04% | 84% | 96%
Class E |  |  |  |  |  | 
Overall | 0.00% | 1.50% | 1.55% | 0.30% | 84% | 99%
Class D | -0.04% | -0.11% | -0.03% | -0.05% | 89% | 105%
Class F | -0.06% | 0.88% | 0.84% | 0.12% | 100% | 103%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | -0.01% | 0.85% | 1.01% | 0.18% | 87% | 98%
Class C | 0.03% | -0.15% | -0.56% | -0.05% | 78% | 93%
Class E | -0.03% | -0.33% | -2.01% | -0.26% | 78% | 93%
Overall | 0.00% | 0.22% | -0.27% | 0.00% | 82% | 95%
Class D | 0.03% | -1.41% | -1.38% | -0.25% | 82% | 96%
Class F | -0.06% | 0.35% | 0.74% | 0.06% | 82% | 94%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 8: Conclusion
Propose to use power of 2 values for JC-CCALF weight candidates, to avoid multiplication or division in Cr refinement value derivation
Compared with the original JC-CCALF with weight multiplication, method 1 reduces the number of candidates from 14 to 2, and only sign change is needed
Thanks Kwai for cross-checking