## Slide 1
JVET-Q0125 CE5-related:
JC-CCALF with Alternative Filter Weight
Che-Wei Kuo, Jingya Li, Chong Soon Lim

## Slide 2: Introduction
JC-CCALF in CE5-3.2
  removes multiplication in Cb refinement value derivation
  halves filtering operations by weight multiplication in Cr refinement value derivation
Alternative filters for CCALF are tested in CE5 anchor, to adapt different content in the same slice
Motivation: JC-CCALF weight is essentially part of filter coefficients and need to be included in alternative filter design

## Slide 3: Proposal
Propose to use individual JC-CCALF filter weight for each alternative filter (as filter coefficients)
  A filter weight map to indicate 4 weights for 4 filters in SH
  Current CTU selects the filter weight according to the filter index.
  No further signaling overhead.
  Simplification: the weight map only includes sign flag changes, e.g., +--+, w = +1, -1, -1, +1
Simulation results
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV | Y | U | V | YUV
CCALF (CE5 anchor) | 0.17% | -8.31% | -7.06% | -1.40% | 0.14% | -10.14% | -9.82% | -1.88% | 0.12% | -13.00% | -9.48% | -2.15%
JC-CCALF (CE5-3.2) | 0.10% | -5.84% | -4.87% | -0.99% | 0.16% | -8.63% | -8.27% | -1.56% | 0.12% | -12.71% | -9.47% | -2.12%
alternative filter weight | 0.10% | -6.65% | -5.56% | -1.14% | 0.15% | -9.39% | -9.16% | -1.74% | 0.11% | -13.03% | -10.11% | -2.22%

## Slide 4: Simulation Results
CE5-3.2 v.s. Q0125
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.12% | -4.06% | -3.61% | -0.67% | 102% | 101%
Class A2 | 0.08% | -5.46% | -10.29% | -1.51% | 102% | 101%
Class B | 0.09% | -10.73% | -7.77% | -1.78% | 101% | 101%
Class C | 0.08% | -3.31% | -3.22% | -0.59% | 101% | 102%
Class E | 0.11% | -8.04% | -2.20% | -0.93% | 101% | 101%
Overall | 0.10% | -6.65% | -5.56% | -1.14% | 101% | 101%
Class D | 0.07% | -3.23% | -2.05% | -0.47% | 101% | 100%
Class F | 0.07% | -4.89% | -5.40% | -0.97% | 101% | 101%
TGM | 0.04% | -4.04% | -3.87% | -0.76% | 100% | 101%
 | Random Access Main 10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.14% | -5.37% | -5.22% | -0.95% | 101% | 100%
Class A2 | 0.15% | -9.47% | -14.53% | -2.28% | 101% | 101%
Class B | 0.20% | -16.01% | -12.84% | -2.72% | 101% | 101%
Class C | 0.08% | -4.08% | -3.49% | -0.69% | 101% | 101%
Class E |  |  |  |  |  | 
Overall | 0.15% | -9.39% | -9.16% | -1.74% | 101% | 101%
Class D | 0.05% | -4.37% | -3.41% | -0.73% | 101% | 100%
Class F | 0.11% | -3.68% | -3.76% | -0.66% | 101% | 101%
TGM | 0.27% | -4.78% | -4.94% | -0.76% | 101% | 101%
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.15% | -19.05% | -17.17% | -3.50% | 101% | 101%
Class C | 0.15% | -5.42% | -4.50% | -0.87% | 101% | 100%
Class E | -0.01% | -13.14% | -5.83% | -1.90% | 102% | 100%
Overall | 0.11% | -13.03% | -10.11% | -2.22% | 101% | 101%
Class D | 0.08% | -5.99% | -4.32% | -0.97% | 100% | 100%
Class F | 0.06% | -8.02% | -6.15% | -1.37% | 101% | 100%
TGM | -0.15% | -6.45% | -6.02% | -1.37% | 101% | 101%
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.12% | -2.97% | -3.95% | -0.60% | 99% | 99%
Class A2 | 0.07% | -3.76% | -9.08% | -1.23% | 99% | 99%
Class B | 0.09% | -9.55% | -6.23% | -1.51% | 99% | 98%
Class C | 0.10% | -2.96% | -2.91% | -0.51% | 99% | 90%
Class E | 0.14% | -8.42% | -1.90% | -0.92% | 99% | 94%
Overall | 0.10% | -5.84% | -4.87% | -0.99% | 99% | 96%
Class D | 0.07% | -2.57% | -1.85% | -0.39% | 99% | 94%
Class F | 0.06% | -4.30% | -4.75% | -0.86% | 100% | 94%
 | Random access Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.13% | -4.86% | -4.50% | -0.83% | 100% | 100%
Class A2 | 0.16% | -7.88% | -13.37% | -2.00% | 100% | 101%
Class B | 0.22% | -15.02% | -11.45% | -2.47% | 100% | 99%
Class C | 0.10% | -4.01% | -3.31% | -0.65% | 100% | 100%
Class E |  |  |  |  |  | 
Overall | 0.16% | -8.63% | -8.27% | -1.56% | 100% | 100%
Class D | 0.04% | -4.17% | -2.79% | -0.66% | 100% | 100%
Class F | 0.11% | -2.92% | -3.06% | -0.51% | 100% | 100%
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.16% | -18.38% | -16.05% | -3.32% | 100% | 101%
Class C | 0.11% | -5.26% | -4.33% | -0.87% | 100% | 99%
Class E | 0.09% | -13.18% | -5.35% | -1.78% | 100% | 100%
Overall | 0.12% | -12.71% | -9.47% | -2.12% | 100% | 100%
Class D | 0.09% | -5.71% | -4.43% | -0.94% | 100% | 98%
Class F | 0.17% | -7.89% | -6.17% | -1.27% | 100% | 100%

## Slide 5: Simulation Results
CE5 anchor v.s. Q0125
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.12% | -4.06% | -3.61% | -0.67% | 102% | 101%
Class A2 | 0.08% | -5.46% | -10.29% | -1.51% | 102% | 101%
Class B | 0.09% | -10.73% | -7.77% | -1.78% | 101% | 101%
Class C | 0.08% | -3.31% | -3.22% | -0.59% | 101% | 102%
Class E | 0.11% | -8.04% | -2.20% | -0.93% | 101% | 101%
Overall | 0.10% | -6.65% | -5.56% | -1.14% | 101% | 101%
Class D | 0.07% | -3.23% | -2.05% | -0.47% | 101% | 100%
Class F | 0.07% | -4.89% | -5.40% | -0.97% | 101% | 101%
TGM | 0.04% | -4.04% | -3.87% | -0.76% | 100% | 101%
 | Random Access Main 10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.14% | -5.37% | -5.22% | -0.95% | 101% | 100%
Class A2 | 0.15% | -9.47% | -14.53% | -2.28% | 101% | 101%
Class B | 0.20% | -16.01% | -12.84% | -2.72% | 101% | 101%
Class C | 0.08% | -4.08% | -3.49% | -0.69% | 101% | 101%
Class E |  |  |  |  |  | 
Overall | 0.15% | -9.39% | -9.16% | -1.74% | 101% | 101%
Class D | 0.05% | -4.37% | -3.41% | -0.73% | 101% | 100%
Class F | 0.11% | -3.68% | -3.76% | -0.66% | 101% | 101%
TGM | 0.27% | -4.78% | -4.94% | -0.76% | 101% | 101%
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.15% | -19.05% | -17.17% | -3.50% | 101% | 101%
Class C | 0.15% | -5.42% | -4.50% | -0.87% | 101% | 100%
Class E | -0.01% | -13.14% | -5.83% | -1.90% | 102% | 100%
Overall | 0.11% | -13.03% | -10.11% | -2.22% | 101% | 101%
Class D | 0.08% | -5.99% | -4.32% | -0.97% | 100% | 100%
Class F | 0.06% | -8.02% | -6.15% | -1.37% | 101% | 100%
TGM | -0.15% | -6.45% | -6.02% | -1.37% | 101% | 101%
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV* | EncT | DecT
Class A1 | 0.17% | -4.94% | -5.31% | -0.89% | 99% | 101%
Class A2 | 0.11% | -7.94% | -12.25% | -1.93% | 99% | 102%
Class B | 0.15% | -13.28% | -10.55% | -2.26% | 99% | 102%
Class C | 0.19% | -3.92% | -3.59% | -0.60% | 99% | 101%
Class E | 0.24% | -9.63% | -2.44% | -1.01% | 99% | 102%
Overall | 0.17% | -8.31% | -7.06% | -1.40% | 99% | 101%
Class D | 0.10% | -3.39% | -1.70% | -0.43% | 100% | 100%
Class F | 0.16% | -5.87% | -6.05% | -1.06% | 100% | 101%
 | Random access Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV* | EncT | DecT
Class A1 | 0.12% | -5.69% | -6.08% | -1.08% | 102% | 101%
Class A2 | 0.12% | -10.99% | -16.01% | -2.61% | 102% | 99%
Class B | 0.17% | -17.31% | -13.53% | -2.94% | 101% | 101%
Class C | 0.13% | -3.89% | -3.33% | -0.62% | 103% | 102%
Class E |  |  |  |  |  | 
Overall | 0.14% | -10.14% | -9.82% | -1.88% | 102% | 101%
Class D | 0.10% | -3.86% | -2.91% | -0.60% | 101% | 99%
Class F | 0.16% | -3.93% | -3.85% | -0.65% | 99% | 100%
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV* | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.16% | -19.28% | -17.34% | -3.53% | 95% | 97%
Class C | 0.09% | -5.27% | -3.79% | -0.83% | 102% | 98%
Class E | 0.10% | -12.85% | -3.99% | -1.61% | 101% | 99%
Overall | 0.12% | -13.00% | -9.48% | -2.15% | 99% | 98%
Class D | 0.08% | -4.58% | -3.12% | -0.71% | 102% | 101%
Class F | 0.09% | -8.02% | -6.50% | -1.38% | 100% | 99%

## Slide 6: Simulation Results
Q0125 on CE5 Anchor
 | All Intra Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | -0.05% | 0.96% | 1.82% | 0.24% | 88% | 91%
Class A2 | -0.03% | 2.82% | 2.28% | 0.48% | 85% | 89%
Class B | -0.06% | 2.93% | 3.30% | 0.57% | 86% | 87%
Class C | -0.11% | 0.63% | 0.39% | 0.02% | 85% | 78%
Class E | -0.13% | 1.75% | 0.26% | 0.10% | 81% | 74%
Overall | -0.08% | 1.88% | 1.73% | 0.30% | 85% | 84%
Class D | -0.03% | 0.22% | -0.31% | -0.03% | 80% | 64%
Class F | -0.09% | 1.08% | 0.70% | 0.11% | 87% | 78%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Random Access Main 10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.02% | 0.38% | 0.93% | 0.14% | 85% | 100%
Class A2 | 0.03% | 1.79% | 1.73% | 0.38% | 86% | 101%
Class B | 0.03% | 1.66% | 0.91% | 0.28% | 84% | 98%
Class C | -0.05% | -0.19% | -0.15% | -0.07% | 84% | 96%
Class E |  |  |  |  |  | 
Overall | 0.01% | 0.94% | 0.79% | 0.18% | 85% | 98%
Class D | -0.04% | -0.51% | -0.52% | -0.14% | 89% | 104%
Class F | -0.05% | 0.28% | 0.09% | 0.00% | 101% | 103%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM-7.0 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | -0.01% | 0.38% | 0.30% | 0.06% | 88% | 98%
Class C | 0.06% | -0.16% | -0.73% | -0.04% | 78% | 93%
Class E | -0.10% | -0.34% | -1.90% | -0.31% | 79% | 94%
Overall | -0.01% | 0.02% | -0.60% | -0.07% | 82% | 95%
Class D | 0.00% | -1.45% | -1.24% | -0.27% | 82% | 96%
Class F | -0.03% | -0.01% | 0.36% | 0.01% | 83% | 93%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 7: Conclusion
Propose to use individual JC-CCALF filter weight for each alternative filter (as part of filter coefficients)
Halves CCALF complexity while preserving 93% RA gains, when combined with CE5-3.2
Coding gains come from various filter options with minor signaling overhead in SH
Thanks InterDigital for cross-checking