## Slide 1: Separate transform skip checking of Luma and Chroma for LFNST index signalling (JVET-Q0138)
Moonmo Koo, Jaehyun Kim, Mehdi Salehifar, and Seung Hwan Kim

## Slide 2: Summary [1/2]
Motivation
  In the 16th JVET meeting, chroma transform skip mode was adopted.
  However, LFNST index signaling for chroma separate tree still depends on collocated luma transform skip flag in VVC WD.
    Also reported through JVET bug tracker ticket #720
coding_unit( x0, y0, cbWidth, cbHeight, cqtDepth, treeType, modeType ) {
……
if( Min( lfnstWidth, lfnstHeight ) >= 4 && sps_lfnst_enabled_flag = = 1 && CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && transform_skip_flag[ x0 ][ y0 ][ 0 ] = = 0 && ( treeType != DUAL_TREE_CHROMA ¦ ¦ !intra_mip_flag[ x0 ][ y0 ] ¦ ¦ Min( lfnstWidth, lfnstHeight ) >= 16 ) && Max( cbWidth, cbHeight ) <= MaxTbSizeY) {
if( ( IntraSubPartitionsSplitType != ISP_NO_SPLIT ¦ ¦ LfnstDcOnly = = 0 ) && LfnstZeroOutSigCoeffFlag = = 1 )
lfnst_idx
}
……

## Slide 3: Summary [2/2]
Proposed methods
  Method 1: if one or any components are not coded by transform skip, the index is signaled.
    Can be described implicitly and most concisely through LfnstDcOnly
  Method 2: minimal fix only for chroma separate tree
    Separate tree: same as Method 1 through LfnstDcOnly
    Single tree: same as the current WD
      LFNST index can be signaled only if luma transform skip flag is equal to 0,
coding_unit( x0, y0, cbWidth, cbHeight, cqtDepth, treeType, modeType ) {
……
LfnstDcOnly = 1
……
if( Min( lfnstWidth, lfnstHeight ) >= 4 && sps_lfnst_enabled_flag = = 1 && CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && transform_skip_flag[ x0 ][ y0 ][ 0 ] = = 0 && ( treeType = = DUAL_TREE_CHROMA ¦ ¦ !intra_mip_flag[ x0 ][ y0 ] ¦ ¦ Min( lfnstWidth, lfnstHeight ) >= 16 ) && Max( cbWidth, cbHeight ) <= MaxTbSizeY) {
if( ( IntraSubPartitionsSplitType != ISP_NO_SPLIT ¦ ¦ LfnstDcOnly = = 0 ) && LfnstZeroOutSigCoeffFlag = = 1 )
lfnst_idx
}
……
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
……
if( lastSubBlock = = 0 && log2TbWidth >= 2 && log2TbHeight >= 2 && !transform_skip_flag[ x0 ][ y0 ][ cIdx ] && lastScanPos > 0 )
LfnstDcOnly = 0
……
 LfnstDcOnly can be updated only in non-transform skip case. Otherwise, residual_ts_coding is invoked.

## Slide 4: Conclusion
Experimental results (BD-rate/EncT/DecT) with VTM 7.0 anchor under CTC
  Method 1: 0.00%/100%/100% (AI) and 0.00%/100%/99% (RA)
  Method 2: 0.00%/101%/102% (AI) and 0.00%/100%/100% (RA)
No effective changes in both coding gain and complexity
It is recommended that one of the two proposed fixes should be adopted in next VTM and VVC WD.
Thanks to Canon and KDDI for cross-checking

## Slide 5: Appendix – Suggested spec text changes for Method 1
coding_unit( x0, y0, cbWidth, cbHeight, cqtDepth, treeType, modeType ) {
……
LfnstDcOnly = 1
……
if( Min( lfnstWidth, lfnstHeight ) >= 4 && sps_lfnst_enabled_flag = = 1 && CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && transform_skip_flag[ x0 ][ y0 ][ 0 ] = = 0 && ( treeType = = DUAL_TREE_CHROMA ¦ ¦ !intra_mip_flag[ x0 ][ y0 ] ¦ ¦ Min( lfnstWidth, lfnstHeight ) >= 16 ) && Max( cbWidth, cbHeight ) <= MaxTbSizeY) {
if( ( IntraSubPartitionsSplitType != ISP_NO_SPLIT ¦ ¦ LfnstDcOnly = = 0 ) && LfnstZeroOutSigCoeffFlag = = 1 )
lfnst_idx
}
……
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
……
if( lastSubBlock = = 0 && log2TbWidth >= 2 && log2TbHeight >= 2 && !transform_skip_flag[ x0 ][ y0 ][ cIdx ] && lastScanPos > 0 )
LfnstDcOnly = 0
……
8.7.4. Transformation process for scaled transform coefficients 8.7.4.1 General …… When lfnst_idx is not equal to 0 and transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 0 and both nTbW and nTbH are greater than or equal to 4, the following applies: ……

## Slide 6: Appendix – Suggested spec text changes for Method 2
coding_unit( x0, y0, cbWidth, cbHeight, cqtDepth, treeType, modeType ) {
……
LfnstDcOnly = 1
……
if( Min( lfnstWidth, lfnstHeight ) >= 4 && sps_lfnst_enabled_flag = = 1 && CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && ( treeType != SINGLE_TREE ¦ ¦ transform_skip_flag[ x0 ][ y0 ][ 0 ] = = 0 ) && ( treeType = = DUAL_TREE_CHROMA ¦ ¦ !intra_mip_flag[ x0 ][ y0 ] ¦ ¦ Min( lfnstWidth, lfnstHeight ) >= 16 ) && Max( cbWidth, cbHeight ) <= MaxTbSizeY) {
if( ( IntraSubPartitionsSplitType != ISP_NO_SPLIT ¦ ¦ LfnstDcOnly = = 0 ) && LfnstZeroOutSigCoeffFlag = = 1 )
lfnst_idx
}
……
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
……
if( lastSubBlock = = 0 && log2TbWidth >= 2 && log2TbHeight >= 2 && !transform_skip_flag[ x0 ][ y0 ][ cIdx ] && lastScanPos > 0 )
LfnstDcOnly = 0
……
8.7.4. Transformation process for scaled transform coefficients 8.7.4.1 General …… When lfnst_idx is not equal to 0 and transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 0 and both nTbW and nTbH are greater than or equal to 4, the following applies: ……

## Slide 7: Appendix – Experimental results
Method 1
Method 2
Config. | BD-rate |  |  | EncT | DecT
 | Y | U | V |  | 
AI | 0.00% | 0.01% | 0.01% | 100% | 100%
RA | 0.00% | 0.00% | 0.04% | 100% | 99%
Config. | BD-rate |  |  | EncT | DecT
 | Y | U | V |  | 
AI | 0.00% | 0.01% | 0.01% | 101% | 102%
RA | 0.00% | 0.00% | 0.06% | 101% | 100%