## Slide 1: JVET-Q0165 CE5-related: On the CC-ALF filtering process
Zhi Zhang
Ericsson
2020-01-08

## Slide 2: CC-ALF filtering process in CE5
A residual correction is derived by applying a 3×4 diamond-shape filter to the co-located luma samples centered at the chroma sample to be refined
  8 unique coefficients in CE5 anchor
    Coefficients values ranges between [-32, 31], inclusive
    Each coefficient but is estimated in the encoder side
    and then clipped to the range [-32, 31], inclusive
  8 unique coefficients in CE5-2
    Coefficients values restrict to have values either 0 or power-of-two
    Each coefficient is estimated in the encoder side

## Slide 3: DC-neutral problem and solution
DC-neutral problem due to the clipping / restriction of the coefficient values
  DC-neutral, coefficients sum to zero:
  If not DC-neutral, CC-ALF filtering modifies chroma even if luma is flat
  Encoder coefficient optimization tends to select DC-neutral filter sets
Guarantee DC-neutral CC-ALF filter
  Signal 7 unique CC-ALF coefficients, skip
  Apply coefficients to the delta values of the co-located luma samples
CTC AI configuration | DC-neutral filter sets | Total numer of filter sets
CE5 anchor | 27620 | 27636
CE5-2.1 | 28221 | 28231
CE5-2.2 | 29099 | 29207

## Slide 4: Modified CC-ALF filtering process
A residual correction is derived by applying 7 unique CC-ALF coefficients to the delta values of the co-located luma samples centered at the chroma sample to be refined
  DC-neutral guarantee CC-ALF filter
Actual weight applied to the
  Does not need to be restricted to be in the range of [-32, 31] or have a value of power-of-two

## Slide 5: Advantage on top of CE5-2 multiplication removal
In CE5-2, the CC-ALF coefficients are restricted to have a value of either 0 or power-of-two, the number of coefficients combination that guarantee DC-neutral is much less (0.6% for CE5-2.1 and 3.2% for CE5-2.2) than the total number of coefficients combination
In the modified CC-ALF filtering process on top of CE5-2, all coefficients combination guarantee DC-neutral
  The number of DC-neutral coefficients combinations is 9.8x over CE5-2.1
  The number of DC-neutral coefficients combinations is 3.4x over CE5-2.2
 | Nr. Combinations Total | Nr. Combinations DC-neutral | Rate
CE5-2.1 | 2 562 890 625 | 16 089 375 ( A ) | B ∕ A = 9.8
Modified CE5-2.1 | 170 859 375 | 157 657 497 ( B ) | 
CE5-2.2 | 43 046 721 | 1 402 689 ( C ) | D ∕ C = 3.4
Modified CE5-2.2 | 4 782 969 | 4 782 969 ( D ) | 

## Slide 6: Simulation results
Modified CC-ALF filtering process on top of CE5 anchor
Modified CC-ALF filtering process on top of CE5-2.1
Modified CC-ALF filtering process on top of CE5-2.2
Over CE5-Anchor |  |  |  | 
 | Y | U | V | YUV
All Intra | 0.00% | -0.11% | -0.15% | -0.03%
Random Access | 0.01% | -0.18% | -0.11% | -0.03%
Low delay B | -0.04% | -0.26% | -0.35% | -0.09%
 | Over CE5-Anchor |  |  |  | Over CE5-2.1 |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV
All Intra | -0.02% | -0.02% | -0.19% | -0.04% | 0.00% | -0.55% | -0.54% | -0.11%
Random Access | 0.00% | -0.28% | -0.31% | -0.06% | -0.02% | -0.36% | -0.37% | -0.09%
Low delay B | 0.03% | -0.51% | -0.63% | -0.09% | 0.03% | -0.27% | -0.50% | -0.05%
 | Over CE5-Anchor |  |  |  | Over CE5-2.2 |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV
All Intra | -0.03% | 0.15% | -0.06% | -0.02% | 0.00% | -0.58% | -0.65% | -0.12%
Random Access | -0.01% | -0.13% | -0.13% | -0.03% | -0.01% | -0.47% | -0.57% | -0.12%
Low delay B | 0.00% | -0.55% | -0.63% | -0.12% | -0.01% | -0.47% | -0.53% | -0.11%