## Slide 1: CE5-related: CCALF filter for 4:2:2 and 4:4:4 color format (JVET-Q0301)
Jangwon Choi

## Slide 2: Summary
Background and problem statement
  8-tap 3x4 diamond CCALF filter is designed for 4:2:0 chroma sample structure
Proposed method
  Simplify CCALF filter for 4:2:2 and 4:4:4 chroma sample structure
    CCALF filter shape is reduced to 3x3 diamond (square 5-tap) in 4:2:2 and 4:4:4 color format
    Symmetrical luma samples can be used for the chroma refinement
    CCALF operations could be reduced by 38% without any syntax change of the CCALF common base
Experimental results with 4:4:4 YUV test condition, based on CCALF common base anchor
    Y, Cb, Cr / -0.01%, 0.15%, 0.16% (AI) / -0.02%, 0.17%, 0.22% (RA) / 0.02%, 0.36%, 0.26% (LDB)
Thanks to Tencent for cross-checking

## Slide 3: Proposed method
Square 3x3 diamond filter (5-tap) is introduced for CCALF in 4:2:2 and 4:4:4 color format
  Chroma sample can be refined using co-located neighbor 5 luma symmetry samples
  CCALF operation complexity for 4:2:2 and 4:4:4 color format could be reduced by 38%
4:2:0, 4:2:2, and 4:4:4 chroma format sampling structure and associated 3x4 diamond filter
4:2:2, and 4:4:4 chroma format sampling structure and associated proposed 3x3 diamond filter

## Slide 4: Proposed method
For the minimal change of the draft text of CCALF common base, only some semantics are added
  8 filter coefficients of CCALF are always decoded, but only 5 filter coefficients are used for CCALF in 4:2:2 and 4:4:4 color format

## Slide 5: Experimental Results
Experimental results with 4:4:4 YUV test condition, based on CCALF common base anchor

## Slide 6: Experimental Results
Experimental results with 4:4:4 YUV test condition, based on VTM7.0 anchor

## Slide 7: Conclusion
This contribution proposes to use 3x3 diamond CCALF filter shape for 4:2:2 and 4:4:4 color format.
  The proposed method provides the symmetrical CCALF filtering in 4:2:2 and 4:4:4 color format with the reduced computational complexity.