## Slide 1: Simplified contexts in intra prediction (JVET-Q0302)
Jangwon Choi

## Slide 2: Summary
Background and problem statement
  Theoretically, context coded bins provides better coding performance compared to bypass coded bins because it can estimate the probability more accurately.
  However, it requires more computational complex and delay to estimate the probability so that the number of context coded bins determines throughput efficiency of the system
Proposed method
  Simplify contexts in some intra prediction tools
    Method 1: all bins of cclm_mode_idx are coded in bypass mode
    Method 2: second bin of intra_luma_ref_idx is coded in bypass mode
    Method 3: intra_subpartitions_split_flag is coded in bypass mode
Experimental results (AI, based on VTM7.0 anchor)
    Method 1: Y 0.01%, Cb -0.08%, Cr -0.06%
    Method 2: Y 0.01%, Cb -0.05%. Cr 0.02%
    Method 3: Y 0.01%, Cb 0.00%. Cr 0.02%
Thanks to Tencent for cross-checking

## Slide 3: Proposed method 1
All bins of cclm_mode_idx are coded in the bypass mode
  In the current VVC, first bin of cclm_mode_idx is coded with 1 context model, and the second bin is coded with bypass mode
  To simplify the contexts of cclm_mode_idx, two bins of cclm_mode_idx are coded in bypass mode

## Slide 4: Proposed method 2
Second bin of intra_luma_ref_idx is coded in the bypass mode
  In the current VVC, first bin of intra_luma_ref_idx is coded with 1 context model, and the second bin is also coded with 1 context model
  To simplify the contexts of intra_luma_ref_idx without coding loss, second bin of intra_luma_ref_idx is coded in bypass mode

## Slide 5: Proposed method 3
intra_subpartitions_split_flag is coded in the bypass mode
  In the current VVC, intra_subpartitions_split_flag is coded with 1 context model
  To simplify the contexts of intra_subpartitions_split_flag, it is coded in bypass mode

## Slide 6: Experimental Results
Method 1

## Slide 7: Experimental Results
Method 2

## Slide 8: Experimental Results
Method 3

## Slide 9: Conclusion
In this proposal, three methods of simplified context are proposed to reduce the CABAC data throughput in the parsing of intra prediction syntax with the negligible coding performance change.