## Slide 1: JVET-Q0334 AhG8/AhG12: On the reference picture resampling for the subpictures
​Yao-Jen Chang, Vadim Seregin, Muhammed Coban, Marta Karczewicz
​
​Brussels, Belgium
​Jan. 2020

## Slide 2: Summary
Support RPR and the subpicture to be enabled at the same time.
Proposed to maintain two types of the picture scaling processes
  The regular picture uses the scaling window to derive the scaling ratio (VVC 7)
  When the subpicture is treated as a picture, the subpicture uses the subpicture scaling window to derive the scaling ratio (Q0333)

## Slide 3: Use case
RPR for regular pictures
  Reference picture resampling (RPR) supports an adaptive streaming in an open group of picture (GOP) prediction structure (starting with CRA picture)
  This gets a better compression performance and better subjectively visual quality compared to a traditionally closed GOP prediction structure.
RPR for subpictures
  This allows an adaptive subpicture streaming in an open GOP prediction structure, and share the same benefits that are already in regular picture when RPR is used
Figures from JVET-M0259

## Slide 4: Scaling ratio for regular picture
Current picture
Reference picture
The scaling ratio is derived by the scaling windows cropped from the reference picture and the current picture
  refPicOutW / curPicOutW
  refPicOutH / curPicOutH
Scaling
window
curPicOutW
refPicOutW
refPicOutH
curPicOutH

## Slide 5: Scaling ratio for subpictures
When the subpicture is treated as a picture, the scaling ratio is derived by the subpicture scaling windows cropped from the reference subpicture and the current subpicture
  refSubpicOutW[ i ] / curSubpicOutW[ j ]
  refSubpicOutH[ i ] / curSubpicOutH[ j ]
1
2
3
1
2
3
Reference picture
Current picture
refSubpicOutW[ i ]
refSubpicOutH[ i ]
curSubpicOutH[ j ]
curSubpicOutW[ j ]
Subpicture
Scaling
window

## Slide 6: Signaling of the design
Each subpicture signals a scaling window flag. If enabled, the scaling window offsets are signaled.
  The number of subpictures shall be first signaled to loop a group of the scaling window parameters.
Subpicture scaling window parameters can be signaled in both PPS and PH. The scaling window for the i-th subpicture derived from PH can override the scaling window derived from PPS.
  This proposal also supports to signal the subpicture scaling windows at either PPS or PH only
PPS
scaling_window_flag | u(1)
if( scaling_window_flag ) { | 
scaling_win_left_offset | ue(v)
scaling_win_right_offset | ue(v)
scaling_win_top_offset | ue(v)
scaling_win_bottom_offset | ue(v)
} | 
pps_num_subpics_minus1 | ue(v)
for( i = 0; i <= pps_num_subpics_minus1; i++ ) { | 
pps_scaling_window_flag[ i ] | u(1)
if( pps_scaling_window_flag[ i ] ) { | 
pps_scaling_win_left_offset[ i ] | ue(v)
pps_scaling_win_right_offset[ i ] | ue(v)
pps_scaling_win_top_offset[ i ] | ue(v)
pps_scaling_win_bottom_offset[ i ] | ue(v)
} | 
} | 

## Slide 8: Two types of the scaling ratios
Scaling ratio derivation for regular picture (VVC 7)
  fRefWidth is set equal to PicOutputWidthL of the reference picture RefPicList[ i ][ j ] in luma samples
  fRefHeight is set equal to PicOutputHeightL of the reference picture RefPicList[ i ][ j ] in luma samples
  RefPicScale[ i ][ j ][ 0 ] = ( ( fRefWidth << 14 ) + ( PicOutputWidthL >> 1 ) ) / PicOutputWidthL
  RefPicScale[ i ][ j ][ 1 ] = ( ( fRefHeight << 14 ) + ( PicOutputHeightL >> 1 ) ) / PicOutputHeightL
Scaling ratio derivation for subpictures (Q0333)
  fRefWidth is set equal to PicOutputWidthL[ RefSubPicIdx ] of the reference picture RefPicList[ i ][ j ] in luma samples
  fRefHeight is set equal to PicOutputHeightL[ RefSubPicIdx ] of the reference picture RefPicList[ i ][ j ] in luma samples
  RefPicScale[ i ][ j ][ 0 ] = ( ( fRefWidth << 14 ) + ( PicOutputWidthL[ SubPicIdx ] >> 1 ) ) / PicOutputWidthL[ SubPicIdx ]
  RefPicScale[ i ][ j ][ 1 ] = ( ( fRefHeight << 14 ) + ( PicOutputHeightL[ SubPicIdx ] >> 1 ) ) / PicOutputHeightL[ SubPicIdx ]
SubPicIdx is derived to be such that SubpicIdList[ SubPicIdx ] of the current picture is equal to slice_subpic_id of the current slice
RefSubPicIdx is derived to be such that SubpicIdList[ RefSubPicIdx ] of the reference picture is equal to slice_subpic_id of the current picture

## Slide 9: Constraints on the design
The value of pps_scaling_window_flag[ i ] shall be inferred to be 0 if at least one of the following conditions is true
  The i-th subpicture is not treated as a picture
  Subpicture ID list is not reordered in the CLVS
  Subpicture functionality is disabled
PPS
scaling_window_flag | u(1)
if( scaling_window_flag ) { | 
scaling_win_left_offset | ue(v)
scaling_win_right_offset | ue(v)
scaling_win_top_offset | ue(v)
scaling_win_bottom_offset | ue(v)
} | 
pps_num_subpics_minus1 | ue(v)
for( i = 0; i <= pps_num_subpics_minus1; i++ ) { | 
pps_scaling_window_flag[ i ] | u(1)
if( pps_scaling_window_flag[ i ] ) { | 
pps_scaling_win_left_offset[ i ] | ue(v)
pps_scaling_win_right_offset[ i ] | ue(v)
pps_scaling_win_top_offset[ i ] | ue(v)
pps_scaling_win_bottom_offset[ i ] | ue(v)
} | 
} |