## Slide 1: JVET-Q0340 Non-CE4: Cleanup of the MMVD offset derivation
N. Park, J. Nam, H. Jang, J. Lim, S. Kim

## Slide 2: Introduction
MMVD offset is scaled when both reference picture is short-term reference pictures and the distance between current picture and reference picture of the each direction is different.
The range of the MMVD offset is [−211, 211] by the followings.
mmvd_distance_idx[ x0 ][ y0 ] | MmvdDistance[ x0 ][ y0 ] | 
 | pic_fpel_mmvd_enabled_flag = = 0 | pic_fpel_mmvd_enabled_flag = = 1
0 | 1 | 4
1 | 2 | 8
2 | 4 | 16
3 | 8 | 32
4 | 16 | 64
5 | 32 | 128
6 | 64 | 256
7 | 128 | 512
MmvdOffset[ x0 ][ y0 ][ 0 ] = ( MmvdDistance[ x0 ][ y0 ] << 2 ) * MmvdSign[ x0 ][ y0 ][0]
MmvdOffset[ x0 ][ y0 ][ 1 ] = ( MmvdDistance[ x0 ][ y0 ] << 2 ) * MmvdSign[ x0 ][ y0 ][1]

## Slide 3: Proposed method
MMVD offset is scaled in range of [ −215, 215 ] by distScaleFactor, which is clipped within [-4096, 4095]
Since the maximum value of the scaled MVD cannot exceed the range of the MVD, clipping operation is not necessary.
Following cleanup is proposed.
td = Clip3( −128, 127, currPocDiffL0 ) (572) tb = Clip3( −128, 127, currPocDiffL1 ) (573) tx = ( 16384 + ( Abs( td ) >> 1 ) ) / td (574) distScaleFactor = Clip3( −4096, 4095, ( tb * tx + 32 ) >> 6 ) (575) mMvdL1[ 0 ] = Clip3( −217, 217 − 1, (distScaleFactor * mMvdL0[ 0 ] + (576) 128 − ( distScaleFactor * mMvdL0[ 0 ] >= 0 ) ) >> 8 ) mMvdL1[ 1 ] = Clip3( −217, 217 − 1, (distScaleFactor * mMvdL0[ 1 ] + (577) 128 − ( distScaleFactor * mMvdL0[ 1 ] >= 0 ) ) >> 8 )
(distScaleFactor * mvd + 128 –(1)) >> 8 = (212 * 211 + 128) / 28 = 215

## Slide 4: Conclusion
In this contribution, cleanup of the MMVD offset derivation process is proposed.
The experimental results reportedly show no changes.
It is recommended to consider this method in the next VTM.