## Slide 1: JVET-Q0341 Non-CE4: Range of the motion vector
N. Park, J. Nam, H. Jang, J. Lim, S. Kim

## Slide 2: Introduction
In HEVC,
  The motion vector range is defined as 16-bit signed integer, [2^15, 2^15 – 1].
  If a motion vector exceeds the range, wrapping operation is applied for INTER mode.
  Wrapping operation for INTER mode was adopted in Stockholm meeting for HEVC (J Meeting)
Followings were commented:
It was remarked that there is clipping in MV scaling process. Having a clipping in MV derivation process would be consistent with the MV scaling process.
It was remarked that additional clipping is burden for decoders and unnecessary.

## Slide 3: Introduction
In current VVC,
  The motion vector range is defined as 18-bit signed integer, [2^17, 2^17 – 1].
  If a motion vector exceeds the range, two different operations are applied according to coding mode.
    Wrapping operation (using modulo) is used for INTER mode
    Clipping operation is used for general MERGE mode
Category | Mode | HEVC | VVC
INTER | IBC |  | Wrapping
 | AFFINE |  | Wrapping (CPMV) Clipping (Sub-block MV)
 | INTER | Wrapping | Wrapping
MERGE | IBC |  | N/A
 | AFFINE |  | Clipping (Sub-block MV)
 | Regular merge | N/A | N/A
 | MMVD |  | Clipping
 | CIIP |  | N/A
 | TPM |  | N/A
 | DMVR |  | Clipping

## Slide 4: Proposed method
In this proposal, the methods of the range control are unified.
  In the method #1, clipping operation is used for all cases.
  In the method #2, wrapping operation is used for all cases.
Category | Mode | VVC | Method #1 | Method #2
INTER | IBC | Wrapping | Clipping | Wrapping
 | AFFINE | Wrapping (CPMV) Clipping (Sub-block MV) | Clipping (CPMV) Clipping (Sub-block MV) | Wrapping (CPMV) Wrapping (Sub-block MV)
 | INTER | Wrapping | Clipping | Wrapping
MERGE | IBC | N/A | N/A | N/A
 | AFFINE | Clipping (Sub-block MV) | Clipping (Sub-block MV) | Wrapping (Sub-block MV)
 | Regular merge | N/A | N/A | N/A
 | MMVD | Clipping | Clipping | Wrapping
 | CIIP | N/A | N/A | N/A
 | TPM | N/A | N/A | N/A
 | DMVR | Clipping | Clipping | Wrapping

## Slide 5: Proposed method
Behaviors changed by applying the clipping operation
MVP : 2^17-1
MVD : 1
MV : -2^17
MVP : 2^17-1
MVD : 1
MV : -2^17
MVP : 2^17-1
MVD : 1
MVP : 2^17-1
MVD : 1
MV : 2^17-1
MV : -2^17 - 1
[Example 1]

## Slide 6: Proposed method
Behaviors changed by applying the clipping operation
[Example 2]
MVP : 2^17-1
MVD : 2^17-1
MV : -2
MVP : 2^17-1
MVD : 2^17-1
MV : 2^17-1

## Slide 7: Conclusion
In this contribution, unified range control methods are proposed.
  In extreme cases, It can control the motion vector to more reasonable range.
  It can unify the motion vector control for all INTER/MERGE mode.
It is recommended to consider this method1 in the next VTM.