## Slide 1
CE4-related: Geometric partitioning signaling
JVET-Q0429
T. Poirier, F. Le Léannec, F. Urban, A. Robert

## Slide 2: CE4-related: Geometric partition signaling JVET-Q0429
In VTM-7.0, geometric merge mode a total of 4 distances and 24 angles are used
  1 index is coded and a look-up table is used to derive distance and angle
Proposal: separate the coding of distance and angle
Test 1
  Distance use 2 bypass bins
  Angle use Truncated Binary with 24 values (10 for distance 0)
if( !ciip_flag[ x0 ][ y0 ] && MaxNumGeoMergeCand > 1 ) { | 
merge_geo_partition_idx[ x0 ][ y0 ] | ae(v)
merge_geo_partition_distance_idx | ae(v)
merge_geo_partition_angle_idx | ae(v)
merge_geo_idx0[ x0 ][ y0 ] | ae(v)
if( MaxNumGeoMergeCand > 2 ) | 
merge_geo_idx1[ x0 ][ y0 ] | ae(v)
} | 

## Slide 3: CE4-related: Geometric partition signaling JVET-Q0429
Test 2
  Distance use 2 bypass bins
  Angle use a coding tree

## Slide 4: CE4-related: Geometric partition signaling JVET-Q0429
Test 1 results (vs CE4_common_base)
 | Random access Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.07% | 0.05% | 84% | 69%
Class A2 | 0.01% | 0.04% | -0.05% | 83% | 70%
Class B | 0.00% | 0.00% | 0.04% | 82% | 69%
Class C | -0.01% | 0.14% | 0.05% | 82% | 67%
Class E |  |  |  |  | 
Overall | 0.00% | 0.03% | 0.02% | 83% | 69%
Class D | 0.01% | -0.09% | 0.18% | 81% | 63%
Class F | 0.02% | 0.08% | 0.07% | 81% | 61%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.12% | -0.08% | 72% | 64%
Class C | 0.06% | 0.18% | 0.05% | 72% | 66%
Class E | 0.21% | -0.30% | -0.27% | 74% | 60%
Overall | 0.06% | 0.04% | -0.09% | 73% | 64%
Class D | 0.00% | -0.42% | -0.03% | 71% | 65%
Class F | -0.05% | -0.17% | -0.26% | 73% | 61%

## Slide 5: CE4-related: Geometric partition signaling JVET-Q0429
Test 2 results (vs CE4_common_base)
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.11% | 0.00% | 71% | 63%
Class A2 | -0.01% | 0.02% | -0.07% | 71% | 64%
Class B | -0.03% | -0.03% | 0.02% | 70% | 62%
Class C | -0.04% | 0.05% | 0.03% | 70% | 62%
Class E |  |  |  |  | 
Overall | -0.02% | -0.01% | 0.00% | 70% | 63%
Class D | -0.03% | -0.02% | 0.01% | 70% | 59%
Class F | -0.01% | 0.01% | 0.04% | 69% | 56%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.02% | 0.06% | 0.09% | 68% | 57%
Class C | -0.01% | -0.01% | -0.02% | 65% | 55%
Class E | 0.15% | 0.01% | -0.05% | 67% | 52%
Overall | 0.03% | 0.02% | 0.02% | 67% | 55%
Class D | 0.01% | -0.07% | 0.42% | 66% | 59%
Class F | -0.06% | -0.44% | 0.30% | 65% | 53%