## Slide 1: SAO Modification for 12-bit
JVET-Q0441
Advanced Technology Team
European Professional Engineering
Sony Europe BV.
Adrian Browne / Karl Sharman / Steve Keating
Sony Corp.

## Slide 2: Introduction
In the specification the SAO offset is defined as:
    SaoOffsetVal[ cIdx ][ rx ][ ry ][ i + 1 ] =
    ( 1 − 2 * sao_offset_sign[ cIdx ][ rx ][ ry ][ i ] ) * sao_offset_abs[ cIdx ][ rx ][ ry ][ i ]
  Where sao_offset_abs is clipped using:
    cMax = ( 1 << ( Min( BitDepth, 10 ) − 5 ) ) – 1
Offset is clipped at same relative value for both 8 and 10 bit processing
For 12-bit processing (e.g. HDR) relative offset is clipped to ¼ value
  SAO is selected less often
SAO is considered as a subjective-based tool
  Effect will be less for 12 bit processing than for 8/10 bit

## Slide 3: Proposal
Modify specification as follows:
    SaoOffsetVal[ cIdx ][ rx ][ ry ][ i + 1 ] =
    ( 1 − 2 * sao_offset_sign[ cIdx ][ rx ][ ry ][ i ] ) * (sao_offset_abs[ cIdx ][ rx ][ ry ][ i ] << (bitDepth – Min(10, bitDepth)))
Inserted left shift that increases effect of sao_offset_abs for 12 bit
  No effect for 8/10 bit
  SAO is used more often for 12-bit processing

## Slide 4: Comparison of SAO Usage
 | SAO usage count at given bit depth (K) |  |  |  | As a fraction of the 10 bit usage count | 
 | 8 | 10 | 12 | 12 with modification | 12 | 12 with modification
AI | 1512 | 1208 | 771 | 1068 | 64% | 88%
RA | 2289 | 1956 | 1149 | 1577 | 59% | 81%
LDB | 1167 | 926 | 520 | 780 | 56% | 84%
Number of uses of SAO for blocks within CTC tests (AI, RA, LDB)
at different bit depths

## Slide 5: Comparison of SAO Usage
With modification
Without modification

## Slide 6: Comparison of tool off tests
For AI, chroma losses experienced with 12 bit SAO are reversed by introducing the proposed modification.
 |  | All Intra | 
Variant | Y | U | V
10 bit overall | 0.00% | 0.15% | 0.17%
12 bit overall (without modification) | 0.01% | -0.02% | -0.07%
12 bit overall (with modification) | 0.00% | 0.12% | 0.11%

## Slide 7: Comparison of tool off tests
For RA, 12 bit results are much closer to 10 bit with the proposed modification.
 |  | Random Access | 
Variant | Y | U | V
10 bit overall | 0.08% | 0.20% | 0.33%
12 bit overall (without modification) | 0.03% | 0.10% | 0.08%
12 bit overall (with modification) | 0.07% | 0.18% | 0.23%

## Slide 8: Conclusion
Modification maintains effect of SAO for 12 bit processing
  Usage increased
  Regained relative coding losses
Likely to require profiles for 12 bit processing in future
No effect on existing 8 / 10 bit processing