## Slide 1: JVET-Q0457: MIP input value calculation unification
Shuai Wan, Haixin Wang, Junyan Huo,
Danni Wang,Yanzhuo Ma, Fuzheng Yang,
Yuanfang Yu, Yang Liu,
January. 2020

## Slide 2: MIP in VVC
If mipSizeId is equal to 2, the following applies:
p[ x ] = pTemp[ x + 1 ] − pTemp[ 0 ]
Otherwise (mipSizeId is less than 2), the following applies:
p[ 0 ] = pTemp[ 0 ] − ( 1 << ( BitDepth − 1 ) )
p[ x ] = pTemp[ x ] − pTemp[ 0 ] for x = 1..inSize – 1
mipSizeId = 2 :
mipSizeId = 0 or 1 :
pTemp[0]
Substruct
Substruct
Substruct
MID = 1<<(bitDepth-1)
Substruct
pTemp[i]
……
pTemp[inSize-1]
p[0]=MID-pTemp[0]
p[i]=pTemp[i]-pTemp[0]
……
p[inSize-1]= pTemp[inSize-1]-pTemp[0]
……
pTemp
[inSize]
Substruct
Substruct
pTemp
[
0
]
p
[
0
]=
pTemp
[
1
]
-
pTemp
[
0
]
Substruct
……
pTemp[1]
p[inSize-1]= pTemp[inSize]-pTemp[0]

## Slide 3: Proposed Modification
The input values p[ x ] with x = 0.. inSize − 1 are derived as follows:
p[ x ] = pTemp[ x + 1 ] − pTemp[ 0 ] for x = 0..inSize − 1
The boundary sample array pTemp[2*boundarySize] is filled by using the 1 << ( BitDepth−1 ).
p
[
0
]=
pTemp
[
1
]
-
pTemp
[
0
]
pTemp
[
1
]
……
pTemp
[
0
]
pTemp
[x]
p[inSize-1]=MID-pTemp[0]
Substruct
Substruct
Substruct
Substruct
MID = 1<<(bitDepth-1)
……
p[x]= pTemp[x]-pTemp[0]
Mathematically, sW, fO, and mWeight are also changed correspondingly to make the calculation of predMip[ x ][ y ] with the new p[i] identical to the one in VVC draft.

## Slide 4: Proposed Modification
Clean draft up and Reduce judgments:
The reduced top and left boundary samples redT and redL are assigned to the boundary sample array pTemp[ x ] with x = 0..2 * boundarySize − 1 as follows:
If isTransposed is equal to 1, pTemp[ x ] is set equal to redL[ x ] with x = 0..boundarySize − 1 and pTemp[ x + boundarySize ] is set equal to redT[ x ] with x = 0..boundarySize − 1.
Otherwise, pTemp[ x ] is set equal to redT[ x ] with x = 0..boundarySize − 1 and pTemp[ x + boundarySize ] is set equal to redL[ x ] with x = 0..boundarySize − 1.
The boundary sample array pTemp[2 * boundarySize ] is filled by 1 << ( BitDepth − 1 ).
The input values p[ x ] with x = 0.. inSize − 1 are derived as follows:
p[ x ] = pTemp[ x + 1 ] − pTemp[ 0 ] (255)
If mipSizeId is equal to 2, the following applies:
p[ x ] = pTemp[ x + 1 ] − pTemp[ 0 ] (255)
Otherwise (mipSizeId is less than 2), the following applies:
p[ 0 ] = pTemp[ 0 ] − ( 1 << ( BitDepth − 1 ) ) p[ x ] = pTemp[ x ] − pTemp[ 0 ] for x = 1..inSize − 1 (256)

## Slide 5: Conclusion
Propose to unify p[ x ].
  The prediction is identical with the prediction of VVC Draft
  The coding performance is identical with that of VTM
    AI: 0.00% 0.00% 0.00% 100% 100%
    RA: 0.00% 0.00% 0.00% 100% 100%
Editorial improvement
Reduce hardware complexity of make judgments
  Removes the dependency of p[ x ] on the mipSizeId and sample position
Recommend to adopt into VVC.
Thanks crosschecking by Alibaba.

## Slide 6
Thank you