## Slide 1: JVET-Q0461 – QP-independent and slice type-independent initialization of context models for the high throughput CABAC mode of JVET-P0300
A context model of the high throughput CABAC mode is initialized in dependence on the QP, the slice type and the cabac init flag
Proposal: Use one fixed (qp-independent) context initialization value per context model for the high throughput CABAC mode
Advantage: Context index derivation rules can directly derive the state instead of a context model index

## Slide 2: Recap: High throughput CABAC mode of JVET-P0300
Coding interval subdivision:
VTM-7.0
qRangeIdx = ivlCurrRange >> 5 pState = pStateIdx1 + 16 * pStateIdx0 valMps = pState >> 14 ivlLpsRange = ( qRangeIdx * ( (valMps ? 32767 − pState : pState )>>9 )>>1 ) + 4
High throughput mode of JVET-P0300
ivlLpsRange = ivlCurrRange >> ( pShiftGB + 1 )
pShiftGB is initialized in dependence on QP, slice type and cabac_init_flag!

## Slide 3: Recap: High throughput CABAC mode of JVET-P0300
Context model update (done after each regular bin)
VTM-7.0:
pStateIdx0 = pStateIdx0  (pStateIdx0 >> shift0) + (1023 * binVal >> shift0) pStateIdx1 = pStateIdx1  (pStateIdx1 >> shift1) + (16383 * binVal >> shift1)
Proposed high throughput mode:
No update.

## Slide 4: Proposed context initialization
JVET-P0300:
Two state variables: pShiftGB and valMpsGB
State variables depend on initValue, SliceQpY, cabac_init_flag, and slice_type
Proposed changes:
Use one fixed value for pShiftGB and valMpsGB per context model
Store values for pShiftGB and valMpsGB along with shiftIdx (window size parameter)
Initialization: pShiftGB = shiftIdx >> 5; valMpsGB = (shiftIdx >> 4 ) & 1
Additional required ROM: Increase shiftIdx from 4 bit to 7 bit per ctx (and rename to reflect the joint variable)

## Slide 5: Training of context init values
Training method: As specified in CE description JVET-N1021
Bitstreams: VTM-7.0 low QP (2 – 17) and lossless with 100 frames
Normalized rates d() according to JVET-N1021 are weighted such that low QP bitstreams are equally important as lossless bitstreams

## Slide 6: Implicit context reduction example
New init values (representing different probabilities) for sig_coeff_flag (Luma, QState=3):
init_sig_qstate3 = { 5, 7, 7, 7, 3, 7, 7, 7, 0, 7, 7, 7, }
VTM-7.0 context derivation for sig_coeff_flag (Luma, QState=3):
ctxInc = Min( ( locSumAbsPass1 + 1 ) >> 1, 3 ) + ( d < 2 ? 8 : ( d < 5 ? 4 : 0 ) )
Simplified rule (directly deriving a state):
ctxState = locSumAbsPass1 != 0 ? 7 : ( d < 2 ? 0 : ( d < 5 ? 3 : 5 ) )
Only the significance of locSumAbsPass1 needs to be derived!

## Slide 7: Coding efficiency: Low QP (2-17), 100 frames
Runtimes are not very accurate
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 QP2-17 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 5,77% | 4,08% | 4,51% | 101% | 84%
Class A2 | 4,87% | 4,64% | 4,74% | 92% | 80%
Class B | 5,65% | 5,58% | 6,04% | 96% | 84%
Class C | 4,41% | 3,93% | 4,05% | 95% | 83%
Class E | 3,82% | 3,79% | 4,21% | 92% | 80%
Overall | 4,96% | 4,51% | 4,82% | 95% | 82%
Class D | 4,35% | 3,74% | 3,95% | 90% | 86%
Class F | 6,10% | 5,31% | 5,43% | 96% | 90%
Class TGM | 8,65% | 8,69% | 8,79% | 95% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 QP2-17 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 6,78% | 4,74% | 3,22% | 102% | 86%
Class C | 4,79% | 5,01% | 3,61% | 92% | 88%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 4,28% | 4,15% | 3,20% | 93% | 89%
Class F | 7,00% | 5,71% | 4,97% | 95% | 92%
Class TGM | 9,38% | 9,29% | 9,47% | 94% | 99%

## Slide 8: Coding efficiency: Low QP (2-17), 100 frames
Runtimes are not very accurate
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 QP2-17 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 6,27% | 6,31% | 5,98% | 109% | 84%
Class C | 4,65% | 5,14% | 3,63% | 95% | 86%
Class E | 4,82% | 4,13% | 4,17% | 94% | 82%
Overall | 5,37% | 5,37% | 4,74% | 100% | 84%
Class D | 4,20% | 4,33% | 3,88% | 94% | 87%
Class F | 6,02% | 5,90% | 4,98% | 94% | 93%
Class TGM | 8,89% | 9,06% | 9,21% | 95% | 97%
 | Low delay P Main10 |  |  |  | 
 | Over VTM-7.0 QP2-17 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 6,43% | 6,40% | 6,01% | 103% | 83%
Class C | 5,16% | 4,79% | 3,49% | 94% | 81%
Class E | 5,27% | 3,99% | 4,10% | 94% | 78%
Overall | 5,72% | 5,26% | 4,69% | 98% | 81%
Class D | 4,47% | 4,30% | 3,91% | 98% | 87%
Class F | 6,19% | 5,64% | 4,74% | 93% | 90%
Class TGM | 8,66% | 8,85% | 9,01% | 96% | 99%

## Slide 9: Coding efficiency: Lossless, 100 frames
Runtimes are not very accurate
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM-7.0 | proposed |  | VTM-7.0 | proposed |  | VTM-7.0 | proposed | 
Class A1 | 2,2 | 2,1 | 8,12% | 2,2 | 2,1 | 7,81% |  |  | 
Class A2 | 1,6 | 1,5 | 8,89% | 1,7 | 1,6 | 9,13% |  |  | 
Class B | 2,2 | 2,0 | 7,38% | 2,3 | 2,2 | 6,65% | 2,3 | 2,2 | 6,78%
Class C | 1,9 | 1,8 | 6,98% | 2,4 | 2,3 | 6,49% | 2,4 | 2,3 | 6,39%
Class D | 1,9 | 1,8 | 6,84% | 2,8 | 2,5 | 7,66% | 2,7 | 2,5 | 7,53%
Class E | 2,8 | 2,6 | 8,06% |  |  |  | 3,1 | 2,9 | 7,31%
Class F | 5,3 | 4,9 | 6,91% | 33,7 | 30,1 | 10,23% | 50,7 | 43,0 | 11,89%
TGM | 11,8 | 10,8 | 9,52% | 107,1 | 96,3 | 10,39% | 124,9 | 110,5 | 11,56%
Overall | 2,1 | 2,0 | 7,78% | 2,2 | 2,1 | 7,34% | 2,6 | 2,4 | 6,78%
Enc Time[%] | 93% |  |  | 98% |  |  | 98% |  | 
Dec Time[%] | 91% |  |  | 89% |  |  | 91% |  |