## Slide 1: Coded Picture Buffer and MinCr in VVC
JVET-R0244
Advanced Technology Team
European Professional Engineering
Sony Europe
Steve Keating
Sony Corp.

## Slide 2: Introduction
In Annex A, Table A1 specifies the maximum coded picture buffer (CPB) size for each level.
Table A2 and A3 specify the minimum compression ratio (MinCr).
  MinCr is used to guarantee that a picture is compressed by at least the specified amount.
However, MinCr is not always the limiting factor:
For example, an 8K picture coded at MinCr cannot be stored in the CPB (using Main 10 profile, level 6, main tier).
For Main 4:4:4 10 profile, this is the case for several levels.

## Slide 3: Problem: Main 10 profile
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size | Max CPB size MaxCPB (CpbVclFactor or CpbNalFactor bits) | Max CPB size MaxCPB Main10 (bits) | Min compression ratio MinCrBase | Max coded picture size Main10 (bits @ 15bits/sample) | Min coded pictures in CPB Main10
 |  |  | Main tier | Main tier | Main tier | Main tier | Main tier
1 | 36,864 |  | 350 | 350,000 | 2 | 276,480 | 1.3
2 | 122,880 |  | 1,500 | 1,500,000 | 2 | 921,600 | 1.6
2.1 | 245,760 |  | 3,000 | 3,000,000 | 2 | 1,843,200 | 1.6
3 | 552,960 |  | 6,000 | 6,000,000 | 2 | 4,147,200 | 1.4
3.1 | 983,040 |  | 10,000 | 10,000,000 | 2 | 7,372,800 | 1.4
4 | 2,228,224 | 2048x1088 | 12,000 | 12,000,000 | 4 | 8,355,840 | 1.4
4.1 | 2,228,224 | 2048x1088 | 20,000 | 20,000,000 | 4 | 8,355,840 | 2.4
5 | 8,912,896 | 4096x2176 | 25,000 | 25,000,000 | 6 | 22,282,240 | 1.1
5.1 | 8,912,896 | 4096x2176 | 40,000 | 40,000,000 | 8 | 16,711,680 | 2.4
5.2 | 8,912,896 | 4096x2176 | 60,000 | 60,000,000 | 8 | 16,711,680 | 3.6
6 | 35,651,584 | 8192x4352 | 60,000 | 60,000,000 | 8 | 66,846,720 | 0.9
6.1 | 35,651,584 | 8192x4352 | 120,000 | 120,000,000 | 8 | 66,846,720 | 1.8
6.2 | 35,651,584 | 8192x4352 | 240,000 | 240,000,000 | 6 | 89,128,960 | 2.7
Note that the fields highlighted in green are from Table A.1 or Table A.2 in the spec., other fields are derived from these, CpbVclFactor and MinCrScaleFactor (Table A.3).
Profile | CpbVclFactor | CpbNalFactor | FormatCapabilityFactor | MinCrScaleFactor
Main 10 | 1 000 | 1 100 | 1.875 | 1.0
Main 4:4:4 10 | 2 500 | 2 750 | 3.750 | 0.5
Table A.3

## Slide 4: Problem: Main 4:4:4 10 profile
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size | Max CPB size MaxCPB (CpbVclFactor or CpbNalFactor bits) | Max CPB size MaxCPB Main444_10 (bits) | Min compression ratio MinCrBase | Max coded picture size Main444_10 (bits @30bits/sample) | Min coded pictures in CPB Main444_10
 |  |  | Main tier | Main tier | Main tier | Main tier | Main tier
1 | 36,864 |  | 350 | 875,000 | 2 | 1,105,920 | 0.8
2 | 122,880 |  | 1,500 | 3,750,000 | 2 | 3,686,400 | 1.0
2.1 | 245,760 |  | 3,000 | 7,500,000 | 2 | 7,372,800 | 1.0
3 | 552,960 |  | 6,000 | 15,000,000 | 2 | 16,588,800 | 0.9
3.1 | 983,040 |  | 10,000 | 25,000,000 | 2 | 29,491,200 | 0.8
4 | 2,228,224 | 2048x1088 | 12,000 | 30,000,000 | 4 | 33,423,360 | 0.9
4.1 | 2,228,224 | 2048x1088 | 20,000 | 50,000,000 | 4 | 33,423,360 | 1.5
5 | 8,912,896 | 4096x2176 | 25,000 | 62,500,000 | 6 | 89,128,960 | 0.7
5.1 | 8,912,896 | 4096x2176 | 40,000 | 100,000,000 | 8 | 66,846,720 | 1.5
5.2 | 8,912,896 | 4096x2176 | 60,000 | 150,000,000 | 8 | 66,846,720 | 2.2
6 | 35,651,584 | 8192x4352 | 60,000 | 150,000,000 | 8 | 267,386,880 | 0.6
6.1 | 35,651,584 | 8192x4352 | 120,000 | 300,000,000 | 8 | 267,386,880 | 1.1
6.2 | 35,651,584 | 8192x4352 | 240,000 | 600,000,000 | 6 | 356,515,840 | 1.7
Note that the fields highlighted in green are from Table A.1 or Table A.2 in the spec., other fields are derived from these, CpbVclFactor and MinCrScaleFactor (Table A.3).
Table A.3
Profile | CpbVclFactor | CpbNalFactor | FormatCapabilityFactor | MinCrScaleFactor
Main 10 | 1 000 | 1 100 | 1.875 | 1.0
Main 4:4:4 10 | 2 500 | 2 750 | 3.750 | 0.5

## Slide 5: Historic differences
Table A.3
Profile | CpbVclFactor | CpbNalFactor | FormatCapabilityFactor | MinCrScaleFactor
Main 10 | 1 000 | 1 100 | 1.875 | 1.0
Main 4:4:4 10 | 2 500 | 2 750 | 3.750 | 0.5
In HEVC Version 1,
  Main was developed first, and Table A.3 was duplicated for Main 10.
In HEVC Version 2,
  Entries for the new profiles were equivalent to the Main (4:2:0 8bit) profile, scaled using FormatCapabilityFactor.
Hence in VTM, the relationship between Main 10 and Main 4:4:4 10 is not connected.

## Slide 6
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size | Max CPB size MaxCPB (CpbVclFactor or CpbNalFactor bits) | Max CPB size MaxCPB Main10 (bits) | Min compression ratio MinCrBase | Max coded picture size Main10 (bits @ 15bits/sample) | Min coded pictures in CPB Main10
 |  |  | Main tier | Main tier | Main tier | Main tier | Main tier
1 | 36,864 |  | 350 | 350,000 | 2 | 276,480 | 1.3
2 | 122,880 |  | 1,500 | 1,500,000 | 2 | 921,600 | 1.6
2.1 | 245,760 |  | 3,000 | 3,000,000 | 2 | 1,843,200 | 1.6
3 | 552,960 |  | 6,000 | 6,000,000 | 2 | 4,147,200 | 1.4
3.1 | 983,040 |  | 10,000 | 10,000,000 | 2 | 7,372,800 | 1.4
4 | 2,228,224 | 2048x1088 | 12,000 | 12,000,000 | 4 | 8,355,840 | 1.4
4.1 | 2,228,224 | 2048x1088 | 20,000 | 20,000,000 | 4 | 8,355,840 | 2.4
5 | 8,912,896 | 4096x2176 | 25,000 | 25,000,000 | 6 | 22,282,240 | 1.1
5.1 | 8,912,896 | 4096x2176 | 40,000 | 40,000,000 | 8 | 16,711,680 | 2.4
5.2 | 8,912,896 | 4096x2176 | 60,000 | 60,000,000 | 8 | 16,711,680 | 3.6
6 | 35,651,584 | 8192x4352 | 60,000 80,000 | 60,000,000 | 8 | 66,846,720 | 1.2
6.1 | 35,651,584 | 8192x4352 | 120,000 | 120,000,000 | 8 | 66,846,720 | 1.8
6.2 | 35,651,584 | 8192x4352 | 240,000 | 240,000,000 | 6 | 89,128,960 | 2.7
Proposed Changes: Main 10 profile

## Slide 7: Proposed Changes: Main 4:4:4 10 profile (Method 1)
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size | Max CPB size MaxCPB (CpbVclFactor or CpbNalFactor bits) | Max CPB size MaxCPB Main444_10 (bits) | Min compression ratio MinCrBase | Max coded picture size Main444_10 (bits @30bits/sample) | Min coded pictures in CPB Main444_10
 |  |  | Main tier | Main tier | Main tier | Main tier | Main tier
1 | 36,864 |  | 350 | 875,000 | 2 | 737,280 | 1.2
2 | 122,880 |  | 1,500 | 3,750,000 | 2 | 2,457,600 | 1.5
2.1 | 245,760 |  | 3,000 | 7,500,000 | 2 | 4,915,200 | 1.5
3 | 552,960 |  | 6,000 | 15,000,000 | 2 | 11,059,200 | 1.4
3.1 | 983,040 |  | 10,000 | 25,000,000 | 2 | 19,660,800 | 1.3
4 | 2,228,224 | 2048x1088 | 12,000 | 30,000,000 | 4 | 22,282,240 | 1.3
4.1 | 2,228,224 | 2048x1088 | 20,000 | 50,000,000 | 4 | 22,282,240 | 2.2
5 | 8,912,896 | 4096x2176 | 25,000 | 62,500,000 | 6 | 59,419,307 | 1.1
5.1 | 8,912,896 | 4096x2176 | 40,000 | 100,000,000 | 8 | 44,564,480 | 2.2
5.2 | 8,912,896 | 4096x2176 | 60,000 | 150,000,000 | 8 | 44,564,480 | 3.4
6 | 35,651,584 | 8192x4352 | 60,000 80,000 | 200,000,000 | 8 | 178,257,920 | 1.1
6.1 | 35,651,584 | 8192x4352 | 120,000 | 300,000,000 | 8 | 178,257,920 | 1.7
6.2 | 35,651,584 | 8192x4352 | 240,000 | 600,000,000 | 6 | 237,677,227 | 2.5
Profile | CpbVclFactor | CpbNalFactor | FormatCapabilityFactor | MinCrScaleFactor
Main 10 | 1 000 | 1 100 | 1.875 | 1.0
Main 4:4:4 10 | 2 500 | 2 750 | 3.750 | 0.5 0.75
Table A.3

## Slide 8: Proposed Changes: Main 4:4:4 10 profile (Method 2)
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size | Max CPB size MaxCPB (CpbVclFactor or CpbNalFactor bits) | Max CPB size MaxCPB Main444_10 (bits) | Min compression ratio MinCrBase | Max coded picture size Main444_10 (bits @30bits/sample) | Min coded pictures in CPB Main444_10
 |  |  | Main tier | Main tier | Main tier | Main tier | Main tier
1 | 36,864 |  | 350 | 700,000 | 2 | 552,960 | 1.3
2 | 122,880 |  | 1,500 | 3,000,000 | 2 | 1,843,200 | 1.6
2.1 | 245,760 |  | 3,000 | 6,000,000 | 2 | 3,686,400 | 1.6
3 | 552,960 |  | 6,000 | 12,000,000 | 2 | 8,294,400 | 1.4
3.1 | 983,040 |  | 10,000 | 20,000,000 | 2 | 14,745,600 | 1.4
4 | 2,228,224 | 2048x1088 | 12,000 | 24,000,000 | 4 | 16,711,680 | 1.4
4.1 | 2,228,224 | 2048x1088 | 20,000 | 40,000,000 | 4 | 16,711,680 | 2.4
5 | 8,912,896 | 4096x2176 | 25,000 | 50,000,000 | 6 | 44,564,480 | 1.1
5.1 | 8,912,896 | 4096x2176 | 40,000 | 80,000,000 | 8 | 33,423,360 | 2.4
5.2 | 8,912,896 | 4096x2176 | 60,000 | 120,000,000 | 8 | 33,423,360 | 3.6
6 | 35,651,584 | 8192x4352 | 60,000 80,000 | 160,000,000 | 8 | 133,693,440 | 1.2
6.1 | 35,651,584 | 8192x4352 | 120,000 | 240,000,000 | 8 | 133,693,440 | 1.8
6.2 | 35,651,584 | 8192x4352 | 240,000 | 480,000,000 | 6 | 178,257,920 | 2.7
Profile | CpbVclFactor | CpbNalFactor | FormatCapabilityFactor | MinCrScaleFactor
Main 10 | 1 000 | 1 100 | 1.875 | 1.0
Main 4:4:4 10 | 2 500 2 000 | 2 750 2 200 | 3.750 | 0.5 1.0
Table A.3

## Slide 9: Conclusion
Either remove MinCr or adjust values in Annex A so that MinCr is still useful
If MinCr is still to be useful then:
  increase Max CPB Size for level 6 from 60,000 to 80,000
  and:
    Either
    increase MinCrScalingFactor to 0.75 for Main 4:4:4 10 profile
    Or
    increase MinCrScalingFactor to 1.0 for Main 4:4:4 10 profile
    set CpbVclFactor, CpbNalFactor for Main 4:4:4 10 profile to be 2x those of Main 10 profile (JVET-R0243 compares 4:4:4 and 4:2:0 bit-rates)