## Slide 1: On chroma QP mapping
JVET-S0130
Ling Li, X. Li, S. Liu

## Slide 2: Chroma QP mapping
For 420 in HEVC
For non-420 in HEVC (identical QP)
In VVC
Mapping table can be configured using a flexible piecewise linear model regardless of chroma format
For 420 CTC in VTM
For non-420 in VTM (identical QP)
qPi | < 30 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | > 43
QpC | = qPi | 29 | 30 | 31 | 32 | 33 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | = qPi − 6
qPi | … | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | > 51
QpC | … | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 51
Luma | … | 17 | … | 27 | … | 32 | … | 44 | …
chroma | … | 17 | … | 29 | … | 34 | … | 41 | …
Luma | … | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | … | 63
chroma | … | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | … | 63

## Slide 3: Chroma QP mapping derivation
sps_qp_table_start_minus26[ i ] : has range of [−26 − QpBdOffset, 36]
sps_num_points_in_qp_table_minus1[ i ] : has range of [0, 63 + QpBdOffset]
qpInVal[ i ][ 0 ] = sps_qp_table_start_minus26[ i ] + 26 qpOutVal[ i ][ 0 ] = qpInVal[ i ][ 0 ] for( j = 0; j <= sps_num_points_in_qp_table_minus1[ i ]; j++ ) { qpInVal[ i ][ j + 1 ] = qpInVal[ i ][ j ] + sps_delta_qp_in_val_minus1[ i ][ j ] + 1 qpOutVal[ i ][ j + 1 ] = qpOutVal[ i ][ j ] + ( sps_delta_qp_in_val_minus1[ i ][ j ] ^ sps_delta_qp_diff_val[ i ][ j ] ) }
It is a requirement of bitstream conformance that the values of qpInVal[ i ][ j ] and qpOutVal[ i ][ j ] shall be in the range of −QpBdOffset to 63, inclusive for i in the range of 0 to numQpTables − 1, inclusive, and j in the range of 0 to sps_num_points_in_qp_table_minus1[ i ] + 1, inclusive
Note that, when sps_qp_table_start_minus26[ i ] has value 37, then qpInVal[i][0] is 63 which is the upper bound of luma QP. However, highlighted equation generates
qpInVal[i][1] = 64 + sps_delta_qp_in_val_minus1[ i ][ 0 ]. This violates the bitstream conformance.
Similarly, when QpBdOffset is 0 and sps_num_points_in_qp_table_minus1[ i ] is 63, which means there are 64 entries in luma QP. However, highlighted equation generates
qpInVal[i][64]=qpInVal[i][63] + sps_delta_qp_in_val_minus1[ i ][ j ] + 1. This violates the bitstream conformance.
Luma | -QpBdOffset | … | 63
chroma |  |  | 

## Slide 4: Proposed Method
Aspect 1: Bugfix for the range of sps_num_points_in_qp_table_minus1[ i ]
Propose change the range from [0, 63 + QpBdOffset] to [0, 62 + QpBdOffset]
Aspect 2: introduce sps_chroma_qp_identical_to_luma_flag in SPS
It is asserted that this shortcut is the common case for 4:2:2 and 4:4:4, and substantive bits can be saved by skipping all the chroma QP mapping related syntax elements in SPS.

## Slide 5: Analysis for aspect 2
Only need 1 bit sps_chroma_qp_identical_to_luma_flag to generate identical QP mapping table

## Slide 6: Simulation results for aspect 2
It is implemented on VTM 9.0rc1 and tested using non 420 test condition. Only 1 frame is tested under AI configuration with worst cast QP configured*.
* The worst case QP configuration is sending all the QP entries in the chroma QP mapping table.

## Slide 7: Thank You